## Slide 1: Issues of MC gateway UE
Cuili Ge
Huawei, Hisilicon

## Slide 2: Content
What’s the R18 MCGWUE
Overall issues
Detailed issues
  Issue #1: Architecture and functional model issues
  Issue #2: Scenario and connection authorization issues
  Issue #3: Media plane access enforcement per connection authorization issues
  Issue #4: GW MC service ID issues
  Issue #5: Configuration for the MC client host by N3GPP device
  Issue #6: Signalling between the MC client and the MC gateway UE
Key proposals summary and whole service flow

## Slide 3: R18 MCGWUE features
Functional model of MC gateway UE signalling plane
Function Model of MC gateway UE media plane
1. Two cases: N3GPP device with/without clients
2. Signalling and media plane functional models (the PoV of N3GPP device)
3. Newly procedures and information flow
The other aspects like IMS subscriptions, IP address allocation are not specially listed in this page.
3.1 Connection authorization and disconnection (not shown)
3.2 Location management for GWUE case
- the MC service client on N3GPP device requests the gateway UE to handle the 3GPP related location signallings.
3.3 MBMS support for GWUE case
- the MC service client on N3GPP device requests the gateway UE to handle the MBMS signaling
4. A new GW MC service ID is introduced and used in the information flows in 11.5.2 and 11.5.3
8.1.7 GW MC service ID
The GW MC service ID is used for connection authorisation of non-3GPP devices via an MC gateway UE with an MC system. The GW MC service ID indicates the MC service.
The MC service ID used for MC service authorisation and the GW MC service ID used for connection authorization may have different values. Both identities are configured by the Mission Critical Organisation.

## Slide 4: Why connection authorization is needed ?
Currently why such connection authorization is needed, i.e., what is going to be achieved by performing such connection authorization ? In 11.5.1.2.1, it describes “The MC server performs authorization for the use of the MC gateway UE by the MC gateway client, i.e. the binding between the MC gateway UE and the MC gateway client is authorized and controlled by the MC server. ”.
Q1: Why such connection authorization is needed?
  Restrict the usage of MC gateway UE. Per service, per user, per data flow (i.e., authentication message, service authorization message, group call message) ?
  However, there is no description about whether and how the MC gateway UE will identify the traffic from the N3GPP device is from an connection authorized user or non-authorized user. In addition, there is not description about whether and how the MC gateway UE will identify the traffic is specific to a certain service or user or data flow.
Q2: What happened without such connection authorization ?
  Any user and use the MC gateway UE to exchange any traffic
  Other issues ?
Q3: Authorize “what”?
  Case A: a certain MC service user can only use a specific MC gateway UE(s), i.e., the association b/w the MC service user and the MC gateway UE. There is a association between the MC service user and a MC gateway UE and only the allowed MC service user can use the specific MC gateway UE. The server will check such association.
  Case B: any MC service user who may login the MC client within the N3GPP device, i.e., the connection b/w the N3GPP device and the MC gateway UE. The server dose not care about “who” will login the MC client and use this MC gateway UE. This connection authorization is only performed once, rather than for each new MC service user connected to the MC gateway UE.
The answers to the above questions impact the functional model, the connection authorization and the meaning and usage of “GW MC service ID”.

## Slide 5: Issue#1 - Architecture and functional model issues
In current MC gateway UE clause, the MC gateway client needs to finish the connection authorization firstly, then start to initiate the identity authentication towards the IDM, service authorization towards the MC service server, and then the affiliation, group call…….
Issue: In the Figure 11.2.1-1, the MCX-n, CSC-n, SIP-1, HTTP-1 between the N3GPP UE and the servers are divided by the MC gateway UE. However, the MC gateway UE will not process the MCX-n, CSC-n, SIP-1,HTTP-1 messages from the N3GPP device except transparently routing them as “media”. In other words, the target of those MCX-n, CSC-n, SIP-1 , HTTP-1 message is the server, not the MC gateway UE
Proposal:
  Reconstruct the functional model for application plan and sinalling plane, i.e., keep the application layer reference point (GW-local and GW-core) in figure 11.2.1-1, and move the signaling plane (SIP-1 and HTTP-1) to a new functional model.
  Update clause 11.2.3 to capture that the MC gateway UE also routes all the MCX-n, CSC-n traffic between the CSC server and MC service server.
Figure 11.2.1-1: Functional model of MC gateway UE signalling plane

## Slide 6: Issue#2 Scenario and connection authorization issues
N3GPP device
GW UE
MC servers
N3GPP device host Client
GW UE
MC servers
N3GPP not host Client
IDM authentication, service authorization,group call
MC client hosted by the MC gateway UE
IDM authentication, service authorization, group call
Currently, any traffic not belong to the MC gateway UE should be after a connection authorization.
Issues:
  Is it allowed that any traffic can be directly initiated without the connection authorization ? It looks multiple MC Client (e.g., MCPTT client) ‘instance’ for each user works simultaneously.
Relate to Q1~Q3
  Proposal: authorize the association b/w the MC service user and the gateway UE.
  Proposal: A unique identifier of the user should be provided in the connection request, i.e., the MC ID
  Proposal: The MC gateway UE should provide its own identity along with the MC service user identity (MC ID) to the MC gateway UE function for the server to authorize the “association”
IDM authentication, service authorization, group call……
MC client hosted by the MC gateway UE
MC server
MC gateway UE
MCPTT client#1
MCPTT client#2
……
MCPTT client#N
Option#1：authorize the assoiciation b/w the MC service user and the gateway UE. So the connection authorization is required for both scenarios.
Why connection authorization is needed ? For what ?
Option #2: authorize the connection b/w the N3GPP device and the MC gateway UE. If so, such scenarios does not requires the connection authorization.
Case A, B in P4
Case C in P4

## Slide 7: Issue#3 - Media plane access enforcement per connection authorization issue
After the connection authorization is completed, the N3GPP device can use the gateway UE to send/receive the packet.
Issues:
  It is per service connection authorization, i.e., if the connection is authorized for MCPTT, then only MCPTT traffic can go through the gateway UE, not MCVideo and MCData.
  Only the service information indicated by the GW MC service ID is not sufficient, How the MC gateway UE can identity and route such “MCPTT traffic” , and block the other “MCVideo and MCData traffic” ?
Relate to Q1,Q2
  Proposal: The MC gateway UE function will configured the allowed data filter (e.g., N3GPP device IP, MC service server IP, port, protocol) to the MC gateway UE to enforce the authorization result by controlling the data routing at the MC gateway UE.
N3GPP low layer
IP
TCP/UDP
HTTP
3GPP low layer
IP
L2/L1
IP
TCP/UDP
HTTP
TCP/UDP
HTTP
Control plane stack
N3GPP low layer
IP
TCP/UDP
SIP/RTP,RTCP/HTTP
3GPP low layer
IP
L2/L1
IP
TCP/UDP
SIP/RTP,RTCP/HTTP
User plane stack
GW-Local
GW-core
N3GPP device
GW UE
MC servers
N3GPP device
GW UE
MC servers

## Slide 8: Issue #4: GW MC service ID issues
GW UE#1
GW MC service ID#1
GW MC service ID#2
….
Temporary user identity
Dynamically allocate and recycle
One GW MC service ID is allocated to a MC service user at one time. Multiple users can not have the same GW MC service ID at the same time.
The MC server check whether the MC service user has another connection from another MC gateway UE.
MC server
GW UE#1- GW MC service ID list
GW UE#2 – GW MC service ID list
Currently understandings of GW MC service ID
Some issues
  identify any user, or a certain user ?
  How the gateway UE can identify the “user” if the user initiates multiple request towards the same GW UE. How the server can identify the “user” it initiates two connection authorization from two gateway UEs and each with a different GW MC service ID?
  When it is allocated/configured to the MC gateway client ?
  Will the GW MC service ID will be run out at a MC gateway UE ?
GW UE#1
For Case A in P4, an “identifier” uniquely identify a user in the system (among multiple gateway Ues) is required.
Currently, the GW MC service ID fails to meet this case.
For Case B in P4, it is not a per user association authorization, it is the N3GPP device and gateway UE connection for any users.
Currently, the GW MC service ID fails to meet this case.
Related to Q1~Q3
  Proposal: The GW MC service ID is allocated to the MC service user at the N3GPP device by the MC gateway UE upon receiving the successful connection authorization. This GW MC service ID uniquely identify a MC service user within the MC gateway UE. This GW MC service ID is only used in the GW-local reference point.
  Then the following signallings (e.g., the location management message in clause 11.5.2, the MBMS related message in clause 11.5.3) over the GW-Local will use this IE to identify the MC service user within the MC gateway UE.

## Slide 9: Issue #5: Configuration for the MC client host by N3GPP device
(1)Required configurations at the MC clients on N3GPP device.
  -MC service UE configuration data (see subclause A.2);
  -MC service user profile data (see subclause A.3);
  -MC service group configuration data (see subclause A.4);
  -MC service configuration data (see subclause A.5); and
  -Initial MC service UE configuration data (see subclause A.6).
Currently such configuration is described as, e.g., “The configuration management server is used to configure the MC service user profile configuration data to the MC service user database (CSC-13) and MC service UE (CSC-4).”, “……to the MC service UE (CSC-2)”
  Proposal: e.g., configuration management client (CSC-4) on the MC service UE or the N3GPP device
Initial MC service UE configuration data is the special one, When to configure it to the N3GPP device ?
  Same as the MC service UE: This way will create more work to manage the N3GPP device to the MCX organization
  Proposal: The MC gateway UE delivers the initial MC service UE configuration data to the N3GPP device. So after the connection authorization, the MC client can use such information to contact the MC server.

## Slide 10: Key proposals summary and whole service flow
Q1： Why such connection authorization is needed?
  Restrict the usage of MC gateway UE from MC service user
Q2：What happened without such connection authorization ?
  Any user and use the MC gateway UE to exchange any traffic
Q3: Authorize “what”?
  the association b/w the MC service user and the MC gateway UE, i.e., the association of MC ID and MC gateway identity.
GW MC service ID:
  GW MC service ID is allocated by the gateway UE upon a successful connection authorization from the MC server. It used over the GW-local reference point, and uniquely identify a MC service user within a MC gateway UE.
When to configure the Initial MC service UE configuration data ?
  The MC gateway UE delivers the initial MC service UE configuration data to the N3GPP device. So after the connection authorization, the MC client can use such information to contact the MC server.
Whole service flow of using a gateway UE to connect the MC servers
MC gateway client
MC client
N3GPP device
Media forwarding function
MC gateway UE server
MC gateway UE
Identity management function
MC gateway UE Function
MC server
MC service server
1. Conn authorization req (MC ID )
2. Conn authorization req (MC ID， GW UE ID, N3GPP device IP )
3. Conn authorization check
4. Conn authorization resp (MC ID， authorized flow filter)
5. Save the filter, allocate a GW MC service ID to the user with MC ID
6. Conn authorization req (MC ID, GW MC service ID )
7. IP packet (Identity management message)
7. IP packet (Identity management message)
Based flow filter, route the IP packet
8. IP packet (service authorization message)
8. IP packet (service authorization message)
9. IP packet (Group call request, response)
9. IP packet (Group call request, response)
10. IP packet (location management message)
10. IP packet (location management message)
11. Location management message (GW CMC service ID )
11. Location message interactions
Internal delivery
IP packet (MBMS messages )
IP packet (MBMS messages)
MBMS message (GW MC service ID )
Internal delivery

## Slide 11: Issue #6: Signalling between the MC client and the MC gateway UE
In clause 11.5.2 and 11.5.3, it is the ‘MC client’ exchanges the signallings with MC gateway UE over the GW-local, it is not aligned with the functional model that there is no new reference point between the MC client on the N3GPP device and the MC client in the MC gateway UE.
MC client receive the messages from the e.g., Location management server, and pass it to the MC gateway client (which is the internal implementation outside the scope of SA6). It is the MC gateway client, interacting with the MC gateway UE over the GW-local for the signallings.
  Proposal: Modify the clause 11.5.2 and 11.5.3 accordingly to reflect the signalling is between the MC gateway client and the MC gateway UE server at the MC gateway UE.