## Slide 1: EDGEApp-related metaverse functionality discussion
Catalina Mladin
Delegate, Convida Wireless

## Slide 2: Outline
General metaverse-EDGE functional links
Application Coordination Use Cases
Multi-user Session Use Cases
Proposal

## Slide 3: General Metaverse-EDGEApp links
Current SID proposal is for “enablement of Localized Mobile Metaverse Services”
  Localization of services is highly relevant to both
  Current metaverse services can be provided over the top. Localization is where and how 3GPP can offer value-add.
Some metaverse requirements can be met by expanding EDGEApp mechanisms. Our alternatives (in SID):
  NOT acknowledge the link, re-start with KI/solutions from zero; or
  Acknowledge the link, mandate SID to stay within current EDGE framework (nobody is proposing that)
  Acknowledge the link, direct KI/solutions to study the link and to reuse existing work whenever possible

## Slide 4: Metaverse app “association/coordination”
Metaverse applications tend to be associated and coordinated when they are providing services to the same UE/AC
“Association/coordination” is easiest to be done in the cloud.
When offload/EDGE is needed to improve performance on one or more metaverse applications, joint functionality may not be seamless without supporting functionality.
Related SA1 usecases in TR 22.856
5.3 Collaborative and concurrent engineering in product design using metaverse services
5.9 Synchronized predictive avatars
5.25 Enabling Metaverse services to users via multiple access connections
5.27 Localized Mobile Metaverse Overload
5.14 Use Case on interconnection of mobile metaverse services

## Slide 5: EDGEapp bundling and Common EAS
EDGEApp Common EAS, EAS bundle features also address “association/coordination”.
Rel-18 EDGEApp work already brought the question whether “common EAS bundle” should be treated
On the other hand, Rel-18 EAS bundling relies on pre-provisioning of the composition of the bundle. This does not account for cases in which a metaverse service gets moved from Cloud to the Edge on-the-go.
  Q1: Does it help or hurt the specs(new TR?) to think of metaverse “association/ coordination” relative to bundling and common EAS, i.e. in EDGE context from the beginning?
  Q2: If thinking metaverse isolated from EDGE, should each type of app interdependence to introduce new IDs, requirements, etc, or can we establish a framework for app interdependence that would work in more usecases?

## Slide 6: App association/coordination example
Two distinct ACs cooperating within metaverse.
Video Storage and Editing Application is relocated.
Video Analysis App traffic can be optimized if the applications are “associated/coordinated”.
Upload to edge
Video Editing Application
Video Analysis Application
(cloud)
?
Video Editing Application
(EAS)
Video data
Move to edge to reduce traffic
Not aware of the change of the other application’s location, the analysis application stays in cloud, so video data still has to be sent to the cloud
Backbone traffic could not be reduced due to sending data to analytic application located in the cloud
AC-1 (editing)
AC-2 (analysis)

## Slide 7: Multi-user sessions
Many metaverse application result in multi-user sessions between clients.
These were studied by SA6 for Edge cases with or without UEs located in the same EDN (Common EAS feature)
Client interactions through different EAS instances is an important usecase for metaverse, e.g. before/after using a common EAS. For these cases synchronization is required. This is not about OTT application context sync, rather service-layer related information: network slices, QoS configurations, as well as new metaverse-specific data, i.e. avatars, digital representations.
  Q3: Should metaverse-related synchronization reuse EDGE framework for (E)AS synchronization? Are there other suitable SA6 data management frameworks available?

## Slide 8: Summary
We addressed 3 questions on fundamental and broadly reaching issues in the treatment of Metaverse in SA6.
The commonality between the issues is the pre-existence of EDGEapp concepts and mechanisms which should form the baseline for requirements and solutions.
The kind request is for SA6 to decide whether to purposefully point towards reuse of EDGE functionality for Metaverse
  If yes: bullet on relationship to EDGEApp, enhancements and /or generalization of EDGE functionality should be added in SID
  If no: bullet on staying away from overloading EDGE functionality should be added in SID
Proposal: Acknowledge the metaverse-edge link in the SID, direct KI/solutions to study the link and to reuse existing work