## Slide 1: DP on EAS information provisioning issues
Catalina Mladin
Delegate, Convida Wireless LLC.

## Slide 2: TS 23.558 excerpt from clause 8.15.2.2
When the selection is that of a common EAS for application group, the request message may contain the list of EESs for a certain Application Group ID, received from the ECS in the service provisioning response message. This application group related information may be used for further common EAS announcement(s) between EES(s). In the case of no ECS-ER, if the request message does not contain the list of EESs for a certain Application Group ID, then the EES determines the other EESs to which announce common EAS request needs to be sent as described in clause 8.8.3.3. If there is ECS-ER, the EEC selected EAS is used in interaction between the EES and ECS-ER, and EEC receives common EAS in the EAS information provisioning response. If the common EAS is registered to another EES, then the EES endpoint of the EES where the common EAS is registered is also included in the EAS information provisioning response.

## Slide 3: EES to ECS-ER interactions
Query (i.e. Obtain EAS info, clause 8.20.2.2)
  In: EAS ID, App. Group ID
  Out: List of EAS endpoints (if successful)
Store (i.e. Common EAS info storage, clause 8.20.2.3)
  In: EAS ID, EAS Endpoint, App Group ID, EDN info
  Out: List of EAS endpoints (if FAILURE)

## Slide 4: Questions
If EEC sends EAS provisioning request of type “EAS selection” why does it need to receive common EAS in the EAS information provisioning response ?
“If the common EAS is registered to another EES,” sentence implies we are talking of “Common EAS” as provided by EEC in the EAS information provisioning request, i.e. via EAS ID and/ or EAS endpoint. In this case, EEC could have obtained this info either from:
Service provisioning response (clause 8.3.3.3.3). But Service provisioning response does not provide EAS endpoints, only EAS IDs.
EAS discovery response (clause 8.5.3.3) . However, in this case the EAS needs to belong to EES.
If Common EAS info provided in the EAS information provisioning request = EAS ID only:
  If current EES has EAS with EAS ID, it should assume that its EAS = Common EAS
  If current EES does not have EAS with EAS ID, how can it determine another EES serving an EAS with that EAS ID? Assumingly by interacting with ECS-ER. But the EES to ECS-ER interactions in clause 8.20 do not provide this functionality.

## Slide 5
Information element | Status | Description
EECID | M | The identifier of the EEC.
ACID | M | The identifier of the AC.
Security credentials | M | Security credentials resulting from a successful authorization for the edge computing service.
Selected EAS ID(s) | EAS ID, 1 or more | Shouldn’t this be mandatory for request type “EAS selection”?
Application Group ID (NOTE 4) | Group ID | This IE may be present only if the request type is "EAS selection".
List of EES(s) (NOTE 4) | O | This IE may be present only if the request type is "EAS selection".
Selected EAS Endpoint(s) | May be present | This IE is allowed for “EAS selection “ request type. If it is NOT present, and based on current text, Common EAS info may be provided in the response. This turns this procedure effectively into a EAS discovery procedure. Is this the intent? If it is included, how is it used?
DNAIs and service area of the selected EAS(s) | May be present | Seems to be neither useful nor an issue for our case.
Request type | EAS selection | 
Selected ACR scenario list (NOTE 1) | NP | NP for this request type
AC Profile (NOTE 2, NOTE 3) | NP | NP for this request type
EEC Service Continuity Support (NOTE 2, NOTE 5) | NP | NP for this request type
Associated EES(s) endpoint | ? | Shouldn’t this get note of conditionality?
CAS information | ? | Shouldn’t this get note of conditionality?

## Slide 6: Proposal
It is proposed to simplify the language in 8.15.2.2 to clarify that EAS ID received in information provisioning request of type “EAS selection” which includes Application Group ID may be used to store this info in the ECS-ER.