## Slide 1: MC Gateway UE Discussion
Kiran Kapale, Samsung
MC user authentication and authorization to use MC Gateway UE for MC Service

## Slide 2: Outline
Existing Definitions in Specification
Types of Services and Access for MCPTT user
MCPTT Service Access via MC Gateway UE
Connection Authentication with MC Gateway UE
Connection Authorization with MCPTT Server
MCPTT user authentication and MCPTT user service authorization
Conclusion

## Slide 3: Existing Definitions in Specification
MC user: A user, identified by an MC ID (Mission Critical user identity), who, after authorization, obtains mission critical service(s).
MC ID: The mission critical user identity is also known as the MC ID. The MC ID uniquely identifies the MC service user to the identity management server and linked to a set of credentials (e.g. biometrics, secureID, username/password). The MC ID is used by the identity management server to provide the identity management client a means for mission critical service authentication.
MC service ID: A generic name for the user ID of a mission critical user within a specific MC service. The MC service ID is a globally unique identifier within the MC service that represents the MC service user. MC service ID could be replaced by MCPTT ID, or MCVideo ID, or MCData ID depending on the context.
MC gateway UE: A functional entity that enables simultaneous access to the MC system for multiple MC clients.
Non-3GPP device: A device that enables connectivity towards an MC gateway UE using an access method not specified by 3GPP. A subset of these devices can host an MC client specified by 3GPP.
MC gateway client: A client that enables the authorized binding with one or more MC GW UEs in order to be able to handle MC services (only one MC gateway UE per MC service).
MC gateway UE server: A server on an MC gateway UE that controls authorized binding with multiple MC gateway clients.
MC gateway UE function: Functional block as part of the MC service server that authorises and manages the association between MC client and MC gateway UE.

## Slide 4: Types of Services and Access for MCPTT user
Types of Services
The MCPTT user can get the services provided by
  MC Gateway UE
  MCPTT System
The services provided by MC Gateway UE
  Enables MCPTT access for a MCPTT user residing on non-3GPP capable devices and for devices which are unable to host MCPTT clients.
  Sharing of MC gateway UE 3GPP transport resources.
  Providing location management support ( e.g. triggers related to 3GPP access network)
  Ensure that signalling, media content and traffic attributes, e.g. priority and QoS, of communications between the MCPTT system and MCPTT client remains unaltered.
The services provided by MCPTT Service (No discussion required)
  Number of services provided by MCPTT (e.g., Affiliation, Group Call, Private Call, emergency call etc.) are well defined in the existing specifications.
Access to the service
The MCPTT user can get the access to the services provided by
  MC Gateway UE
  MCPTT Server
The services access provided by MC Gateway UE
  Step 1: MCPTT user authentication with MC Gateway UE to access the MC Gateway UE services.
  Step 2: MCPTT user authorization with MCPTT server to receive the MCPTT services via the MC Gateway UE.
The services access provided by MCPTT Server (No discussion required)
  Step 1: MCPTT user authentication and authorization with IDM to get access token for MCPTT service.
  Step 2: MCPTT user service authorization with MCPTT system for MCPTT service.

## Slide 5: MCPTT Service Access via MC Gateway UE
MCPTT user at non-3gpp device accessing MCPTT service via MC Gateway UE
The MCPTT user can have two set of access credentials
  MC Gateway UE access credentials
  MCPTT System access credentials
The MCPTT client hosted at non-3GPP device
  The MC gateway client at non-3GPP device performs the Connection Authentication and Connection Authorization to access MC Gateway UE service and MCPTT service via MC Gateway UE.
  The MCPTT client at non-3GPP device performs MCPTT user authentication and MCPTT user service authorisation to access the MCPTT service.
The MCPTT client hosted at MC Gateway UE
  The MC gateway client at non-3GPP device performs the Connection Authentication and Connection Authorization to access MC Gateway UE service and MCPTT service via MC Gateway UE.
  The MCPTT client at MC Gateway UE performs MCPTT user authentication and MCPTT user service authorisation to access the MCPTT service.

## Slide 6: Connection Authentication with MC Gateway UE
To support MCPTT user authentication with MC Gateway UE
  The MCPTT user at non-3gpp device is provisioned with MC ID and Credentials and how to obtain these information is out of scope. The credentials are applicable only between non-3GPP device and MC Gateway UE. The MC ID used here is same as that of MC ID provisioned in IdMS for MCPTT user authentication for MCPTT service.
  The MC Gateway UE provisioned with the user's MC ID and MCPTT ID. A mapping between the MC ID and MCPTT ID shall be created and maintained in the MC Gateway UE.
The MCPTT user authentication is supported for both the cases
  The MCPTT client hosted at non-3GPP device.
  The MCPTT client hosted at MC Gateway UE.
The MC service user authentication with MC Gateway UE is done for all the services (MCPTT, MCDATA, MCVIDEO). Individual service specific MC service user authentication is not required.

## Slide 7: Connection Authorization with MCPTT Server
To support MCPTT user authorization with MCPTT Server to use MC Gateway UE
  The MCPTT user at non-3gpp device is provisioned with MCPTT ID and how to obtain this information is out of scope. The MCPTT ID used here is same as that of MCPTT ID provisioned into the MCPTT user database and mapped to a user profile.
  The MCPTT user at non-3gpp device is also provisioned with MC ID and Credentials that are MCPTT system access information and how to obtain these information is out of scope.
  The MC gateway UE configuration data is provisioned in configuration management server. The MCPTT server downloads this configuration to perform the MCPTT user authorization to authorize MCPTT user at non-3gpp device to use the MCPTT service via the MC Gateway UE.
The MCPTT user authorization request between non-3GPP device and MC Gateway UE
  The MC gateway client at non-3GPP device provides the MCPTT ID, and Optionally the MC ID and Credentials to be used by MCPTT client hosted at MC Gateway UE.
The MCPTT user authorization request between MC Gateway UE and MCPTT server
  The MC gateway UE provides the MCPTT ID, and MC GW Service ID. The MCPTT server validates the provided data against MC gateway UE configuration data to authorize the MCPTT user. Creates the binding between MC GW Service ID and MCPTT ID of the MC user at non-3GPP device.
  The MC Gateway UE uses the MC ID and Credentials provided for the MCPTT user identified by MCPTT ID for the MCPTT client which will be instantiated by MC Gateway UE after successful MCPTT user authorization to use the MC Gateway UE. The MC Gateway UE creates mapping between MC ID, MCPTT ID, MCPTT Domain credentials and MC Gateway Access credentials.
The MCPTT user authorization is supported for both cases
  The MCPTT client hosted at non-3GPP device.
  The MCPTT client hosted at MC Gateway UE.
The MC service user authorization with MC service server is performed for service specific.

## Slide 8: MCPTT user authentication and MCPTT user service authorization
To support MCPTT user authentication and MCPTT user service authorization to get MCPTT service
  The MCPTT user at non-3gpp device is provisioned with MC ID and Credentials that are MCPTT Domain access information and how to obtain these information is out of scope.
  If the MCPTT client is hosted in the non-3gpp device then the MC ID and Credentials that are MCPTT Domain access information are used while instantiating the MCPTT client.
  If the MCPTT client is hosted in the MC Gateway UE then the MC ID and Credentials that are MCPTT Domain access information are provided by MCPTT user at non-3gpp device during MCPTT user authorization with MCPTT Server to use MC Gateway UE procedure.
MCPTT user authentication and MCPTT user service authorization (No discussion required)
  The existing specification has well defined procedures.

## Slide 9: Conclusion
Any MCPTT user is always provisioned with MCPTT ID, MC ID and Credentials for MCPTT Domain.
The MCPTT user is using MCPTT service via MC Gateway UE then
  The MCPTT user should authenticate with MC Gateway UE and authorize with MCPTT server to use the MC Gateway UE for MCPTT service.
  To get the MCPTT service, the MCPTT user should authentication and service authorization with IDM and MCPTT server respectively (existing procedures).
Any MCPTT user using his/her provisioned data will be used on-3gpp device to access the MCPTT service. The non-3gpp device can be sharable between multiple MCPTT users.
Proper configuration needs to be provisioned on the non-3GPP device, the MC GWUE and the Configuration management server of MC Domain.
The existing procedures of MC Gateway UE and configuration needs to be reviewed and updated.

## Slide 10: Thank You
Kiran Kapale, Samsung