## Slide 1: Discussion on adding pause and resume option to Ambient Listening
Mythri Hunukumbure, Sivasubramaniam Ramanan
UK Home Office

## Slide 2: SA1 requirements capture
The mini-WID and the CR on ‘pause and resume for AL calls’ requirements were agreed in the last SA1 #109 meeting.
The new clauses in TS 22.179 read as:
6.16.2.2 Ambient listening requirements
6.16.2.2.1 General Ambient Listening requirements
[R-6.16.2.2.1-001] Void
[R-6.16.2.2.1-002] Void
[R-6.16.2.2.1-003] Void
[R-6.16.2.2.1-004] The MCPTT Service shall either terminate Ambient Listening if the MCPTT User being listened to starts to transmit or receive an MCPTT Private Call or an MCPTT Group Call or shall execute one of the two following options.
NOTE: An authorized MCPTT User could initiate Discreet Listening at this point if needed
[R-6.16.2.2.1-005] The MCPTT service shall pause an Ambient Listening call if the MCPTT User being listened to starts to transmit or receive an MCPTT Private Call or an MCPTT Group Call and resume the paused Ambient Listening call once the interrupting call that caused the pause has concluded.
[R-6.16.2.2.1-006] The MCPTT service shall continue the ambient listening call without pause or termination, in parallel with a transmission or reception of an MCPTT Private Call or an MCPTT Group Call, if the MCPTT service allows two parallel calls.

## Slide 3: Current status of AL in TS 23.379
Both remotely initiated and locally initiated AL calls are supported.
Remotely initiated AL call procedure
Locally initiated AL call procedure

## Slide 4: Potential use of AL calls
An MC system can utilize only the ‘remotely initiated’ AL calls. The control room or an authorized dispatcher can initiate an AL call.
The ‘listened to’ user will have no knowledge of the AL call. Only the client 2 of the ‘listened to’ user will handle the AL call.
The ‘listened to’ user should be able to handle the incoming or outgoing calls as normal.
  The pause and resume process for the ’listened to’ user should be handled entirely by the MCPTT client 2 in this scenario.

## Slide 5: Main aspects for developing a solution
We would focus on developing ‘pause and resume’ for remotely initiated AL calls and the ‘listened to’ user’s client 2 will start the process.
  The ‘listened to’ user will be able to receive and initiate MCPTT calls as normal. The pause and resume process will run on the background without user’s knowledge.
We can extend the changes to also cover locally initiated AL calls and when the ‘listening’ user wants to pause and resume the AL call.
  Is complete solution needed in one go or can be staggered? Is there interest to develop solutions here?
  There is the option for the client 2 to inform the ‘listened to’ user about the impending pause of the AL call.