## Slide 1: Remote UE disable – token times and device ID usage
Mythri Hunukumbure & Sivasubramaniam (Ram) Ramanan
UK Home Office

## Slide 2: ‘Immediate’ UE disable need in ESN
Devices can be stolen from police officers during violent disorder and used by bad actors to deny service on operational groups (by using the PTT or emergency key on the device, blocking other floor requests in a group), or can be used to eavesdrop on operational information about the on-going incident.
Device can become damaged resulting in the PTT key being stuck on the ‘on’ position. Examples are when the environmental protection of the device gets damaged and the device suffers water ingress (esp. contact with sea-water). The device must be disabled to prevent denial of service to the group to which the device is affiliated.

## Slide 3: How MC networks set token times
Access and refresh tokens allow the user to keep connectivity with MCX services without the need to re-authenticate with the IdMS.
These token times are set in MC networks purely on operational needs, to allow MC users to move in and out of coverage when attending emergency incidents, without having to re-authenticate.
  In currently operational MC networks the access token times are set to durations of hours, rather than minutes. Refresh token times much longer than the access token times.

## Slide 4: Why token timer trade-off will not work
Given the due priority for operational needs, the token times cannot be reduced to few minutes.
  The evidence from current MC networks is that these times are set as long as possible, to cover a wide range of operational scenarios.
The MC networks also require remote re-enabling of the devices by the control room or authorized dispatcher, before someone logs-in.
  When emergency vehicles are sent for repair/ servicing, a central command should remotely disable them and also re-enable them afterwards.

## Slide 5: Identifying the MC Device
ESN proposes introduction of a unique ID linked to the device (or the client) and use this ID to remotely disable the device.
There are other wider usages of such a unique ID, when a MC user has logged into multiple devices.
  If the location report from a particular device is required.
  If the user is subject to ambient listening, and the control room wants to ambient listen to the device closest to a particular incident.
  If the user is subject to discreet listening, and the control room wants to discreet listen to only the personal device of the user (eg: not to the in-vehicle device where other users in the vehicle may also communicate through).
Ideally, a newly introduced single ID shall be able to meet all above requirements.