## Slide 1
ZTE Corporation
Shao Weixiang
Discussion on
WA7 Digital Twin Aspects

## Slide 2: WA7: Digital Twin Aspects
Work Area Description: Application enablement common aspects of digital twins service and use of digital twins to support various applications.
Candidate Work Tasks:
  WT7.1: Application Digital Twins different from Network Digital Twins to support various verticals such as Factories, Network.
  WT7.2: Enabler Layer supported Service Digital Twins to enable rapid service development, testing, optimization, and deployment of services.
  WT7.3: Application enablement layer impacts for different deployments/business models and exposure of Digital Twin services required by different vertical / applications over 6G.
  WT7.4: Implications to existing SA6 application enablers (e.g. AIML, ADAES, Sensing, EnergySys and other SEAL services) for supporting Digital Twin services.

## Slide 3: Digital Twin as a Service (DTaaS)
Digital Twin as a Service (DTaaS) is a delivery model that provides digital twin capabilities and functions to customers. Under this model, digital service providers deploy digital twin functions on their own servers and clouds, and users can access the service through the network.
The target customers of DTaaS include multiple roles of wireless communication network eco-system, such as: application developers, technology researchers, industry users, telecom operators and equipment vendors.
DTaaS can provide with the following values for the above customers:
  Low-cost trials: DTaaS provides capabilities like physical network capability provisioning, simulation, parameter strategy optimization and algorithm deployment. This enables customers to accurately recreate specific networks in the digital twin environment for low-cost yet efficient execution, iteration and optimization of new technologies, applications and autonomous network strategies.
  Open architecture: DTaaS provides customers with multiple capabilities through open interfaces. This allows equipment vendors, technology researchers and third-party developers to deploy their own algorithms, models and even systems based on the DTaaS platform, realizing efficient innovation of new technologies, applications and autonomous network strategies.
  Easier data acquisition: DTaaS provides capabilities such as data augmentation and data collection, which enables to produce, process, transform, transmit and apply data from different network elements, devices, users and environments into complete and consistent datasets to support network analysis and modeling, making data acquisition much easier.
  Improved model generalizability and interpretability: DTaaS provides model generation capabilities. Using a blended modeling approach that combines knowledge and data, DTaaS builds highly dynamic network models with high fidelity and precision. This leverages the strength of both model types to achieve a holistic network understanding, improving models' generalizability and interpretability.

## Slide 4: DTaaS architecture
Physical network
Data collection and control delivery
Service capability expose layer of digital twin
CN
Service
UE
BS
Data collection
Model generation
Simulation
Visualization
Application layer
Open interfaces
(Service openness and capability invocation)
Intelligent O&M
Digital twin network
Strategy optimization
Algorithm development
Data augmentation
Fault diagnosis and prediction
Physical network provisioning
User perception twinning
SLA service twinning
Industry service twinning
Innovation service twinning: e.g. XR
New application
New technology
…
Twin loop
Virtual-real loop
Network layer of digital twin
Service layer of digital twin
Application Digital Twins
Network Digital Twins
Service Digital Twins
Application enablement
Network element models
Environment models
User behavior
models
Energy consumption models

## Slide 5: DTaaS architecture
Physical networks: The physical network refers to the object simulated by the digital twin network, including the physical core network, transmission network, wireless access network elements, the deployment environment and real services. The physical network provides APIs for the digital twin network to collect data and accept digital twin network configurations and capability callings.
Network layer of digital twin: The twin network constructed in this layer is a virtual image of the physical network in the digital domain. The twin model can reproduce various complex factors in the real field network with high fidelity and has the dynamic simulation ability to simulate the interaction and changes of these complex factors. The network twin layer includes various network element models such as core networks, bearer networks, and wireless access networks, as well as simulations of algorithms and software deployed on them. It also includes modeling complex external physical factors such as wireless environment, user behavior, energy consumption models, etc. The simulation engine can drive various models to run and interact according to communication protocols and physical laws, simulating the dynamic changes of real networks.
Service layer of digital twin: This layer is responsible for executing various service models and conducting realistic and complete end-to-end or partial network segment simulations of real services. These services include traditional network SLA service, B2B industry services, perception services, various new types of services (e.g. XR service). It can simulate and predict uplink and downlink performance of these services in a closed-loop manner, then send the corresponding data to the network layer of digital twin to evaluate the quality of these services.
Service capability expose layer of digital twin: This layer provide various DTaaS capabilities and allocates corresponding resources through orchestration and management to meet the needs of various scenario applications. It provide open interfaces to deliver DTaaS capabilities to different users.
Application layer: The vertical application can call various capabilities of DTaaS through open interfaces. Different applications can support different scenarios and tasks, and the typical scenario task types provided by DTaaS mainly include: self intelligent network, new technology verification, new business verification, etc. The applications can also integrate DTaaS capabilities into other applications and platforms in a more flexible way to complete other highly comprehensive tasks beyond typical scenarios.

## Slide 6: DTaaS basic capabilities
Data collection: This capability is to collect data from specified network elements and modules in both physical network and digital twin network based on user requirements. Efficient and timely data collection from the physical network plays a crucial role in monitoring network status and constructing twin models. There are two methods for data collection: specialized measurement devices and real-time monitoring of signals, services, and metrics during network operation. The measurement device method entails higher time costs but yields precise and direct results, such as using drones to capture on-site topographic information or employing channel measurement devices to detect wireless channel responses. The monitoring method carries relatively lower costs but may impact regular operations, providing indirect data for certain tasks, such as wireless signal records or network operation logs. Hence, careful consideration is necessary to determine the appropriate data collection method for different tasks. For instance, foundational data can be collected using specialized measurement devices in a one-time process, followed by ongoing adjustments and enrichment of the model using measurements during network operation to ensure the model's evolutionary capabilities.
Model generation: This capability is to refine, train, and generate models from raw data. Traditional twin models include mathematical and data-driven models. Mathematical models offer some level of generalization but face challenges in obtaining all parameters and boundary conditions for specific scenarios and entities, limiting the construction of highly precise models. Data-driven models, on the other hand, utilize input-output data from specific scenarios and entities to train neural networks, providing a good fit for those cases but may lack generalization abilities. Hence, knowledge-and-data dual-driven approach is recommended. This approach abstracts mathematical formulas and physical laws into knowledge, which is then utilized to reduce the complexity of neural networks and enhance the generalization abilities. For instance, in the case of wireless channel modeling, one can leverage knowledge about the transmission characteristics of electromagnetic signals, along with digital maps, satellite and aerial photographs, field measurement results, and data generated during network operations, to collectively achieve context-specific based accurate modeling.
Simulation: This capability is to utilize the simulation engine within the digital twin entity for conducting simulation calculations on a specified network. Given the time-sensitive nature of network decisions, computational speed and efficiency play a vital role in facilitating real-time decision-making within the digital twin network.
Visualization: This capability is to visually present network data, network status, environment, and models using various methods such as charts, videos, 3D models, and even virtual reality technologies. Visualization plays a critical role in DTaaS by effectively conveying complex and high-dimensional information in an intuitive manner, empowering users to directly interact with and control the physical network through the interface. One of the key challenges in visualization is the efficient execution of 3D modeling and rendering. To address this, lightweight modeling techniques, including polygon reduction and elimination of redundant information, are employed to minimize the complexity of 3D models. Additionally, Level of Detail (LOD) techniques are utilized to achieve multi-level representations, reducing the rendering workload in 3D scenes. As a result, visualization and interaction can be seamlessly experienced on lightweight terminals while maintaining a high-quality visual presentation.

## Slide 7: DTaaS advanced capabilities
Strategy optimization: This capability is to optimize parameters and strategies. Due to the complexity of wireless networks and the vast space for parameter and policy optimization, it is necessary to provide AI based optimization capabilities, such as multi-objective black box optimization techniques under multiple constraints, or online optimization capabilities based on reinforcement learning that can adapt to changing environments, businesses, and networks. It is necessary to choose appropriate AI solutions based on specific problems for intelligent and efficient processing.
Algorithm deployment: This capability enables users to seamlessly integrate their own algorithms or modules into the digital twin network.
Data augmentation: This capability is to generate customized virtual scenarios as per user requirements and extract data from designated network elements and modules to create datasets on-demand. Users have the flexibility to define their desired scenarios, whether based on real or virtual environments. They can also specify the data to be collected and the preferred format. The digital twin network operates accordingly, generating the necessary data to fulfill user requests. This capability enables users to generate cost-effective datasets from a diverse range of scenarios, spanning various modules and contexts. These datasets can be valuable for research or decision-making purposes.
Fault diagnosis and prediction: This capability is to diagnose and predict network faults based on imported network telemetry data, logs, and Key Performance Indicator (KPI) information. Root cause analysis plays a vital role in fault diagnosis and prediction and can be achieved through two methods: causal relationship diagram and Failure Mode and Effects Analysis (FMEA). Both approaches are highly effective for daily network fault diagnosis and prediction, leading to significant reductions in network downtime and prevention of potential failure risks.
Physical network provisioning: This capability enables users to deploy their software in real physical network environments, facilitating real-time evaluation of software responsiveness, quality, and performance in authentic environments.

## Slide 8: DTaaS typical scenarios
No. | Customer | Category | Requirement | Requirement Description | DTaaS capabilities | Open Interfaces
1 | Operators and industrial users | Network construction and network planning | Site construction and site planning | Use the digital twin system for network planning. The customer wants to know how to build sites | 1,2,3,4,5 | Input: scenarios data , such as photos and maps Output: Recommended antenna locations, engineering parameters, and the corresponding RSRP or KPI distribution
2 | Operators and industrial users | Network construction and network planning | Introduction of new functions | The customer has a built-up network, and wants to know the benefits and changes of the network if new functions are introduced. | 1,2,3,4,6 | Input: engineering parameters, scenario data, network parameters and KPI records, new function information Output: Network KPIs after new functions are introduced
3 | Operators and industrial users | Network construction and network planning | Introduction of new frequencies and new sites | The customer has a built-up network and wants to know the benefits and changes of the network if new frequencies and new sites are introduced. | 1,2,3,4 | Input: engineering parameters, scenario data, network parameters and KPI records, new frequencies and new sites information Output: Network KPIs after new frequencies and new sites are introduced
4 | Operators and industrial users | Network O&M | Online Network Visualization | The customer has a built-up network and wants to use the visualization to display the real-time operations and control network online. | 1,4 | Input: element management system interface, other data interface Output: Visual interface, network operation command
5 | Operators and industrial users | Network O&M | Network Fault Diagnosis | The customer has a built-up network, and hopes to analyze the root causes of network faults and provide strategy. | 1,2,3,4,8 | Input: element management system interface, KPI data interface, network O&M log, fault-related information Output: Root cause of the fault, strategy
6 | Operators and industrial users | Network optimization | Offline Network Optimization | The customer has a built-up network and wants to know how to adjust parameters to optimize the network. | 1,2,3,4,5 | Input: engineering parameters, scenario data, network parameters and KPI records, target KPI sets Output: optimized parameters and KPIs
7 | Operators and industrial users | Network optimization | Online Network Optimization | The customer has a built-up network and wants to automatically optimize the network | 1,2,3,4,5 | Input: element management system interface, other data interface Output: Visual interface, network operation command (optimization configuration)

## Slide 9: DTaaS typical scenarios
No. | Customer | Category | Requirement | Requirement Description | DTaaS capabilities | Open Interfaces
8 | Researchers | Data augmentation | Algorithm data set generation | The customer wants to research the AI algorithm, but lacks data from live network, and hopes to use the digital twin platform to generate a large amount of field data for training. The algorithm can be L1, L2, L3 or network-level algorithm | 1, 2,3,7 | Input: data type Output: data set
9 | Researchers | Data augmentation | Channel data set generation | The customer wants to research the AI algorithm, but lacks field environment, and hopes to use the digital twin platform to produce amount of field channels data for training | 1,2,3,7 | Input: channel data type Output: data set
10 | Researchers | Data derivation | Service data set generation | The customer wants to research AI algorithms but lacks actual service data, and hopes to use the digital twin platform to produce amount of field service data for training | 1,2,3,7 | Input: service data type Output: data set
11 | Researchers | Innovation verification | Algorithm verification | The customer has a new L1 algorithm, but does not know how it performs in the live network, and hopes to validate the algorithm. | 3,6,9 | Input: algorithm function module, system and environment configuration Output: algorithm performance in the system and specific environment
12 | Researchers | Innovation verification | Protocol pre-research | The customer has a new protocol design and wants to validate the performance | 3,6,9 | Input: all modules related to the protocol Output: protocol performance in the system and specific environments
13 | Researchers | Innovation verification | Large AI/ML model training | The customer is training a wireless network large AI/ML model and wants to evaluate/score the output of the model and build reward network | 1,2,3 | Input: site, engineering parameters, scenario data, photos, maps, and network parameters Output: corresponding KPIs
14 | Developer | APP development | APP development | The customer develops a corresponding new APP for any of the foregoing scenarios | 1,2,3,4,5,6,7,8,9 | Input: API and development data Output: APP

## Slide 10: DTaaS use case: new XR service introduction
A new application that supports the performance evaluation of XR in commercial wireless network has been constructed to complete new service verification. This application invokes DTaaS capabilities such as data collection, model generation , and simulation.
Data collection: The drone with high-precision positioning capability faces the antenna plane, automatically identifies the edge of the antenna by using the grayscale recognition algorithm, and obtains the engineering parameter data in real time.
Model generation : Digital modelling is performed for base stations, wireless channels, terminals, core networks, and XR services, to build high-precision digital twins for physical networks and lay the foundation for accurate guarantee of user experience.
Simulation: Digital twin platform uses key technologies such as ray tracing (see figure), GPU acceleration, and AI calibration for dynamic simulation, and improve the precision of model in the digital twin network through simulation of drive test and fixed-point test, and evaluate the difference between the output of the platform and those of the physical network.
The results of large-scale fixed-point test have shown that the twinning precision of XR performance has reached over 90% in areas such as parks and squares, etc.
Ray Tracing Demonstration

## Slide 11: DTaaS use case: high-speed railway
A new application that supports visual and precise network planning for high-speed railway scenario has been constructed based on digital twin platform. The application invokes DTaaS capabilities such as data collection, model generation , simulation, strategy optimization, and visualization.
Data collection: The image data of the tower and antenna system of the high-speed railway site is collected. During the test, 12 sites and 119 antennas are surveyed, where 113 antennas can be tested for engineering parameter acquisition, accounting for 95%.
Model generation : After the digital survey is completed, the data such as the map, site location, and engineering parameters are pre-processed, and the digital twin model of the high-speed railway is constructed through the digital twin components, high-speed railway networks, and digital twin engines.
Simulation: Run the digital twin system for simulation, use the adaptive Simpson algorithm and the greedy algorithm combined with ray tracing algorithm to search the local network planning parameters, and use the group intelligent algorithm, reinforcement learning algorithm combined with Monte Carlo algorithm to search the global network planning parameter.
Strategy optimization : The digital twin platform exports the optimal parameters of base station hardware, RF software, and system software.
Visualization: The 3D real-view models, pre-built models, panoramic photos, and satellite maps are displayed in a multi-layer, multi-perspective, and multi-dimensional manner. The single canvas is used to implement scaling and roaming, marking and positioning, and measurement design, bringing users one-stop operation experience and dynamically display geographic data over time.
Higher-precision digital twins support more precise network planning, in this case, the Mean Error of RSRP is 1 dB and the RMSE is 4 dB. The precision planning based on digital twins can support the improvement of engineering optimization efficiency in the early stage of network construction. It can be verified that the number of low-rate users on the high-speed railway system is improved significantly, and the proportion of users with the rate lower than 2Mbps is reduced by about 50 percentage points.
Digital twin site visualization

## Slide 12: DTaaS use case: port
A new application that supports precise network planning has been constructed for port scenario, which is for B2B use. The application invokes DTaaS capabilities such as data collection, model generation , simulation, strategy optimization , and algorithm deployment.
Data collection: Based on the port environment twin information collection, the image data is obtained through tilt photography by using drone-mounted camera, and a deep learning algorithm model is constructed by using computer graphics, so as to identify, extract, and reconstruct the on-site environment to obtain the 3D physical modeling of the environment.
Model generation : Equipment entities and network elements in real world can be flexible combined and deployed based on the 3D vector map, and the variables such as truck, quay bridge, and container can be added together to build a digital twin model.
Simulation: Driverless trucks service is divided into automatic driving mode and remote driving mode in the Port. The network transmission requirements under the two modes are quite different. Considering the characteristics of the environment changes greatly, the digital twin model can be used to implement precise network planning, preferentially ensure the large rate time-frequency backhaul service, and ensure the location changes of various containers and shore cranes.
Strategy optimization : AI calibration is performed based on the drive test result, and parameter optimization is performed based on the calibrated results. By adjusting the horizontal angle of the antenna, the RSRP of 18% of the sampled points has seen a consistent improvement.
Algorithm deployment: The planning and optimization module and black box optimization algorithm are used to optimize antenna engineering parameters and beams in the network. This module can be opened to different optimization algorithm providers, who can upload their own modules according to different optimization objectives and algorithm development to complete different network planning and optimization.
real photo
modeling picture

## Slide 13: What SA6 can do
DTaaS capabilities | SA5 (TS 28.561) | SA6 objects
Data collection | Current support collect physical network information include Performance data, MDT/Trace data, Fault management data, Configuration data | Collect digital twin network information Collect physical network information by specialized measurement devices Collect data through Sensing, EnergySys and other SEAL services Data delivery by SEALDD
Model generation | Current support mathematical model for Simulation Not support service twin models | Knowledge-and-data dual-driven models Service twin models
Simulation | Network twin supported | Service twin simulation
Visualization | SA4 scope | 
Strategy optimization | Not Supported | Optimize parameters and strategies AI based optimization through AIML
Algorithm deployment | Not Supported | Integrate vertical own algorithms or modules
Data augmentation | Current support to generate ML training data and user experience data | Generate customized virtual scenarios and datasets on-demand
Fault diagnosis and prediction | Network twin supported | Service twin diagnosis and prediction
Physical network provisioning | Network twin supported | Service twin provisioning Distributed physical network provisioning according to different deployments/business models

## Slide 14: Thank you！