## Slide 1: MC service UE disable and enable
AIRBUS
3GPP TSG-SA6 Meeting #69 S6-254107
Wuhan, China, 13th Oct 2025 - 17th Oct 2025

## Slide 2: Solutions under consideration
MDM/EMM
  Not covered in this presentation, see discussion paper from UKHO
    https://www.3gpp.org/ftp/tsg_sa/WG6_MissionCritical/Informal_ConfCalls/2025/IWS_20250918_MC_service_UE_remote_mgmt/inbox/S6-254xxx%20-%20Device%20disable%20for%20ESN-UKHO.pptx
Server based disable/enable feature
  Access/refresh token based solution not covered in this paper, see the above DP from UKHO
  A high level architecture&solution included, but has major issues
Adding new MC service procedures to cover DM
  Ref: the proposed CR0679 and CR0680 for TS 23.280
  Major issues identified
Dedicated DM server and client

## Slide 3: Server based UE disable/enable feature
  What would this require?
    MC servers should separately authorize the MC service UE for each request from the clients
    A common database would be needed, containing information of the MC service UEs enable/disable status

## Slide 4: Server based disable/enable feature
Issues:
Currently no MC service UE (device) access control in MC standards
  The user authentication / service authorisation functionality (TS 33.180) should be extended with device authentication/authorization (MC service UE id)
Most of the client-server messages should be amended with a new (mandatory) element (MC service UE id)
  This would be a major update to many (all?) MC specifications and potentially also a major backwards compatibility issue in the client-server interface
New functionality needed to all MC servers to check the device enable/disable status at every transactions
How to perform (MC) data erasure in the device when it is disabled?

## Slide 5: Adding new MC service procedures for disable/enable
Issues with the proposed CR0679 and CR0680
    CR679: https://www.3gpp.org/ftp/tsg_sa/WG6_MissionCritical/TSGS6_068_Gothenburg/docs/S6-253237.zip
    CR680: https://www.3gpp.org/ftp/tsg_sa/WG6_MissionCritical/TSGS6_068_Gothenburg/docs/S6-253240.zip
  No MC service client can communicate with the server if a user is not logged in
  Therefore, the MC service UE management (disable/enable) will not work e.g. in the following cases:
    The stolen UE is powered on, but the (MC) user is not logged in. As the thief does not have the credentials, the MC service UE cannot be accessed  not possible to erase any sensitive (MC) data from the UE
    A disabled UE is to be reactivated, but the user is unable to log in because the device is disabled, meaning the enable command cannot be sent

## Slide 6: Dedicated DM server
New device management server and client
UE’s device management client is started when UE is powered on
  A requirement can be added to 3GPP TS but the actual process (to start the client) is out of 3gpp scope
Enable/disable information is stored in MC service UE
  Possible server side database is implementation specific
DM client authentication (with DM server) is separated from the MC user authentication / service authorization
  Mutual TLS authentication can be used (mutual TLS already existing in 3GPP standards)
  No backwards compatibility issues to the MC specifications