ETSI CN1/ SMG3-WPA	Tdoc N1-99-506

Sophia Antipolis,

1-4 June 1999

| CHANGE REQUEST No : | Axxx | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
| --- | --- | --- |
| Technical Specification GSM / UMTS: | 04.08 | Version | 6.3.0 |  |
| Submitted to SMG |  | for approval |  | without presentation ("non-strategic") | x |  |
| list plenary meeting or STC here ( | for information |  | with presentation ("strategic") |  |  |
| PT SMG CR cover form. Filename: crf26_3.doc |

| Proposed change affects: | SIM |  | ME | X | Network | x |
| --- | --- | --- | --- | --- | --- | --- |

(at least one should be marked with an X)

| Work item: | GPRS |
| --- | --- |

| Source: | Nortel Networks | Date: | 27 May 1999 |
| --- | --- | --- | --- |

| Subject: | Align Mean Throughput definition in GSM 04.08 with GSM 03.60 |
| --- | --- |

| Category: | F Correction | x | Release: | Phase 2 |  |
| --- | --- | --- | --- | --- | --- |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (one category | B Addition of feature |  |  | Release 97 | X |
| and one release | C Functional modification of feature |  |  | Release 98 |  |
| only shall be | D Editorial modification |  |  | Release 99 |  |
| marked with an X) |  |  |  | UMTS |  |

| Reason for change: | This change request proposes to align the Mean Throughput definition in GSM 04.08 with that specified in GSM 03.60. GSM 03.60 defines: 0 0 0 0 1 = Best Effort |
| --- | --- |

| Clauses affected: | 10.5.6.5 Table 10.5.156 |
| --- | --- |

| Other specs | Other releases of same spec |  | ( List of CRs: |  |
| --- | --- | --- | --- | --- |
| affected: | Other core specifications |  | ( List of CRs: |  |
|  | MS test specifications / TBRs |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |

| Other comments: |  |
| --- | --- |

<--------- double-click here for help and instructions on how to create a CR.

#### 10.5.6.5	Quality of service

The purpose of the quality of service information element is to specify the QoS parameters for a PDP context.

The quality of service is a type 3 information element with 4 octets length.

The quality of service information element is coded as shown in figure 10.5.138/GSM 04.08 and table 10.5.156/GSM 04.08.

|  | 8 7 6 5 4 3 2 1 |  |
| --- | --- | --- |
|  | Quality of service IEI | octet 1 |
|  | 0 0 spare | Delay class | Reliability class | octet 2 |
|  | Peak throughput | 0 spare | Precedence class | octet 3 |
|  | 0 0 0 spare | Mean throughput | octet 4 |

Figure 10.5.138/GSM 04.08: Quality of service information element

Table 10.5.156/GSM 04.08: Quality of service information element

Reliability class, octet 2 (see GSM 03.60)
Bits
3 2 1
0 0 0	Subscribed reliability class
0 0 1	Acknowledged GTP, LLC, and RLC; Protected data
0 1 0	Unacknowledged GTP; Acknowledged LLC and RLC, Protected data
0 1 1	Unacknowledged GTP and LLC; Acknowledged RLC, Protected data
1 0 0	Unacknowledged GTP, LLC, and RLC, Protected data
1 0 1	Unacknowledged GTP, LLC, and RLC, Unprotected data

All other values are interpreted as Subscribed reliability class in this version 
of the protocol.
Delay class, octet 2 (see GSM 02.60 and GSM 03.60)
Bits
6 5 4
0 0 0	Subscribed delay class 
0 0 1	Delay class 1
0 1 0	Delay class 2
0 1 1	Delay class 3

1 0 0	Delay class 4 (best effort)

All other values are interpreted as Subscribed delay class in this version 
of the protocol.

Bit 7 and 8 of octet 2 are spare and shall be coded all 0.

Precedence class, octet 3 (see GSM 03.60)
Bits
3 2 1
0 0 0	Subscribed precedence
0 0 1	High priority
0 1 0	Normal priority
0 1 1	Low priority

All other values are interpreted as Unspecified Subscribed precedence in this version of the protocol.

Peak throughput, octet 3
Bits
8 7 6 5
0 0 0 0	Subscribed peak throughput
0 0 0 1	Up to 1 000 octet/s
0 0 1 0	Up to 2 000 octet/s
0 0 1 1	Up to 4 000 octet/s
0 1 0 0	Up to 8 000 octet/s
0 1 0 1	Up to 16 000 octet/s
0 1 1 0	Up to 32 000 octet/s
0 1 1 1	Up to 64 000 octet/s
1 0 0 0	Up to 128 000 octet/s
1 0 0 1	Up to 256 000 octet/s
All other values are interpreted as Subscribed peak throughput in this 
version of the protocol.

Mean throughput, octet 4
Bits
5 4 3 2 1
0 0 0 0 0		Subscribed mean throughput
0 0 0 0 1		Best effort
0 0 0 1 0		100 octet/h
0 0 0 1 1		200 octet/h
0 0 1 0 0		500 octet/h
0 0 1 0 1		1 000 octet/h
0 0 1 1 0		2 000 octet/h
0 0 1 1 1		5 000 octet/h
0 1 0 0 0		10 000 octet/h
0 1 0 0 1		20 000 octet/h
0 1 0 1 0		50 000 octet/h
0 1 0 1 1		100 000 octet/h
0 1 1 0 0		200 000 octet/h
0 1 1 0 1		500 000 octet/h
0 1 1 1 0		1 000 000 octet/h
0 1 1 1 1		2 000 000 octet/h
1 0 0 0 0		5 000 000 octet/h
1 0 0 0 1		10 000 000 octet/h
1 0 0 1 0		20 000 000 octet/h
1 0 0 1 1	50 000 000 octet/h

The value Best effort indicates that throughput shall be made available to the MS on a per need and availability basis.

All other values are interpreted as Subscribed mean throughput in this 
version of the protocol.
Bits 8 to 6 of octet 3 are spare and shall be coded all 0.