ETSI SMG3WPA	Tdoc N1-99572

Sophia Antipolis	Revision of Tdoc N1-99491

1-4 June 99

| CHANGE REQUEST No : | A120r2 | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
| --- | --- | --- |
| Technical Specification GSM / UMTS: | 03.60 | Version | 6.3.1 |  |
| Submitted to SMG | 29 | for approval | X | without presentation ("non-strategic") |  |  |
| list plenary meeting or STC here ( | for information |  | with presentation ("strategic") |  |  |
| PT SMG CR cover form. Filename: crf26_3.doc |

| Proposed change affects: | SIM |  | ME | X | Network |  |
| --- | --- | --- | --- | --- | --- | --- |

(at least one should be marked with an X)

| Work item: | GPRS |
| --- | --- |

| Source: | SMG3 WPA | Date: | 2 June, 1999 |
| --- | --- | --- | --- |

| Subject: | Circuit Switched and Packet Switched priority handling |
| --- | --- |

| Category: | F Correction | X | Release: | Phase 2 |  |
| --- | --- | --- | --- | --- | --- |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (one category | B Addition of feature |  |  | Release 97 | X |
| And one release | C Functional modification of feature |  |  | Release 98 |  |
| Only shall be | D Editorial modification |  |  | Release 99 |  |
| marked with an X) |  |  |  | UMTS |  |

| Reason for change: | For a class B mobile, when a TBF is on, there is the problem with all the cases which would request a dedicated channel establishment, such as : what to do with a periodic-or not- LU needed, what to do with a speech call requested by the user what to do with an emergency speech call requested by the user etc… CS quality of service should not be decreased because of another feature introduction. All this is related to the open issue ”CS and PS priority handling”. If nothing is standardised regarding this issue, release 97 MS are likely to have really different behaviours, and further standardising will get more and more difficult. The general solution proposed here for this is : Give priority to CS : cancel the TBF, establish the dedicated channel, and trigger the suspend mechanism. Meanwhile, for responses to CS paging, MO –non emergency- user calls, MO SS ans SMS, this is an implementation dependant whether to give priority to CS. |
| --- | --- |

| Clauses affected: | 6.9.1.2 and 8.3.2. |
| --- | --- |

| Other specs | Other releases of same spec |  | ( List of CRs: |  |
| --- | --- | --- | --- | --- |
| affected: | Other core specifications |  | ( List of CRs: |  |
|  | MS test specifications / TBRs |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |

| Other comments: |  |
| --- | --- |

<--------- double-click here for help and instructions on how to create a CR.

#### 6.9.1.2	Routeing Area Update Procedure

A routeing area update takes place when a GPRS-attached MS detects that it has entered a new RA, when the periodic RA update timer has expired, or when a suspended MS is not resumed by the BSS (see subclause "Suspension of GPRS Services"). The SGSN detects that it is an intra SGSN routeing area update by noticing that it also handles the old RA. In this case, the SGSN has the necessary information about the MS and there is no need to inform the GGSNs or the HLR about the new MS location. A periodic RA update is always an intra SGSN routeing area update.

An MS in READY state due to anonymous access shall not perform routeing area updates for the AA MM context. If the MS has entered a new routeing area, a new Anonymous Access PDP Context Activation procedure shall be initiated. The old context is implicitly deleted upon expiry of the READY timer.

## 16.2	Circuit-switched Services

The ability for a GPRS user to access circuit-switched services depends on the subscription held, the network capabilities, and the MS capabilities. Interaction between GPRS and circuit-switched services is described in subclause "Interactions Between SGSN and MSC/VLR".

### 16.2.1	Suspension of GPRS Services

When a GPRS-attached MS enters dedicated mode, and when the MS limitations make it unable to communicate on GPRS channels, the MS shall request the network for suspension of GPRS services. The suspend and resume procedure is illustrated in Figure 1. Each step is explained in the following list.

Figure 1: Suspend and Resume Procedure

1)	The MS enters dedicated mode.

2)	The MS sends an RR Suspend (TLLI, RAI) message to the BSS. The BSS may terminate any ongoing GPRS traffic for this TLLI.

3)	The BSS sends a Suspend (TLLI, RAI) message to the SGSN, and the SGSN acknowledges by returning Suspend Ack. The BSS shall store TLLI and RAI in order to be able to request the SGSN to resume GPRS services when the MS leaves dedicated mode.

4)	Eventually, the BSS determines that the circuit-switched radio channel shall be released. If the BSS is able to request the SGSN to resume GPRS services, the BSS shall send a Resume (TLLI, RAI) message to the SGSN. The SGSN acknowledges the successful outcome of the resume by returning Resume Ack.

5)	The BSS sends an RR Channel Release (Resume) message to the MS. Resume indicates whether the BSS has successfully requested the SGSN to resume GPRS services for the MS, i.e., whether Resume Ack was received in the BSS before the RR Channel Release message was transmitted. The MS leaves dedicated mode.

6)	If the BSS did not successfully request the SGSN to resume GPRS services, or if the RR Channel Release message was not received before the MS left dedicated mode, then the MS shall resume GPRS services by sending a Routeing Area Update Request message to the SGSN, as described in subclause "Routeing Area Update Procedure".

The full handling of suspended MSs in the BSS and the SGSN is implementation dependent. Typically, the SGSN should not page suspended MSs.

If the MS performs an inter-BSC handover while suspended, then TLLI and RAI should be transferred as BSC-to-BSC information in the Handover Required and Handover Request messages, see GSM 08.08. This allows the new BSC to initiate the Resume request procedure to the SGSN. In the case where the BSC-to-BSC information was not transferred or not understood, then the MS doesn’t receive an indication that resumption has been successful, and the MS shall resume GPRS services by initiating a Routing Area Update Request procedure as described in step 6.

### 16.2.2	GPRS and Dedicated Mode Priority Handling

An MS in class-B mode of operation that communicates on GPRS radio channels when a dedicated channel is needed, shall immediately abort the GPRS communication and trigger the Suspend and Resume procedure.

[Response to circuit-switched paging, ]non-emergency MO circuit-switched calls, MO SMS, and MO supplementary services are exceptions to the above rule. In these cases, it is an implementation choice whether to immediately abort GPRS communication or to delay the dedicated mode establishment.