3GPP CN2-A	Tdoc 2NA99344

Sophia Antipolis (France)											revised N2-99 337

15 – 16 April, 1999

| CHANGE REQUEST No : | A058r2 | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
| --- | --- | --- |
| Technical Specification GSM / UMTS: | 09.78 | Version | 6.3.0 |  |
| Submitted to SMG | #29 | for approval | x | Without presentation ("non-strategic") | x |  |
| list plenary meeting or STC here ( | for information |  | with presentation ("strategic") |  |  |
| PT SMG CR cover form. Filename: crf26_3.doc |

| Proposed change affects: | SIM |  | ME |  | Network | x |
| --- | --- | --- | --- | --- | --- | --- |

(at least one should be marked with an X)

| Work item: | CAMEL Phase 2 |
| --- | --- |

| Source: | Ericsson | Date: | 15/04/1999 |
| --- | --- | --- | --- |

| Subject: | Corrections on the ASN.1 descriptions and Procedure Flow descriptions. |
| --- | --- |

| Category: | F Correction | X | Release: | Phase 2 |  |
| --- | --- | --- | --- | --- | --- |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (one category | B Addition of feature |  |  | Release 97 | x |
| and one release | C Functional modification of feature |  |  | Release 98 |  |
| only shall be | D Editorial modification |  |  | Release 99 |  |
| marked with an X) |  |  |  | UMTS |  |

| Reason for change: | The description of the Cancel operation in sect. 6.1 is incomplete. This incompleteness is rectified in the present CR. The description of the RequestReportBCSMEvent in sect. 6.1 is incorrect. This incorrectness is rectified in the present CR. The description of the InitialDP procedure in sect. 9.19.1.1 is incorrect. This incorrectness is rectified in the present CR. |
| --- | --- |

| Clauses affected: | 6.1, 9.19.1.1 |
| --- | --- |

| Other specs | Other releases of same spec |  | ( List of CRs: |  |
| --- | --- | --- | --- | --- |
| Affected: | Other core specifications |  | ( List of CRs: |  |
|  | MS test specifications / TBRs |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |

| Other comments: |  |
| --- | --- |

***   First modified section   ***

6.1	Operation types

...

Cancel 							::= OPERATION

ARGUMENT

CancelArg

ERRORS {

CancelFailed

}

--  Direction: gsmSCF  gsmSSF, or gsmSCF  gsmSRF, Timer: Tcan

--  When this operation is sent from gsmSCF to gsmSSF, then all outstanding requests will be cancelled.
--  The following outstanding requests will be cancelled: RequestReportBCSMEvent, ApplyChargingReport,

--  CallInformationReport.
--

--  When this operation is sent from gsmSCF to gsmSRF, then the indicated previous operation will be

--  cancelled.--  The following operations may be cancelled: PlayAnnouncement and PromptAndCollectUserInformation.

***   Next modified section   ***

...

RequestReportBCSMEvent	::= OPERATION

ARGUMENT

RequestReportBCSMEventArg

ERRORS {

MissingParameter,

SystemFailure,

TaskRefused,

UnexpectedComponentSequence,

UnexpectedDataValue,

UnexpectedParameter

}

--  Direction: gsmSCF -> gsmSSF, Timer: Trrb

--  This operation is used to request the gsmSSF to monitor for a call-related event (e.g., BCSM

--  events such as answer or disconnect), then send a notification or request for instructions

--  back to the gsmSCF when the event is detected.

...

***   Next modified section   ***

## 9.19	InitialDP procedure

### 9.19.1	General description

This operation is sent by the gsmSSF after detection of a TDP-R in the BCSM, to request the gsmSCF for instructions to complete the call.

#### 9.19.1.1	Parameters

-	serviceKey:

This parameter identifies for the gsmSCF unambiguously the requested IN service. It is used to address the correct application/SLP within the gsmSCF (not for gsmSCF addressing).

-	calledPartyNumber:

This parameter contains the number used to identify the called party in the forward direction, e.g. the Called party number of ISUP (see ETS 300 356-1 [4]). This parameter shall be sent only in the Mobile Terminating and Mobile Forwarding cases.

-	callingPartyNumber:

This parameter carries the calling party number to identify the calling party or the origin of the call. The encoding of the parameter is defined in ETS 300 356-1 [4].

-	callingPartysCategory:

Indicates the type of calling party (e.g., operator, pay phone, ordinary subscriber).

-	originalCalledPartyID:

This parameter carries the dialled digits if the call has met call forwarding on the route to the gsmSSF.

-	locationNumber:

This parameter is used to convey the geographical area address for mobility services. It is used when "callingPartyNumber" does not contain any information about the geographical location of the calling party (e.g., origin dependent routing when the calling party is a mobile subscriber).

-	bearerCapability:

This parameter indicates the type of the bearer capability connection to the user:

-	bearerCap:

This parameter contains the value of the ISUP User Service Information parameter.

The parameter "bearerCapability" shall only be included in the InitialDP operation in case the ISUP User Service Information parameter is available at the gsmSSF.

If User Service Information and User Service Information Prime are available at the gsmSSF the "bearerCap" shall contain the value of the User Service Information Prime parameter.

-	eventTypeBCSM:

This parameter indicates the armed BCSM DP event, resulting in the InitialDP operation.

-	redirectingPartyID:

This parameter indicates the directory number the call was redirected from.

-	redirectionInformation:

It contains forwarding related information, such as redirecting counter.

-	iPSSPCapabilities:

Indicates which gsmSRF resources supported within the VMSC/GMSC the gsmSSF resides in are attached and available.

-	additionalCallingPartyNumber:

The calling party number provided by the access signalling system of the calling user.

-	highlayerCompatibility:

This parameter indicates the type of the high layer compatibility, which will be used to determine the ISDN-teleservice of a connected ISDN terminal. For encoding, DSS1 (see ETS 300 403-1 [5]) is used.

-	iMSI:

IMSI of the mobile subscriber for which the CAMEL service is invoked. For encoding see GSM 09.02 [15].

-	subscriberState:

The state of the mobile subscriber for which the CAMEL service is invoked. The possible states are Busy, Idle, Not reachable and Not provided from VLR. For encoding see GSM 09.02 [15].

-	locationInformation:

This parameter indicates the whereabouts of the MS, and the age of the information defining the whereabouts. For encoding see GSM 09.02 [15].

-	ext-BasicServiceCode:

Indicates the Basic Service Code. For encoding see GSM 09.02 [15].

-	callReferenceNumber:

This parameter gives the network call reference number assigned to the call by the GMSC/MSC. For encoding see GSM 09.02 [15].

-	mscAddress:

This parameter gives the mscId assigned to the GMSC/MSC. For encoding see GSM 09.02 [15].

-	calledPartyBCDNumber:

This parameter contains the number used to identify the called party in the forward direction. It may also include service selection information, including ( and # digits. This parameter shall be sent only in the MO case.

-	time&Timezone:

This parameter contains the time that the gsmSSF was triggered, and the time zone that the invoking gsmSSF resides in.

-	gsm-ForwardingPending:

This parameter indicates that a forwarded-to-number was received and the call will be forwarded due to GSM supplementary service call forwarding in the GMSC.