| 3GPP N2 Meeting | Document | N2A000318 |
| --- | --- | --- |
| Charleston, USA, 27-31 MAR 2000 |  | e.g. for 3GPP use the format TP-99xxx or for SMG, use the format P-99-xxx |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 23.078 | CR | 128 | Current Version: | 3.4.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submission to: |  | for approval |  |  | strategic |  | (for SMG |
| list expected approval meeting # here ( | for information |  |  | non-strategic |  | use only) |
| Form: CR cover sheet, version 2 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CR-Form-v2.doc |
| Proposed change affects: | (U)SIM |  | ME |  | UTRAN / Radio |  | Core Network |  |
| (at least one should be marked with an X) |
| Source: | Siemens | Date: | 27 March 2000 |
| Subject: | Principle in opening TCAP dialogue by SGSN |
| Work item: | CAMEL Phase 3 |
| Category: | F Correction |  | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature |  |  | Release 97 |  |
| shall be marked | C Functional modification of feature | x |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 | x |
|  |  |  |  | Release 00 |  |
| Reason for change: | For ease TCAP relationship handling between SGSN and SCP, all the CAP operations except ActivityTestGPRS are proposed to be initiated by the SGSN. There are four possible operations whose dialogue the SGSN opens, i.e., ApplyChargingGPRS, EntityReleaseGPRS, EventReportGPRS and InitialDPGPRS. Other operations which are initiated by the SCP shall follow one of the previously listed operations and use the same dialogue. The proposed changes are: (1) Delete figures 6.14 the Process GPRS_SSF sheets 8 and 9. (2) Add a figure on the next page as one of the Process GPRS_SSF. |
| Clauses affected: | 6 |
| Other specs | Other 3G core specifications | x | ( List of CRs: | 29.078-061 |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

Treatment of ActivityTestGPRS in monitoring state.?

Figure 6.14 x: Process GPRS_SSF (sheet x)

Figure 6.14 h: Process GPRS_SSF (sheet 8)

Figure 6.14 i: Process GPRS_SSF (sheet 9)