Meeting Report

TSG CN WG2#18
Puerto Rico, USA

14 – 18 May, 2001

Chairman:	Keijo Palviainen (Nokia)

Secretary:   Andrijana Jurisic  (MCC)

Host:   The North American Friends of 3GPP

List of participants:		Annex A

Output documents		Annex B

Tdoc list (incl. the status)		Annex C

Joint meeting between CN1/2/3/4	Annex D

Documents could be found on the 3GPP-server:

ftp://ftp.3gpp.org/TSG_CN/WG2_camel/Plenary/TSGN2_18_PuertoRico/Docs

# 1	Opening of the meeting and approval of the agenda

N2-010278 :  CN2 chairman, Title: Proposed meeting agenda

Discussion : It is agreed meeting will start at 8 a.m. and end at 5 p.m. every day

Conclusion :Approved

# 2	Allocation of documents to agenda items

N2-010364 : MCC,  Title: Tdoc list before CN2#16 starts

Discussion :

Conclusion : Noted

N2-010279 :  CN2 chairman,  Title: Alocation of documents to agenda items

Discussion : Document 281 is CN2 year 2001 meeting calendar, source is MCC. Document 366 will be CN2 year 2002 meeting calendar provided by CN2 chairmen.  Tdoc 356 and 357 are R99 documents related to CAMEL3 and will be allocated to agenda item 6.4.

CR#296 is allocated for document 356, and CR 175 is allocated for document 357. Those CRs will need mirror CRs for Rel-4. Document 360 is revised to 367. Document 326 is discussion document  will be the first document on the item 8.4. C-DOT documents will be presented not before Wednesday and paper copies should be provided before presentation. New document  from Ericsson for the agenda item 6.3 (CAMEL3/GPRS) will be provided during the meeting.

Conclusion : Noted

# 3	Reports

N2-010327 : MCC,  Title: Draft Meeting Report CN2#17, Sophia Antipolis

Discussion :

Conclusion: Aproved

N2-010332 : C2 chairman,  Title:  Report from CAMEL4 CPH adHoc Meeting, Newburry

Discussion :

Conclusion: Aproved

N2-010328:   MCC,   Title: Draft Meeting report from CN#11

Discussion:

Conclusion: Noted

N2-010329:   MCC,   Title: Draft Meeting report from  SA#11

Discussion: In the last plenary first Rel-4 was introduced. All the 99 CRs have to be mirrored to Rel-4.

Conclusion:Noted

N2-010365 :  Lucent ,   Title: Report from SA1 CAMEL adHoc Meeting, Helsinki

Discussion: Two change requests have been approved against R 99 (Clarification of PDP context QoS change notification to the CSE  and Clarification of CUG requirements). Three change requests introduce new functionality for CAMEL Phase 4 (Inclusion of ODB data in ATM, Location information during an ongoing call and Enhance ATI operation (CAMEL4) – GPRS Location).

Next SA1 AdHoc meeting will be 25th of June and the topics for discussion will be requirements of CAMEL on IP Multimedia Subsystem and CPH charging requirements. One LS statement from this meeting  will be provided as Tdoc 369. Title is LS statement on Charging requirements for call party handling, source: SA1 adHoc and will be under agenda item 4.

S1 documents 341,342 and 464 in the report are all Rel-5. Rel-5 could implement GPRS QoS  according to SA1. Rel-5 CR was withdrawn in SA1.Updated document will be provided. Document N2-010365 is revised to N2-010370.

Conclusion:Revised to 370

N2-010370:   SA1 ,   Title: Report from SA1 CAMEL adHoc Meeting, Helsinki

Discussion:

Conclusion: Noted

# 4	Input Liaison Statements

N2-010330 : SA1, Type: LS IN , Title: LS on IMS Service Provision

Discussion : SA2 discussed the subject on Service Provision for the IM Subsystem and came to the following conclusion which is brought to the attention of SA, SA1 and CN working groups:Besides the Cx interface SA2 agreed on a single standardised protocol to be supported by the S-CSCF for service control. Guidelines for further details are summarised in a new chapter to 23.228. This details are given in S2-010797 which is approved by S2 and attached to this LS.

CAP interface between IM SSF and CSE will not change.  Only service control is showed on the diagram in attachment. Using interface which is closed to SIP interface  SA tried to come up with a single interface to S-CSCF. SIP+ name needs to be changed

IM SSF includes CCF and BCSM also. Do we need to change BCSM? CN2 should specify IM SSF and CN1 shall specify SIP+. CSI downloading is opened question for CN1.

What is the protocol between between IM SSF and S-CSCF – Some companies propose control protocol and some propose standard SIP?

S-CSCF will have a filter function to filter messages which will be delivered to IM SSF. IMS SSF does not have a full call state.  IMS SSF could tell the armed EDPs to CSCF to change3 filtering dynamicaly.

Peter Kim SA2 delegate, proposed to write all the questions to S2 in form of LS statement. One of the questions is where is the basic call state maschine defined.

Conclusion: Noted

N2-010369 : SA1 adHoc, Type: LS IN , Title: LS "Charging requirements for Call Party Handling”

Discussion: TSG SA WG1 asks TSG CN WG2 to recognise the charging requirements for CPH are still under discussion. CN2 to provide the response to LS statement discussed in form of LS statement to SA1. Siemens things that requirements from operators have to be taken in to consideration. Sumio will send open questions to the mailing list. Alcatel document is implementation related and it will be taken in consideration regarding summary of open issues. Siemens would like to have concrete quidance to CPH issues.

Conclusion: Noted

N2-010458: Excpected LS IN from SA1

Conclusion: LS was not received

- Work item management & miscellaneous

  - IPR call reminder

Reminder to Individuals Members and the persons making the technical proposals about their obligations under their respective Organizational Partners IPR Policy.

An IPR declaration was announced by the chairman. IPRs does not need to be declared at the WG meeting but should go to the respective organization. No IPRs were declared.

## Work Item (WI) status review

N2-010331 : MCC, Type: Discussion , Title: Latest version of the Workplan

Discussion : CN2 chairman will make sumarry of progress of the existing tasks. MCC will update work plan  and add new tasks accordingly.

Conclusion: Noted

N2-010372:   CN2 Chairman,Title:CN2#18 comments on the work plan

Discussion :After approval source will become CN2.

Conclusion: Revised to 471

N2-010471:   CN2 Chairman,Title:CN2#18 comments on the work plan

Discussion :

Conclusion: Approved

N2-010363: MCC, Type:info, Title: List of CN2 specifications after TSG#11

Discussion: Specs DB has to be changed, because R96 have a wrong title. Status list is maintained by MCC , on the server, after each plenary. This document will not be sent to plenary.

Conclusion: Noted

## Meeting calendar of year 2002

N2-010366 : CN2 chairman, Title: CN2 year 2002 meeting calendar

Discussion: There will be six coolocated meetings in year 2002. Comments to the work plan will be sent to the plenary.  Siemens requests that the meeting place have to be covered by GSM network.

Conclusion :Noted

## CAMEL4 CN Work Item Description

N2-010280 : CN2 Chairman, Type: WID, Title: Rel-5 CAMEL4 scope in Rel-5 for TSG-CN

Discussion : 23.060 will be added in the list of specifications.

Conclusion: Revised to 371

N2-010371 : CN2 Chairman, Type: WID, Title: Rel-5 CAMEL4 scope in Rel-5 for TSG-CN

Discussion : WID will be entered to the Work plan with a level of approval WG.

Conclusion: Approved without presentation

# 6	CAMEL3, Resolution of outstanding issues for Release 99

## 6.1	CAMEL3, Miscellaneous

N2-010307 : 23.008,  R99,  Vodafone, Type:  CR, Title: Supported CAMEL Phases in VLR is temporary

Discussion : “Supported CAMEL Phases in VLR" is currently marked as permanent data in the HLR and are changed to temporary data, so that it can be updated when the subscriber changes VLR. “Negotiated  Camel Phases” are also temporary fields.

Conclusion : Revised to 377

N2-010377: 23.008,  R99,  Vodafone, Type:  CR, Title: Supported CAMEL Phases in VLR is temporary

Discussion: Revised document will be provided to MCC.

Conclusion: Endorsed without presentation, sent to CN4

N2-010362 : 23.008  Rel-4,  Vodafone, Type:  CR, Title: Supported CAMEL Phases in VLR is temporary

Discussion :

Conclusion :Revised to 378

N2-010378: 23.008  Rel-4,  Vodafone, Type:  CR, Title: Supported CAMEL Phases in VLR is temporary

Discussion:

Conclusion: Endorsed without presentation, will be sent to CN4

N2-010323 : 29.078 , CR161, R99,  Ericsson, Type:  CR, Title: Correction to IMPORT statements

Discussion : The present CR proposes to add “ExtensionField” to the IMPORT statement in section 8.1 for the data type definitions from CAP-datatypes and to add an IMPORT statement in section 5.1 of 29.078 to IMPORT “ExtensionContainer” from 29.002. This MAP data module shall be referenced in section 2.1 as well.

Change the cover sheet instead of essential correction to Correction. Relevant CR to Rel-4 needed. CCITT(0) is used for most parameters, not (4). Category is marked as F (essential correction).

Conclusion :revised to 384

N2-010384 : 29.078 , CR161, R99,  Ericsson, Type:  CR, Title: Correction to IMPORT statements

Discussion :

Conclusion :Approved without presentation

N2-010385: 29.078, CR176, Rel-4, Ericsson, Type: CR, Title: Correction to IMPORT statements

Discussion : This document is Rel-4 mirror CR to document  384 (R99). CR#176 is allocated during the meeting.  It will be included in the draft specification for Rel-5 by Rogier off line.

Conclusion: Approved without presentation

N2-010333 : 29.078 , CR162, R99,  Siemens, Type:  CR, Title: ASN.1 syntax correction

Discussion : CR corrects certain errors in the ASN.1 description of CAP such as erroneous upper or lower case for parameter of type definitions, missing imports. EstablishTemporaryConnection end-of-bracket is in wrong place. Subcategory has to be specified as essential correction.

The first change shall be cancelled – part of Rogiers tdoc 384.

MCC will check if it is possible within MCC to check all the ASN1 errors (ASN1 compiler) and if ASN1 files could be extracted.

Conclusion : Revised to 386

N2-010386 : 29.078 , CR162, R99,  Siemens, Type:  CR, Title: ASN.1 syntax correction

Discussion: Revision of Tdoc 333. Originally was approved without presentation, and later revised again.

Conclusion : Revised to 453

N2-010453 : 29.078 , CR162, R99,  Siemens, Type:  CR, Title: ASN.1 syntax correction

Discussion :Revision of 386

Conclusion : Revised to 456

N2-010456 : 29.078 , CR162, R99,  Siemens, Type:  CR, Title: ASN.1 syntax correction

Discussion: Revision of 453

Conclusion : approved

N2-010334 : 29.078 , CR163, Rel-4,  Siemens, Type:  CR, Title: ASN.1 syntax correction

Discussion : Needs same changes as document  333. Category is A.

Conclusion :revised to 387

N2-010387 : 29.078 , CR163, Rel-4,  Siemens, Type:  CR, Title: ASN.1 syntax correction

Discussion : It will be incorporated in Rel-5draft specification offline.

Conclusion : Revised to 454

N2-010454  : 29.078 , CR163, Rel-4,  Siemens, Type:  CR, Title: ASN.1 syntax correction

Discussion : It will be incorporated in Rel-5 offline. This document was originally approved without presentation and later revised.

Conclusion : Revised to 457

N2-010457  : 29.078 , CR163, Rel-4,  Siemens, Type:  CR, Title: ASN.1 syntax correction

Discussion : It will be incorporated in Rel-5 offline

Conclusion : Approved

N2-010335 : 29.078 , CR164, R99,  Nokia, Type:  CR, Title: Correction of the MAXIMUM-FOR-FCI-BILLING-CHARGING value

Discussion : The value of MAXIMUM-FOR-FCI-BILLING-CHARGING does not allow record 160 octets free format data, therefore the maximum length is corrected to the value 174. Same value is used for all cases (FCI-GPRS/SMS/calls) but they have different data (leg, PDPid, etc).

No calculation is available for the result value of MAXIMUM-FOR-FCI-BILLING-CHARGING. Revised document will include the monitoring. Subcategory is “essential correction”.

Conclusion :Revised to388

N2-010388 : 29.078 , CR164, R99,  Nokia, Type:  CR, Title: Correction of the MAXIMUM-FOR-FCI-BILLING-CHARGING value

Discussion : This document is revision of 335. Summary of change needs improvement. Ralated ASN is copied for information.

Conclusion :Revised to 441

N2-010441 : 29.078 , CR164, R99,  Nokia, Type:  CR, Title: Correction of the MAXIMUM-FOR-FCI-BILLING-CHARGING value

Discussion : Revision of document 388.

Conclusion : approved without presentation

N2-010336 : 29.078 , CR165, Rel-4,  Nokia, Type:  CR, Title: Correction of the MAXIMUM-FOR-FCI-BILLING-CHARGING value

Discussion :

Conclusion :Approved

N2-010373 : 29.002 , R99,  Lucent, Type:  CR, Title: Addition of SCCP information for the interface between gsmSCP and SGSN

Discussion : Postponed to Tuesday

Conclusion :withdrawn

N2-010374 : 29.002 , Rel-4,  Lucent, Type:  CR, Title: Addition of SCCP information for the interface between gsmSCP and SGSN

Discussion : Postponed to Tuesday

Conclusion :withdrawn

N2-010375 : 29.002 , Rel-5,  Lucent, Type:  CR, Title: Addition of SCCP information for the interface between gsmSCP and SGSN

Discussion : Postponed to Tuesday

Conclusion :withdrawn

## 6.2			CAMEL3/ATM&ATSI

No contributions received.

## 6.3	CAMEL3/GPRS

N2-010290 : 23.078  R99, CR 290,  Rapporteur, Type: CR , Title: Correction of error implementing CR 23.078-181r2

Discussion :   PDP Initiation Type set to “C” in Initial DP GPRS. Initial DP GPRS includes this IE at the initial contact with the gsmSCF for the GPRS session. PDP Initiation Type (IE) indicates whether a PDP context was established as a result of a network-initiated request or as a result of a subscriber request.

The originitor was Lucent.

Conclusion : Approved

N2-010291 : 23.078  Rel-4, CR 291,  Rapporteur, Type: CR , Title: Correction of error implementing CR 23.078-181r2

Discussion :   Corresponding Rel-4 CR to document 290 . CAMEL phase 3 CRs will be automatically implemented in Rel-5 by rapporteur.

Conclusion : Approved

N2-010282 : 23.078  R99, CR 286, Nokia, Type: CR , Title: GGSN address in SGSN to SCP interface

Discussion :   CR specifies that GGSN address (IE) contains the  GGSN address for control

plane to which the MS is connected. If the GPRS Event type contains DP Change of Position Context, then the GPRS Event Specific Information IE contains GGSN address is C1.If the GPRS Event type contains DP PDP context establishment acknowledgement, then the GPRS Event Specific Information IE contains GGSN address as Mandatory.

GGSN adress is reported to SCP and charging ID is unique only with GGSN address.

Conclusion : Approved

N2-010283 : 23.078  Rel-4,  CR 287, Nokia, Type: CR , Title: GGSN address in SGSN to SCP interface

Discussion :The change is identical as 282, but the category is A and is related to Rel-4.

Conclusion : Approved

N2-010284 : 23.078  Rel-5, CR   , Nokia, Type: CR , Title: GGSN address in SGSN to SCP interface

Discussion :

Conclusion : Approved

N2-010320 : 29.078  R99, CR 158,  Ericsson, Type: CR , Title: Correction to IDP-GPRS & EDP-GPRS:reporting the GGSN Address for signalling

Discussion :   Similar change is in document 282 for stage2.

Conclusion : Rejected

N2-010318 : 23.078  R99, CR 294,  Ericsson, Type: CR , Title: Correction to GPRS SDL:no state transition for QoS induced ACR-GPRS

Discussion :   The erroneous change in the spec, from “Monitoring” to “WFI”, shall be undone. The gprsSSF shall remain in state “monitoring” when it reports a Quality of Service change to the gsmSCF, by sending one or two ACR-GPRS operations (Process GPRS_SSF ,sheet 17).

Marked as essential correction. Rel-4 CR needed.

Conclusion : Revised to389

N2-010389 : 23.078  R99, CR 294,  Ericsson, Type: CR , Title: Correction to GPRS SDL:no state transition for QoS induced ACR-GPRS

Conclusion: Approved without presentation

N2-010390 : 23.078  Rel-4, CR 297,  Ericsson, Type: CR , Title: Correction to GPRS SDL:no state transition for QoS induced ACR-GPRS

Discussion: Tdoc390 and CR297 allocated during the meeting for  Rel-4 CR.

Conclusion: Agreed without presentation

N2-010319 : 29.078  R99, CR 157,  Ericsson, Type: CR , Title: Correction to ACR-GPRS procedure description

Discussion :  This CR proposes correction of the ApplyChargingReportGPRS Procedure description.

GprsSSF should not go to IDLE if ACR-GPRS due to duration/volume expiry (different to call related cases). SDL goes to IDLE in this case. Content is approved, but cover page has to be updated.

Conclusion : Revised to 391

N2-010391: 29.078  R99, CR 157,  Ericsson, Type: CR , Title: Correction to ACR-GPRS procedure description

Discussion :

Conclusion : Approved without presentation

N2-010392:  29.078  Rel-4, CR 177,  Ericsson, Type: CR , Title: Correction to ACR-GPRS procedure description

Discussion: This is identical CR as in document 391, but related to Rel-4. CR# 177 is allocated during the meeting.

Conclusion: Approved without presentation

N2-010337 : 29.078  R99, CR 166,  Nokia, Type: CR , Title: Correction of the gprsSSF error handling

Discussion : The gprsSSF reaction to the operation error shall be independent of the opening or continuation of the dialogue. Differences related to TC-BEGIN and TC-CONTINUE error handling are removed.

Proposal is to report errors in TC continue. Cover page updated, subgategory marked as “essential correction”, revision number is incremented.

Conclusion : Revised 393

N2-010393 : 29.078  R99, CR 166,  Nokia, Type: CR , Title: Correction of the gprsSSF error handling

Conclusion: Approved without presentation

N2-010338 : 29.078,  Rel-4, CR 167, Nokia , Type: CR , Title: : Correction of the gprsSSF error handling

Discussion :   Identical CR as 393, but related to Rel-4.

Conclusion : Approved

N2-010339 : 29.078,  R99, CR 168, Nokia , Type: CR , Title: Clarification of the TC dialogue termination

Discussion :      The termination of the TC dialogue is clarified so that after class 1 operation, the related result/error have to be received before the termination of the TC dialogue.

gsm SSF has to be replaced by gprs SSF . EntityReleasedGPRS is also class 1 operation. Reason for change has to changed.

Conclusion : Revised to 394

N2-010394: 29.078,  R99, CR 168, Nokia , Type: CR , Title: Clarification of the TC dialogue termination

Discussion: Revised document 339

Conclusion: Approved without presentation

N2-010340 : 29.078,  Rel-4, CR 169, Nokia  , Type: CR , Title: Clarification of the TC dialogue termination

Discussion :

Conclusion : Revised to 395

N2-010395 : 29.078,  Rel-4, CR 169, Nokia  , Type: CR , Title: Clarification of the TC dialogue termination

Discussion :

Conclusion: Approved without presentation

N2-010341 : 29.078,  R99, CR 170, Nokia , Type: CR , Title: The termination of the dialogue is not clear after ActivityTestGPRS Return Result.

Discussion : The termination of the TC dialogue is clarified so that after ActivityTestGPRS Return Result, the TC dialogue shall be terminated with empty TC-END.

In the last sentence “TC dialoque” should be  instead of “dialoque” only. The same change could be also in the reason for change. The Title should be changed to “Correction of the TC dialogue termination after ActiavityTestGPRS Return Result”.

Category is F, subcategory should be essential correction. Last sentence should have components instead component.

Conclusion : Revised to 396

N2-010396 : 29.078,  R99, CR 170, Nokia , Type: CR , Title: Correction of the TC dialogue termination after ActivityTestGPRS result

Discussion :

Conclusion: Approved wihout presentation

N2-010342 : 29.078,  Rel-4, CR 171, Nokia , Type: CR , Title: The termination of the dialogue is not clear after ActivityTestGPRS Return Result.

Discussion :   Same changes should be enetered as in previous documet.

Conclusion : Revised to 397

N2-010397 : 29.078,  Rel-4, CR 171, Nokia , Type: CR , Title: NEW TITLE

Discussion :

Conclusion :Approved without presentation

N2-010360 : 29.078,  R99, CR 173, Alcatel , Type: CR , Title: Correction of gprsSSF TC usage

Discussion :

Conclusion : revised to 367 before the presentation

N2-010367 : 29.078,  R99, CR 173, Alcatel , Type: CR , Title: Correction of gprsSSF TC usage

Discussion : 29.078 specifies that the gprsSSF shall memorise the gsmSCF address that is returned by the gsmSCF in the first TC_Continue. The gprsSSF needs this address for the possible follow-up TC dialogues comprising a common GPRS dialogue. However the TC interface itself does not provide this address to its TC user.

It is proposed to include the required information in the user information. The TC requirement is SGSN internal behaviour. SCCP level conveys the address anyway. For SCP it is optional to send the UserInformation.

Load sharing is on SCCP layer. Adress is mandatory if SCP is using load sharing.

If we change user information,  is it only internal change in SGSN? Is there any change in the bit flow from SGSN to gsmSCF? Yes

ITU-T TCAP spec provides the mechanism for TCAP to memorise SSF address, and uses that address for subsequent messages, but with GPRS we would like to continue GPRS dialogue when TC dialogue has been discontinued.  We need mechanism for gsm SSF to transport user addres for TCAP layer, so that TC dialogue can be reestablished within GPRS dialogue. This is the reason for recommendation to use User Information.

If GPRS CSI contains address different as the one in the address in SCCP layer, then use GPRS –CSI (according to proposal)?

Keijo: This CR is backward incopatible.If the entity doesn’t support this parameter, it leads to rejection of PDP context. Solution is to introduce cutover date after which this solution can be used.

Alcatel and Ericsson wants this from day one. Siemens doubts the need of this CR for R99. T-Mobil sees this as a backward incompatible solution. Maybe a transition period could be introduced. Lucent does see  this necessary to implement load sharing.

T-Mobil proposes the address in the CAP level. This solution is less elegant but backward compatible. Lucent agrees, Siemens does not agree.

Siemens preference is not to approve this CR. Reality is that good external interface has to be found. Siemens already has solved it on proprietary way.

Proposal to define a date from which this parameter will be used. CAP Operations TC continue and TC Connect are the last ones before we disconnect TC dialogue. Stephen proposal is to have this parameter on the CAP layer in mentioned messages. If we have SCP that operates in load sharing mode, new dialog can be rejected and load sharing will not work. According current specification, different implementations are possible, so Stephen would prefer a clear solution that will enable roaming agreements and other operators requirements.

Decision is to put this parameter to CAP layer. Lucent proposal is not to have cutover date. Christian will draft CRs that have CAP layer address and will draft new CR  for 23.078 CR304 and for 29.078 CR183 for R99.

This CR will be sent to plenary in a separate package as a contraversal.

Conclusion:  Noted

N2-010463  23.078, CR#304, Alcatel, Title:Indication of gsmSCF Address in Continue GPRS and Connect GPRS Ifs

Discussion : Wording of “Consequences if not approved” have to be changed. No cutover date, parameter is put to CAP layer.

Conclusion: Revised to 472

N2-010472  R99, 23.078, CR#304, Alcatel, Title:Indication of gsmSCF Address in Continue GPRS and Connect GPRS Ifs

Discussion :

Conclusion: Approved without presentation

N2-010473 : Rel-4,23.078, CR#305, Alcatel, Title:Indication of gsmSCF Address in Continue GPRS and Connect GPRS Ifs

Discussion :

Conclusion: Approved without presentation

N2-010464: R99, 29.078, CR#183, Alcatel,Title: Indication of gsmSCF Address in Continue GPRS and Connect GPRS IFs

Discussion : Section 12.7.1.3 has the text that needs to be removed. Cover page has to be changed.

Conclusion: Revised to 474

N2-010474 : R99, 29.078, CR#183, Alcatel,Title: Indication of gsmSCF Address in Continue GPRS and Connect GPRS

Discussion : This document should be in sepparate package together with previous contraversal CRs.

Conclusion: Approved without presentation

N2-010475:  Rel-4, 29.078, CR#184, Alcatel,Title: Indication of gsmSCF Address in Continue GPRS and Connect GPRS

Discussion : This document should be in sepparate package together with previous contraversal CRs.

Conclusion: Approved without presentation

N2-010361 : 29.078,  R99, CR#174, Alcatel , Type: CR , Title: Setting of PDP Type Organization Spare Bits

Discussion : 3G TS 29.060 defines the information element End User Address, which is reference for 3G TS 29.078. According to 3G TS 29.060 the four most significant bits of  PDP Type Organization are set to 1. The sender of parameter End User Address shall set most significant bits of PDP Type Organization to 1 according to reference given.

Reason for change has to be improved. Title needs to be corrected in the increased version  of the CR. News title will be “Setting of the End User spare bits”. This CR is supported by consensus. In GTP protocol these bits are set to 1 and in CAP are set to 0. The implementation doesn’t use them. Setting of spare bits, even if ignored in the receiving side, makes the protocol future proof  and spare bits can  be used in the future. Change  becomes essential when spare bits are taken into some other use.

This CR was ment that last 4 bits of the PDP Type Organization octet are set to 1.

Conclusion : Revised to 442

N2-010442 :29.078, R99, CR#174, Alcatel, Type:CR, Title: Setting of End User Address Spare Bits

Discussion :

Conclusion: approved without presentation

N2-010443: 29.078, Rel-4, CR#181, Alcatel , Type: CR , Title: Setting of PDP Type Organization Spare Bits

Discussion :CR  number for Rel-4 CR is allocated during the meeting.

Conclusion: Approved without presentation

N2-010368: R99, Ericsson, Type: Discussion Document, Title: “Reporting of data volume and duration in excess of 4Gbyte and 24 hours respectively”.

Discussion document raises an issue concerning GPRS charging. The operators will have to limit PDP context to 4 GB or to 24 hours. This problem is valid also for CS, but it is more likely that PDP context which is opened continously exceeds 24 hours. Warning for R99 is necessary and implementaion for Rel-5 shall be done.

Option 5 would not be welcome for R99.

Rogier (source) preference is option 1. All the other options do require further study. Stage which it is concerned has to be agreed. Option 1 shall be applied to R99(warning).

Keijo: Until now nothig is specified if this case happens, therefore maybe some implementations are already done (specific to vendors). This problem is serious and urgent. Action has to be taken and CRs to this topic are expected for July meeting. Proposal of final  solution for R99 will be presented in Tdoc 398, CR 298 (allocated during the meeting).

Conclusion:Noted

N2-010398  23.078, R99, CR 298, Ericsson,Ttype: CR Inclusion of warning note for the reporting of total duration or volume for GPRS

Discussion : Proposed solution is to include a warning note in 23.078 to inform Service Logic designers that if no tariff switch timer is used, the maximum duration or volume that may be reported is 24 hour and 4 Giga Byte respectively. The implication of this may be that a Service Logic shall restrict the charging of a Session or PDP Context to the first 24 hour and the first 4 Giga Byte and then allow Session and PDP Context continuation without charging or force terminate the Session or PDP Context after 24 hour or 4 Giga Byte, depending on which one of these occurs first.

SGSN behaviour is not mandated here. SCP has to be changed to gsmSCF. Lucent would like to have a roll-over counter in ASN.

Conclusion:Revised to 459

N2-010459  23.078, R99, CR 298, Ericsson,Ttype: CR Inclusion of warning note for the reporting of total duration or volume for GPRS

Discussion : Contraversial document and has to be put in separate package for CN plenary

Conclusion:Approved without presentation

N2-010460  23.078, Rel-4, CR 303, Ericsson,Ttype: CR Inclusion of warning note for the reporting of total duration or volume for GPRS

Discussion : SCP  should be changed to gsmSCF. Controversial document.

Conclusion:Approved without presentation

N2-010449 : 23.078, R99, CR#301, Vodafone, Type: CR, Title:CAMEL Capability Handling in GPRS-CSI

Discussion : CAMEL Capability Handling should be included in the GPRS-CSI downloaded to the SGSN. It is already specified in MAP. CR proposal is  inclusion of CAMEL Capability Handling in Insert Subscriber Data

Conclusion:Approved

## N2-010450: 23.078, Rel-4, CR#302, Vodafone, Type: CR, Title:CAMEL Capability Handling in GPRS-CSI

Discussion :

Conclusion:Approved

## 6.4	MO SMS

N2-010292 : 29.078 R99,CR#155, Siemens, Type: CR , Title: Contradiction and inconsistency among descriptions on SMS

Discussion : There are contradictions and inconsistensies among descriptions on SMS related messages in 29.078, therefore Siemens recommend to delete contradicting and inconsistent description from subclause 12.1.3.1.

Siemens wants to have all the options.   12.12.1.3 allows SSF to send components in TC-END (last sentence). Second section denies it. SSF TC-END with components makes reception of errors imposible.

Conclusion : Revised to 399

N2-010399: 29.078 R99,CR#155, Siemens, Type: CR , Title: Contradiction and inconsistency among descriptions on SMS

Discussion: The last sentence in the section 12.1.2.1.3 has to be following:: In the case of the basic end gsmSSF/gprsSSF shall send TC-END with zero components.

Conclusion:Revised to 461

N2-010461: 29.078 R99,CR#155, Siemens, Type: CR , Title: Contradiction and inconsistency among descriptions on SMS

Discussion: Ericsson proposal is not to start the sentence with a condition.

Conclusion: Revised to 466.

N2-010466: 29.078 R99,CR#155, Siemens, Type: CR , Title: Contradiction and inconsistency among descriptions on SMS

Discussion:

Conclusion: Approved without presentation

N2-010293 : 29.078 Rel-4, CR#156, Siemens, Type: CR , Title: Contradiction and inconsistency among descriptions on SMS

Discussion : The reason for change is the same as in 292, but the document is related to Rel-4.

Conclusion : Revised to 462

N2-010462: 29.078 Rel-4, CR#156, Siemens, Type: CR , Title: Contradiction and inconsistency among descriptions on SMS

Discussion : The reason for change is the same as in 292, but related to Rel-4.

Conclusion : Revised to 467

N2-010467: 29.078 Rel-4, CR#156, Siemens, Type: CR , Title: Contradiction and inconsistency among descriptions on SMS

Discussion :

Conclusion :  Approved without presentation

N2-010356:  23.078, R99, CR296 Title:Introduction of Reference Number for MO-SMS

Number bertween 0-255 is reference number which produces a MS when sending SMS from MS to MSC. Proposal is to introduce other reference number for MO-SMS which is produced by MSC, not by MS.

If an MO-SMS is subject to CAMEL control, then:

- The MSC/SGSN shall generate a Reference Number.

- The MSC/SGSN shall report this Reference Number, together with the MSC Address/SGSN Number, to the SCP.

3.  The MSC/SGSN shall place this Reference Number and the MSC Address/SGSN Number in the MO-SMS CDR.

Rogier:Reference number should be marked Mandatory, and MSC is not dependent on receivingof  Ref. Number from the other network, but is selfcontrol.

Cover page shall to be changed, has to have CR296 and Wi CAMEL3 but not CAMEL4. Subcategoy will be “agreed by consensus”. Reference number will be mandatory . Rel-4 CR is needed. If this is  approved, ouput liason statement will be sent to SA1 in document 401. If document 400 which is related to R99 is approved, then Rel-4 CR will be submitted.

Conclusion: Revised to 400

N2-010400: 23.078,R99, CR296 ,Ericsson, Title: Introduction of Reference Number for MO-SMS

Discussion:Has to be put in a separate package

Conclusion: Revised to 437

N2-010437: 23.078,R99, CR296 ,Ericsson, Title: Introduction of Reference Number for MO-SMS

Discussion: SGSN address has to be changed in SGSN number and the same pricip is applied to MSC. Improvements in wording are necessary.

Has to be put in a separate package.

Conclusion: Revised to 444

N2-010444: 23.078,R99, CR296 ,Ericsson, Title: Introduction of Reference Number for MO-SMS

Discussion:This document will be put in a separate package as contraversal one. Siemens and Nokia has some conserns about this CR and the document might be rejected on the plenary.The corresponding Rel-4 CR is allocated during the meeting (CR300)

Conclusion: Approved without presentation

N2-010445: 23.078,Rel-4, CR300 ,Ericsson, Title: Introduction of Reference Number for MO-SMS

Discussion:Has to be put in a separate package as contraversal one. Siemens and Nokia has some conserns about this CR and the document  might be rejected on the plenary.

Conclusion: Approved without presentation

N2-010401: Ericsson, Output LS , Title: Liaison Statement on introduction of SMS Reference Number for SMS

Discussion: This LS will be put in the same package as corresponding CRs, and if approved on the plenary it will  be sent to SA5. SGSN has to be changed to SGSN number. Title will be corrected in order to cover MT SMS. Attachment needs to  be updated.

Conclusion: Revised to 446

N2-010446: Ericsson, Output LS , Title: Liaison Statement on introduction of SMS Reference Number for SMS

Discussion: This LS will be put in the same package as SMS CRs, and if approved on the plenary it will  be sent to SA5. SGSN has to be changed to SGSN number.

Conclusion: Conditionaly approved, if corresponding CRs are approved on  TSGCN#12 plenary

N2-010357: 29.078, CR 175,R99, Ericsson,  Title:Introduction of Reference Number for MO-SMS

Discussion: The present CR proposes the introduction of a Reference Number for CAMEL control of Mobile Originated SMS (MO-SMS). During the processing of a MO-SMS, the MSC/SGSN may produce a CDR. If that MO-SMS is subject to CAMEL control, the SCP may also produce a CDR for that MO-SMS. It shall be possible for CDR post processing systems to correlate the MO-SMS CDR produced by the MSC/SGSN with the MO-SMS CDRs produced by the SCP.

This may be achieved by means of a ‘SMS Reference Number’. This Reference Number os produced in the MSC/SGSN at the time of MO-SMS processing. The MSC/SGSN reports this MO-SMS Reference Number to the SCP, together with the MSC Address/SGSN Address.
The MSC/SGSN shall place this MO-SMS Reference Number and the MSC Address/SGSN Address in the CDR for that SMS. The MO-SMS Reference Number shall be unique within the MSC/SGSN.
WI should be CAMEL3 in cover page, and CR 175.

Conclusion: Revised to 402

N2-010402: 29.078, CR 175,R99, Ericsson,  Title:Introduction of Reference Number for MO-SMS

Discussion: One spelling error and parameter names have to be changed.

Conclusion: Revised to 447

N2-010447: : 29.078, CR 175,R99, Ericsson,  Title:Introduction of Reference Number for MO-SMS

Discussion: It has to be put in the same package with SMS CRs

Conclusion: Approved without presentation

N2-010448: 29.078, Rel-4, CR#182, Ericsson  Title:Introduction of Reference Number for MO-SMS

Discussion: It has to be put in the same package with SMS CRs

Conclusion: Approved without presentation

## 6.5			CAMEL3/Call Related

N2-010308 : 23.078, R99, CR#292, Vodafone, Type:  CR, Title: Handling of second SIFOC

Discussion : In CAMEL Phase 2, the MSC sends the VLR a second SIFOC if the call was subject to CAMEL invocation based on O-CSI. This allows the VLR to check the conditional outgoing call barrings against the destination routeing address provided by the gsmSCF. In CAMEL Phase 3, the handling was enhanced to deal with D-CSI and N-CSI as well. The MSC should send the VLR a second SIFOC if the call was subject to at least one of O-CSI, D-CSI and N-CSI. However, following through the SDLs (Procedure CAMEL_MO_Dialled_Services), the MSC will send the second SIFOC regardless of whether there was any CAMEL invocation for the call.

Sumio proposed initialisation of CAMEL_invocation before CAMEL_OCH_MSC_INIT. Corresponding CR to 23.018 shall be provided in Tdoc 405. Corresponding CR to Rel-4 will be provided in document 407 during the meeting.

Conclusion : Revised to 404

N2-010404: 23.078, R99, CR#292, Vodafone, Type:  CR, Title: Handling of second SIFOC

Discussion :

Conclusion: Approved

N2-010309 : 23.078, Rel-4, CR#293, Vodafone, Type:  CR, Title: Handling of second SIFOC

Discussion :

Conclusion : Revised to 406

N2-010406: 23.078, CR#293, Vodafone, Type:  CR, Title: Handling of second SIFOC

Discussion :

Conclusion :Approved

N2-010405:  23.018, R99, Vodafone, Type:CR, Title: Handling of second SIFOC

Discussion :Semicolumn missing, we set the variable.Summary of change has to be improved (second SIFOC shall be sent).

Conclusion: revised to 419

N2-010419: 23.018, R99, Vodafone, Type:CR, Title: Handling of second SIFOC

Discussion :

Conclusion: Endorced without presentation

N2-010407: 23.018, Rel-4, Vodafone, Type:CR, Title: Handling of second SIFOC

Discussion: Summary of change will be imroved in CN4 document.

Conclusion: Endorsed by CN2

N2-010403: Lucent, Type: presentation, Title: VLR Interactions in 23.018 and 23.078

Discussion : This presentation provides a summary of how processes and procedures interact in 23.018 and 23.078 for the proper handling of all CAMEL interactions (for O-CSI, D-CSI and N-CSI) and call barring checks.

Conclusion: Revised to 423

N2-010423: Lucent, Type: presentation, Title: Presentation for discussion of VLR and MSC interactions for CAMEL subscription information.

Discussion :

Conclusion: Noted

N2-010321 : 29.078, R99,CR#159, Ericsson, Type: CR, Title: Clarification on the usage of SII2 parameter in CAP

Discussion : The data type definition of the parameter “ServiceInteractionIndicatorsTwo” (SII2) lacks a clear description in which CAP operations the sub-parameters of SII2 may be included.
CR proposes corrective text that clarifies when these sub-parameters may be included. This text is in alignment with the functional description of the SII2 parameter in 3G TS 23.078. CR adds corrective and clarifying text to the “ServiceInteractionIndicatorsTwo” data type definition in section 5.1.
Rel-4 CR is needed.

Conclusion : Revised to 408

N2-010408: 29.078, R99,CR#159, Ericsson, Type: CR, Title: Clarification on the usage of SII2 parameter in CAP

Discussion :

Conclusion : Approved without presentation

N2-010409 : 29.078, CR#178, Rel-4, Ericsson, Type:CR, Title: Clarification on the usage of SII2 parameter in CAP

Discussion : Rel-4 corresponding CR to previous document. CR number allocated during the meeting, CR178.

Conclusion: Approved without presentation

N2-010343 : 29.078, R99,CR#172, Alcatel, Type: CR, Title: Alignement the 29.078 on the 23.078

Discussion :The 2 specifications 3GPP TS 23.078 and 3GPP TS 29.078 are in line on certain points and that may induce some misunderstandings.

Changes to chapter 5.1 are canceled. Remove “essential” from the cover page. Summary of change has to be updated.

Conclusion : revised to 410

N2-010410 : 29.078, R99,CR#172, Alcatel, Type: CR, Title: Alignement the 29.078 on the 23.078

Discussion:

Conclustion: Approved withou presentation

N2-010411 :   29.078, Rel-4, CR179, Title: Alignement the 29.078 on the 23.078

Discussion: CR179 allocated during the meeting. Rel-5 stage 3 is not modified. New Rel-5 CR will be created.

Conclusion: Approved without presentation

N2-010344 : 23.078, R99,CR#295, Alcatel, Type: CR, Title: Correction on the call-diversion-Treatment-Indicator at the GMSC

Discussion : This document is intervention.  CCBS case has to be checked. In reason for change and in “consequences if not approved”, gsmSSF should be replaced with gsmSCF.

Conclusion : Revised to 412

N2-010412: 23.078, R99,CR#295, Alcatel, Type: CR, Title: Correction on the call-diversion-Treatment-Indicator at the GMSC

Discussion:

Conclusion: Approved without presentation

N2-010413 : 23.78, Rel-4, CR299, Alcatel, Type: CR, Title: Correction on the call-diversion-Treatment-Indicator at the GMSC

Discussion : This is corresponding Rel-4 CR to previous document, CR 299 is allocated during the meeting.

Conclusion: Approved without presentation

N2-010322 : 29.078, R99,CR#160, Ericsson, Type: CR, Title: Correction to state transition for Assisting gsmSSF

Discussion : Marked to essential correction. Rel-4 CR needed.

Conclusion : Revised to 414

N2-010414: 29.078, R99,CR#160, Ericsson, Type: CR, Title: Correction to state transition for Assisting gsmSSF

Discussion:

Conclusion: Approved without presentation

N2-010415: 29.078, Rel-4,CR#180, Ericsson, Type: CR, Title: Correction to state transition for Assisting gsmSSF

Discussion: This is Rel-4 corresponding CR to previous document . CR 180 allocated during the meeting.

Conclusion: approved without presentation

# 7	CAMEL for Release 4

## 7.1	General and miscellaneous Rel-4 issues

## CAP over IP

No contributions received.

# 8	CAMEL4, Release 5

## CAMEL 4 / Stage 1

No contributions received.

## 8.2			Miscellaneous CAMEL 4 issues

N2-010294 : 23.078, Rel-5, Raporteur, Type: TS-INFO, Title: Draft 23.078 V5D.6.0

Discussion : This is the draft 23.078 V5d.7.0 as the output of the CPH adhoc meeting. This is the basis for the further development in CAMEL Phase 4 Release 5. MCC will make available this document in the drafts folder under CN2.

Conclusion :.  noted

N2-010310 : 23.018 Rel-5, Vodafone, Type:  CR, Title: Introduction of CAMEL phase 4

Discussion : This doucument incorporates CRs that are agreed on previous meetings and will be sent to CN4.

Conclusion : Noted

N2-010311 : 23.083, Rel-5, Vodafone, Type: CR , Title: Introduction of CAMEL phase 4

Discussion : Editorial mistake in the word Phase , but it will be corrected in the next version.

Conclusion :Noted

## Interactions with Optimal Routing

N2-010312 :  23.078, Rel-5, Vodafone , Type:  CR,  Title: Corrections for CAMEL support of OR

Discussion :. Treatment of the BOR requested IE in an entity which does not support BOR is defined.

The BOR requested IE can be included in the Connect or Continue with Argument IF for the MF and VT cases.

IE Basic OR interrogation requested  is trigger to entity that receivs it.

Call in GSM network can be subject of late call forwarding.  In that case OR stage 1 allows that forwarding leg can be treathed in the same way as originating call leg.

BOR requested should have “–“  in the VT column.

Parameter that controls GMSC Basic OR interrogation requested  is not applicable to GMSC according to last sentence on the page 2. To make it clear, in the last sentence it will be changed instead of GMSC only to  “GMSC of the served subscriber”. New proposed wording will be provided.

LS statement to SA1 will be submitted. MT column stays as it is. Stage 2 CR will be drafted. If LS is accepted by SA1,  further improvement will be done.

Conclusion : Revised to 416, based on current stage1 requirement for OR

N2-010416: 23.078, Rel-5, Vodafone , Type:  CR,  Title: Corrections for CAMEL support of OR

Discussion :.Wrong document is inside.

Conclusion :Revised to 439

N2-010439:  23.078, Rel-5, Vodafone , Type:  CR,  Title: Corrections for CAMEL support of OR

Discussion : Summary of change does not reflect actual change, but does not cause problems.

Conclusion : Approved

N2-010417:  LS OUT,Source: Vodafone,  Title:Liaison Statement on Optimal Routeing of a forwarded call

Discussion :. New sentence will be introduced indicating CN2 preference.

Conclusion : Revised to 465

N2-010465:  LS OUT,Source: Vodafone,  Title:Liaison Statement on Optimal Routeing of a forwarded call

Discussion :Reivised 417.

Conclusion : Approved without presentation

## 8.4	Call Party Handling

N2-010326 : 23.078, Rel-5, Alcatel, Type:  DISC, Title: Charging and Information concepts

Discussion :  This contribution discusses the various possibilities for charging and reporting in relation to CAMEL Phase 4. Especially the impact of CPH has been considered.

Call Party Handling Charging is based on per leg and separate charging for announcement is charging on per SRF leg.

SA1 should be informed about the decission that has been made regarding this document.  Final decision has to be done by SA1 (Sumio).

Alcatel proposal is overwriting of tarriff switch and e-parameters. The lower level check  must exist. Alcatel proposal is one FCI per leg as well as one CIR per leg, as in CAMEL Phases 2 and 3.

Basic principles are agreed and will be presented to SA1 in Tdoc 418 which is allocated for output liason statement.

Conclusion :Noted

N2-010418   LS OUT, Alcatel, Proposed LS “Charging and Information concepts for CAMEL Call Party Handling”

Discussion: From SA1 is expected to specify charging requirements for CAMEL Call Party Handling as soon as possible (22.078). These requirements should be enhanced existing requirements.  Wording emprovements are necessary.

Conclusion :Revised to 468

N2-010468   LS OUT, Alcatel, Proposed LS “Charging and Information concepts for CAMEL Call Party Handling”

Discussion: Stage 1 does not say anything about CPH charging.

Conclusion : Approved without presentation and  will be sent directly to SA1 by MCC

N2-010313 :  Vodafone, Type:  DISC, Title: CPH Open Issues

Discussion :  This document will be updated for the next meeting based on individual CRs. When decision is checked, LS statement will be sent to SA1.

Conclusion : Revised to 422

N2-010422 :  Vodafone, Type:  DISC, Title: CPH Open Issues

Discussion :  Decisions will not be sent to SA1.

Conclusion : Revised to 469

N2-010469 :  Vodafone, Type:  DISC, Title: CPH Open Issues

Discussion :  This document will be provided by e-mail for discussion.

Conclusion : Noted

N2-010349 : 23.018, Rel-5, Vodafone, Type:  CR, Title: Handling of reconnect after leg2 disconnects (MO case)

Discussion : It has been defined that when a basic call is answered, if a CAMEL4 control relationship exists, the handling of the legs will be seperated into 2 MSC processes, specified within 23.078. However, the SDLs do not cover the scenario where leg2 disconnects and the gsmSCF requests a reconnect.

Due to the changes in N2-010314, the Release Transaction is not sent to the BSS in the CAMEL_MO_Dialled_Services and CAMEL_OCH_MSC_ALERTING procedures. Hence, OG_Call_Setup_MSC procedure is remodelled to send the release.

Conclusion :Approved

N2-010314 : 23.078, Rel-5, Vodafone, Type:  CR, Title: Handling of reconnect after leg 2 disconnects

Discussion : Why page 3 sets Result:=Fail? There are various comments to this document .

Conclusion :Revised to 420

N2-010420 : 23.078, Rel-5, Vodafone, Type:  CR, Title: Handling of reconnect after leg 2 disconnects

Discussion : This document can be reopened in case of problems.

Conclusion :Approved

N2-010325 : 23.078, Rel-5, Alcatel, Type:  CR, Title: Correction of Call Release

Discussion : Int_Release_Call shall be sent to MSC for the remaining leg and  Int_Continue shall be sent to MSC to the leg that should be released.

On page 4, signal direction seems to be wrong, MSC signals are to/from left.  On page 4, decision box wording shall be improved according to Nick’s comment.

Conclusion :Revised to 421

N2-010421: 23.078, Rel-5, Alcatel, Type:  CR, Title: Correction of Call Release

Discussion :

Conclusion :Approved without presentation

N2-010315 : 23.078, Rel-5, Vodafone, Type:  CR, Title: Correction to procedure CAMEL_EXPORT_LEG_MSC

Discussion : Christian proposes that event (alerting/release) would not be considered during “move”, but is saved instead. According to Vesa (Nokia), Cancel is not needed during move. Returning the situation would be very complicated.

Cancel is removed.

Conclusion :Revised to 431

N2-010431 : 23.078, Rel-5, Vodafone, Type:  CR, Title: Correction to procedure CAMEL_EXPORT_LEG_MSC

Discussion :

Conclusion :Approved without presentation

N2-010316 : 23.078, Rel-5, Vodafone, Type:  CR, Title: Addition of NC & NP columns to IF tables

Discussion :  NC and NP columns have been added where appropriate. IFs that are independent of the call-type have had the MO/MF/MT/VT columns replaced by a Status column.

For creation NP column: triggering can happen for D-CSI and N-CSI. For NC column: triggering shall be based on N-CSI. New proposal for this document will be done and discussed.

Sumio: Document shall be accepted except Initial DP that should be marked with *. NP column should have “-“ for the  Backward Service Interaction Indicator in Connect message. Information Elements Audible Indicator and Play Burstlist in Apply charging message are applicable also for NP.

Conclusion :Revised to 424

N2-010424: 23.078, Rel-5, Vodafone, Type:  CR, Title: Addition of NC & NP columns to IF tables

Discussion :

Conclusion: Approved without presentation

N2-010317 : 29.078, Rel-5, Vodafone, Type:  CR, Title:  Introduction of CPH operations (ASN.1)

Discussion :  It will be incorporated in draft specification.

Conclusion :Approved

N2-010324 : 23.078, Rel-5, Alcatel, Type:  CR, Title: Correction of gsmSCF initiated new calls:CAMEL_ICA_MSC process

Discussion :  Last page: Abort is replaced with Int_exception .

Conclusion :Revised to 432

N2-010432 : 23.078, Rel-5, Alcatel, Type:  CR, Title: Correction of gsmSCF initiated new calls:CAMEL_ICA_MSC process

Discussion :

Conclusion : Approved

## DTMF Mid call procedure for MO and MT calls

No contributions received.

## 8.6	Provisioning of  IP-based multimedia services / CAMEL applicability to media strems like VoIP

No contributions received

## 8.7	CAMEL control over MT SMS

N2-010345 : 23.078, Rel-5, Ericsson, Type: CR, Title: Introduction of Reference Number for MT-SMS

Discussion :  The document proposes the introduction of Reference number for SMS. It is mandatory parameter, because MSC is no dependend on receiving it from other entity. Call reference number and SMS reference number are indipendent, and MSC alocates them indipendendly. There is no relation between SMS MT reference number and SMS MO reference number.

GGSN address allocateds charging ID, and if we combine two of them we have unique pair in the network.

Rogier does not support a task box for reference allocation.  GPRS: does it need a reference? There is GGSN address and Charging ID.

Conclusion : Revised to 433

N2-010433 : 23.078, Rel-5, Ericsson, Type: CR, Title: Introduction of Reference Number for MT-SMS

Discussion :  Task box will be introduced and should be documented that there is no reference beween Call reference number and SMS reference number.

Conclusion: conditionally approved, if R99 CRs (Introduction of Reference Number for  MO-SM)S is approved on the Plenary

N2-010346: 29.078, Rel-5, Ericsson, Type: CR, Title: Introduction of Reference Number for MT-SMS

Discussion :  Call reference number is used as data type definition and there is no corelation between it and MO-SMS reference number. There is no relation between  contacinated SMSs, so reference numbers are provided to single SMS process. If there is set of SMSs, every SMS has process within MSC  and Ref number should be produced for each single SMS as well as 1 call data record per SMS. According 32.015 specification SGSN should generate CDR for each single SMS. Corrections to ASN1 shall be introduced.

Conclusion :Revisedto 434

N2-010434: 29.078, Rel-5, Ericsson, Type: CR, Title: Introduction of Reference Number for MT-SMS

Discussion :

Conclusion: Conditionaly approved

N2-010347 : 23.078, Rel-5,  Ericsson, Type:  CR, Title: Correction to MT-SMS Trigger Criteria

Discussion :  The present CR proposes improvements to the text and SDL of MT-SMS to clarify the handling of MT-SMS trigger criteria. Criteria should be replaced by criterion.

Conclusion :revised to 435

N2-010435 : 23.078, Rel-5,  Ericsson, Type:  CR, Title: Correction to MT-SMS Trigger Criteria

Discussion :

Conclusion: Approved without presentation

N2-010348 : 29.002, Rel-5,  Ericsson, Type:  CR, Title: Correction to MT-SMS Trigger Criteria

Discussion :  The structure is the same as originally by Siemens. ASN1 should be corrected.

Conclusion :revised to 436

N2-010436 : 29.002, Rel-5,  Ericsson, Type:  CR, Title: Correction to MT-SMS Trigger Criteria

Discussion :

Conclusion :Approved without presentation

N2-010358 : 23.060, Rel-5,  Ericsson, Type:  CR, Title: Introduction of MT-SMS interworking

Discussion :  CR proposes the required changes to 23.060 to specify the interworking in the SGSN for CAMEL control of MT-SMS. Once the MS has accepted SM it will report it to SGSN. Entered boxes C1 and C2 are CAMEL procedures defined in 23.078.

This CR is aplicable to Rel-5 only.

Conclusion :Revised to 438

N2-010438 : 23.060, Rel-5,  Ericsson, Type:  CR, Title: Introduction of MT-SMS interworking

Discussion :  CR will be sent to SA2

Conclusion: Endorced

N2-010359 :Rel-5, LS from CN2 to SA5: Inclusion of CAMEL elements in MT-SMS CDR

Discussion : TSG CN WG2 asks TSG_SA WG5 group to include  for CAMEL purposes the following information elements in the MT-SMS record for the terminating MSC and in the MT-SMS record for the SGSN:

gsmSCF Address,
service Key,
default SMS Handling,
free Format Data,
Calling Party Number,
SMS Reference Number,
MSC Address (for MT-SMS record for the terminating MSC only),
SGSN Address (for MT-SMS record for the SGSN).

Calling Party Number ise related to  CAMEL. MT SMS Reference number, MSC Address  and SGSN Address are removed from this liason statement.

Conclusion :Revised to 440

N2-010440 :Rel-5, LS from CN2 to SA5: Inclusion of CAMEL elements in MT-SMS CDR

Conclusion :Approved without presentation

## Inclusion of flexibel tone injection

No contributions received.

## 8.9	Charging notification to CSE

N2-010350 : 23.078, Rel-5,  C-DOT, Type:  disc, Title: Definition of eventTypeCharging parameter in RNC & ENC operations

Discussion :

Conclusion :Revised to 425

N2-010425 : 23.078, Rel-5,  C-DOT, Type:  disc, Title: Definition of eventTypeCharging parameter in RNC & ENC operations

Discussion :  Alcatel proposes to use AC/ACR to report also charging units. AC/ACR can be used only if the tariff is known by the SCP.

ENC/RNC: SCP originated charging. How is it reported? MSC should report always its own charging parameters, not the ones given by SCP.

Vesa: What is the access network charge? This is the transit network charge

If dialled services give charging, is it reported for the O-CSI? Only one service should be allowed to modify these charging parameters.AC and RNC are mutually exclussive. SCP must know whether charging is configured. This would be part of a roaming agreement beween operators.

Rejeev: If we have AC and ACR on O-CSI, we can not have the same information on D-CSI.

C-DOT believes that this should be an optional CAMEL4 feature. MSC should indicate to the SCP whether the optional feature is supported. When SCP receives the information about charging , SCP also receives the information till when this charges will be applicable.

T-Mobil: Tarrif is not known by the MSC. There would be no possibility to apply HPLMN tarrif. SCP can deduce the credit based on VPLMN tariff or independently. Currently credit is chedked at IDP.

Conclusion : Noted

N2-010351 : 23.078, Rel-5,  C-DOT, Type:  CR, Title: Handling of RNC & ENC operations in gsmSSF

Discussion :

Conclusion :Revised to 426

N2-010426 : 23.078, Rel-5,  C-DOT, Type:  CR, Title: Handling of RNC & ENC operations in gsmSSF

Discussion :  There are separate states for dialled services and those are not listed in this CR. If there is announcement then charging notification is not running. In section 4.5.7.x “end of connection”  should be “end of call”. Procedure Handle RNC should be covered in SDL (23.078).  NP and NC columns are not described yet

e3 takes care of conversion from local unit to total unit. C-DOT says that  Price per unit (PPU) should be part of roaming agreement. SCP does not know the MSCs PPU. MSC must already be able to calculate PPU. AoC has problem but the feature is not used by operators.

SCP is responsible to calculate price out of the evalues based on call duration. SSP has to deliver enough information to SCP in order to make calculation. In the MSC, e3 has to be configured for each HPLMN. If the roaming subscriber makes the call e3 values are retrieved from the MSC. For home subscribers e1 is used for price calculation.

Stephen: e-parameter ranges are not sufficient to cover all the services used nowdays.  We should take into consideration roaming agreements and GSM Association opinion. The concept may not fit to current charging concepts.

If we support charging units concept, unit has to be enhanced . We should  indicate a real charge from the information received from MSC.  If we want MSC to deliver valid values, then evalues are not enough for it. Price per unit should be introduced. More applicable information should be available.

Rajeev: These parameters are taken as an optional feature.

CN2 will proceede on this feature until there is a requirement.

Conclusion :Revised to 455

N2-010455: 23.078, Rel-5,  C-DOT, Type:  CR, Title: Handling of RNC & ENC operations in gsmSSF

Conclusion :Revised to 470

N2-010470: 23.078, Rel-5,  C-DOT, Type:  CR, Title: Handling of RNC & ENC operations in gsmSSF

Discussion :

Conclusion :Approved without presentation

N2-010352 : 29.078, Rel-5,  C-DOT, Type:  CR, Title: Introduction of RNC & ENC operations , procedures & ASN definitions

Discussion :

Conclusion :Revised to 427

N2-010427 : 29.078, Rel-5,  C-DOT, Type:  CR, Title: Introduction of RNC & ENC operations , procedures & ASN definitions

Discussion :  SMS and GPRS specific part shall not be modified.Comments are considered, revised document will be provided for the next meeting

Conclusion :Noted

## 8.10	Enhancements of dialled services

N2-010354 : 23.078, Rel-5, C-DOT, Type:  CR, Title: Creation of Control/Monitoring relationship with CSE at DP3

Discussion :

Conclusion :Revised to 429

N2-010429 : 23.078, Rel-5, C-DOT, Type:  CR, Title: Creation of Control/Monitoring relationship with CSE at DP3

Discussion :   The term CSE has to be replaced by SCP. The new IDP parameter could be also in the MF case. DP3 SSF special state is used if  dialogue already exists.

This was late document . Revised CR will be prepared for the next N2 meeting.

Conclusion : Noted

N2-010353 : 23.018, Rel-5,  C-DOT, Type:  CR, Title: Handling of a variable to indicate an existing relationship with CSE

Discussion :

Conclusion :Revised to 428

N2-010428 : 23.018, Rel-5,  C-DOT, Type:  CR, Title: Handling of a variable to indicate an existing relationship with CSE

Discussion :   This was late document . Revised CR will be prepared for the next N2 meeting.

Discussion :

Conclusion : Noted

N2-010355 : 29.078, Rel-5, C-DOT, Type:  CR, Title: InitialDP modified to indicate existance of relationship with CSE

Discussion :

Conclusion :Revised to 430

N2-010430 : 29.078, Rel-5, C-DOT, Type:  CR, Title: InitialDP modified to indicate existance of relationship with CSE

Discussion :   This was late document . Revised CR will be prepared for the next N2 meeting.

Conclusion : Noted

N2-010376: Rel-5, Vodafone, Type: Disc, Title: Implementation of enhancements to subscriber dialled services

Discussion :   The  invoke flag message should have the flag already, not in the DP related message. The flag needs to be updated whenever the dialoque is terminated.

This was late document . Revised CR will be prepared for the next N2 meeting.

Conclusion :Noted

N2-010451:  23.018, Rel-5, Vodafone, Type:CR, Title:Enchancements to Subscribed Dialled Services

Discussion :  The introduction of Enhancements to Subscribed Dialled Services requires the initialisation of a variable in 23.018 processes. Change proposes initialisation of CAP_Dialogue (:= False) in OG_Call_Setup_MSC and MT_CF_MSC.

Late document, revised version will be presented on the next meeting.

Conclusion :Noted

N2-010452:  23.078, Rel-5, Vodafone, Type: CR, Title: Enhancements to Subscribed Dialled Services

Discussion :  Late document, revised version will be presented on the next meeting.

Conclusion :Noted

## 8.11	Provision of location information of called subscriber

N2-010303 : 23.078, Rel-5,  Siemens, Type:  CR, Title : Providing the location information during ongoing call

Discussion :   Every time MS change the location, this has to be reported to SCP.

The following changes are proposed in this CR;

-	DP Change_Of_Position added to O/T_BCSM in the alerting phase the active phases.

-	Implicit disarming of the DP is only done when the call is released.

-	New procedure, CAMEL_Change_Of_Position, added.

-	Process gsmSSF; RRB and ERB for the DP added.

-     Information flow; RRB and ERB for the DP added.

These new DPs apply only to MO and MT calls. When HO notification is done towards SCP, evalues should be descarded and tarriff switch should be stopped.

Alcatel thinks that in the future we will have to much DPs and would like to have midcall DP, Siemens and Nokia would like separate DPs. Disarming tables 4.4  and 4.5 have to be revised.

Comments to to this CR are considered and new CR will be provided for the next meeting.

Conclusion :Noted

N2-010304 : 29.078, Rel-5,  Siemens, Type:  CR, Title: Providing the location information during ongoing call

Discussion :

Conclusion :Postponed

## 8.12	Notification of GPRS mobility management to CSE

N2-010297 : 23.008, Rel-5,  Siemens, Type:  CR, Title: Mobility management for GPRS subscriber

Discussion :

Conclusion :Postponed

N2-010298 : 23.016, Rel-5,  Siemens, Type:  CR, Title:  Mobility management for GPRS subscriber

Discussion :

Conclusion :Postponed

N2-010299 : 23.060, Rel-5,  Siemens, Type:  CR, Title:  Mobility management for GPRS subscriber

Discussion :

Conclusion :Postponed

N2-010300 : 23.078, Rel-5,  Siemens, Type:  CR, Title : Mobility management for GPRS subscriber (chapter 9)

Discussion :   Mobility management triggers should contain also network initiated GPRS detach, not only MS initiated GPRS detach. Procedure names are not maching with a names in other CR where the procedure is called. Procedure names have to be checked. Section 9.3 has to be revised, it may not cover all PS related cases.

Last section: Insert Subscriber Data contains  CAMEL specific IE for Mobility Management.M-CSI is sent to VLR only and MG-CSI is sent to SGSN only and they are placed in the same table. Ericsson recommends separate sections.

Comments are considered and will be part of the contribution for the next meeting.

Conclusion :Noted

N2-010301 : 23.078, Rel-5,  Siemens, Type:  CR, Title: Mobility management for GPRS subscriber (chapter 10)

Discussion :

Conclusion :Postponed

N2-010302 : 29.002, Rel-5,  Siemens, Type:  CR, Title: Mobility management for GPRS subscriber

Discussion :

Conclusion :Postponed

## CAMEL4/ ODB in HLR-SCP interface

N2-010305 : 23.078, Rel-5,  Siemens, Type:  CR, Title: Inclusion of ODB data in ATM

Discussion :

Conclusion :Postponed

N2-010306 : 29.002, Rel-5,  Siemens, Type:  CR, Title: Inclusion of ODB data in ATM

Discussion :

Conclusion :Postponed

# 9	Maintenance of earlier CAMEL phases

## 9.1				CAMEL phase 1

No contributions received.

## 9.2				CAMEL phase 2

N2-010285 : 03.78, R97, CR#A161,  Nokia, Type:  CR, Title: Mapping of Call Forwarding  parameters form CAP-Connect to ISUP-IAM and CAP-InitialDP

Discussion: The Redirecting Number and Redirection Information parameters are mandatory parameters in a CF O-BCSM (MF column), but they are not available in all cases. If the SCP sends a CAP-Connect operation to a T-BCSM without these parameters, and these parameters were not received from ISUP, then the MSC/SSP shall not send these parameters. It is already stated that non-present Connect parameters are not modified by the MSC.

CAMEL2 shall have a word of warning. CAMEL3 onwards the parameters shall be conditional. The version shall be 6.8.0. The word parameters shall be singular. Correction to cover page needed.

Conclusion :Revised to 379

N2-010379: 03.78, R97, CR#A161,  Nokia, Type:  CR, Title: Mapping of Call Forwarding  parameters form CAP-Connect to ISUP-IAM and CAP-InitialDP

Discussionn:

Conclusion :Approved without presentation

N2-010286 : 03.78, R98, CR#A162, Nokia, Type:  CR, Title: Mapping of Call Forwarding  parameters form CAP-Connect to ISUP-IAM and CAP-InitialDP

Discussion :   Same changes as in R97 CR are needed. Category is marked as A.

Conclusion :Revised to 380

N2-010380 : 03.78, R98, CR#A162, Nokia, Type:  CR, Title: Mapping of Call Forwarding  parameters form CAP-Connect to ISUP-IAM and CAP-InitialDP

Discussion :

Conclusion :Approved without presentation

N2-010287: 23.078, R99, CR#288, Nokia, Type:  CR, Title: Mapping of Call Forwarding  parameters form CAP-Connect to ISUP-IAM and CAP-InitialDP

Discussion :   The Redirecting Number and Redirection Information parameters are mandatory parameters in a CF O-BCSM (MF column). However, they are not available in all cases. If the SCP sends a CAP-Connect operation to a T-BCSM without these parameters, and these parameters were not received from ISUP, then the MSC/SSP shall not send these parameters. It is already stated that non-present Connect parameters are not modified by the MSC.

Redirecting Party ID and Redirection Information are set to Conditional.

WI should be CAMEL 3 and category A.

Conclusion :revised to 381

N2-010381: 23.078, R99, CR#288, Nokia, Type:  CR, Title: Mapping of Call Forwarding  parameters form CAP-Connect to ISUP-IAM and CAP-InitialDP .

Discussion :

Conclusion :Approved without presentation

N2-010288 : 23.078, Rel-4, CR#289, Nokia, Type:  CR, Title: Mapping of Call Forwarding  parameters form CAP-Connect to ISUP-IAM and CAP-InitialDP

Discussion :   Category is A and WI CAMEL3.

Conclusion :Revised to 382.

N2-010382: 23.078, Rel-4, CR#289, Nokia, Type:  CR, Title: Mapping of Call Forwarding  parameters form CAP-Connect to ISUP-IAM and CAP-InitialDP

Discussion :

Conclusion :Approved without presentation

N2-010289 : 23.078, Rel-5,  Nokia, Type:  CR, Title: Mapping of Call Forwarding  parameters form CAP-Connect to ISUP-IAM and CAP-InitialDP

Discussion :   Sumio prefers “C” without explanation, WI is CAMEL3.

Conclusion :Revised to 383

N2-010383 : 23.078, Rel-5,  Nokia, Type:  CR, Title: Mapping of Call Forwarding  parameters form CAP-Connect to ISUP-IAM and CAP-InitialDP

Discussion :

Conclusion :Approved without presentation

# 10			Review of dates and hosts for future meetings

N2-010281 :  MCC, Title: CN2 year 2001 meeting calendar

Discussion :   During next meeting will be joint meeting on Wednesday. For the next meeting the deadline for request sheets will be 4th of July,Wednesday midday central european time. Tdocs must be sent out during the Wednesday. CN2#21 will be in Mexico, Cancun. Meeting locations should be covered by GSM network

Conclusion :Noted

# 11	Closing of the meeting (15:30 Friday)

Annex A 				Participants list

Member of 3GPP (ETSI)

Ms. Véronique Belfort	ALCATEL S.A.	3GPPMEMBER (ETSI)	FR	+33 1 30 77 86 11	veronique.belfort@alcatel.fr

Miss Archna Gandhi	C-DOT	3GPPMEMBER (ETSI)	IN	+91-11-4678974	archna@cdotd.ernet.in

Mr. Michel Grech	Lucent Technologies N. S. UK	3GPPMEMBER (ETSI)	GB	+44 1793 736 110	grech@lucent.com

Miss Shivali Gupta	C-DOT	3GPPMEMBER (ETSI)	IN	+91-11-4678974	shivali@cdotd.ernet.in

Mr. Steffen Habermann	Deutsche Telekom MobilNet	3GPPMEMBER (ETSI)	DE	+49 228 936 3324	steffen.habermann@t-mobil.de

Mr. Christian Homann	ALCATEL S.A.	3GPPMEMBER (ETSI)	DE	+49 711 821 45632	c.homann@alcatel.de

Ms. Jane D Humphrey	MARCONI COMMUNICATIONS	3GPPMEMBER (ETSI)	GB	+44 1202 853757	jane.humphrey@marconi.com

Mr. Andrew McClurg	Lucent Technologies	3GPPMEMBER (ETSI)	NL	+1 630 979 7357	amcclurg@lucent.com

Mr. Sumio Miyagawa	SIEMENS AG	3GPPMEMBER (ETSI)	AT	+43 51707 21381	sumio.miyagawa@siemens.at

Mr. Keijo Palviainen	NOKIA Corporation	3GPPMEMBER (ETSI)	FI	+358 9 511 69669	keijo.palviainen@nokia.com

Mr. Nick Russell	VODAFONE Group Plc	3GPPMEMBER (ETSI)	GB	+44 1635 682 699	nick.russell@vf.vodafone.co.uk

Mr. Vesa Tiainen	NOKIA Corporation	3GPPMEMBER (ETSI)	FI	+358 95116 9712	vesa.tiainen@nokia.com

Mr. Rogier Noldus	ERICSSON L.M.	3GPPMEMBER (ETSI)	NL	+31 161 249 400	rogier.noldus@eln.ericsson.se

Mr. Rajeev Singh	C-DOT	3GPPMEMBER (ETSI)	IN	+91 11 4678974	rajeev@cdotd.ernet.in

Member of 3GPP (TTC)

Mr. Yutaka Harada	NEC Corporation	3GPPMEMBER (TTC)	JP	+81 3 3798 5837	yharada@mt.ncos.nec.co.jp

Organisation partner representative (ETSI)

Mrs. Andrijana Jurisic	Mobile Competence Center	HR	+385 1 4691 430	a.jurisic@vipnet.hr

Annex B 			Output Documents

## Approved Change Requests for CAMEL Phase 2

| TDoc # | WI | Rel | Cat | Title | Type | Spec | CR # | Rev | Version | Conclusion |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| N2-010379 | CAMEL2 | R97 | F | Mapping of Call Forwarding parameters from CAP-Connect to ISUP-IAM and CAP-InitialDP | CR | 03.78 | A161 | 1 | 6.8.0 | approved |
| N2-010380 | CAMEL2 | R98 | A | Mapping of Call Forwarding parameters from CAP-Connect to ISUP-IAM and CAP-InitialDP | CR | 03.78 | A162 | 1 | 7.5.0 | approved |

## Agreed Change Requests for CAMEL Phase 3

| TDoc # | WI | Rel | Cat | Title | Type | Spec | CR # | Rev | Version | Conclusion | Source |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| N2-010284 | CAMEL3 | Rel-5 | A | GGSN address in SGSN to SCP interface | CR | 23.078 |  |  | 5d.7.0 | approved | Nokia |
| N2-010383 | CAMEL3 | Rel-5 | A | Mapping of Call Forwarding parameters from CAP-Connect to ISUP-IAM and CAP-InitialDP | CR | 23.078 |  |  | 5d.7.0 | approved | Nokia |
| N2-010282 | CAMEL3 | R99 | F | GGSN address in SGSN to SCP interface | CR | 23.078 | 286 | 0 | 3.8.0 | approved | Nokia |
| N2-010283 | CAMEL3 | Rel-4 | A | GGSN address in SGSN to SCP interface | CR | 23.078 | 287 | 0 | 4.0.0 | approved | Nokia |
| N2-010381 | CAMEL3 | R99 | F | Mapping of Call Forwarding parameters from CAP-Connect to ISUP-IAM and CAP-InitialDP | CR | 23.078 | 288 | 1 | 3.8.0 | approved | Nokia |
| N2-010382 | CAMEL3 | Rel-4 | A | Mapping of Call Forwarding parameters from CAP-Connect to ISUP-IAM and CAP-InitialDP | CR | 23.078 | 289 | 1 | 4.0.0 | approved | Nokia |
| N2-010290 | CAMEL3 | R99 | F | Correction of error implementing CR 23.078-181r2 | CR | 23.078 | 290 |  | 3.8.0 | approved | Rapporteur |
| N2-010291 | CAMEL3 | Rel-4 | A | Correction of error implementing CR 23.078-181r2 | CR | 23.078 | 291 |  | 4.0.0 | approved | Rapporteur |
| N2-010404 | CAMEL3 | R99 | F | Handling of second SIFOC | CR | 23.078 | 292 | 1 | 3.8.0 | approved | Vodafone |
| N2-010406 | CAMEL3 | Rel-4 | A | Handling of second SIFOC | CR | 23.078 | 293 | 1 | 4.0.0 | approved | Vodafone |
| N2-010389 | CAMEL3 | R99 | F | Correction to GPRS SDL: no state transition for QoS-induced ACR-GPRS | CR | 23.078 | 294 | 1 | 3.8.0 | approved | Ericsson |
| N2-010412 | CAMEL3 | R99 | F | Correction on the call-Diversion-Treatment-Indicator at the GMSC | CR | 23.078 | 295 | 1 | 3.8.0 | approved | Alcatel |
| N2-010444 | CAMEL3 | R99 | F | Introduction of Reference Number for MO-SMS | CR | 23.078 | 296 | 3 | 3.8.0 | approved | Ericsson |
| N2-010390 | CAMEL3 | Rel-4 | A | Correction to GPRS SDL: no state transition for QoS-induced ACR-GPRS | CR | 23.078 | 297 |  | 4.0.0 | approved | Ericsson |
| N2-010459 | CAMEL3 | R99 | F | Inclusion of warning note for the reporting of total duration or volume for GPRS | CR | 23.078 | 298 | 1 | 3.8.0 | approved | Ericsson |
| N2-010413 | CAMEL3 | Rel-4 | A | Correction on the call-Diversion-Treatment-Indicator at the GMSC | CR | 23.078 | 299 |  | 4.0.0 | approved | Alcatel |
| N2-010445 | CAMEL3 | Rel-4 | A | Introduction of Reference Number for MO-SMS | CR | 23.078 | 300 |  | 4.0.0 | approved | Ericsson |
| N2-010449 | CAMEL3 | R99 | F | CAMEL Capability Handling in GPRS-CSI | CR | 23.078 | 301 |  | 3.8.0 | approved | Vodafone |
| N2-010450 | CAMEL3 | Rel-4 | A | CAMEL Capability Handling in GPRS-CSI | CR | 23.078 | 302 |  | 4.0.0 | approved | Vodafone |
| N2-010460 | CAMEL3 | Rel-4 | A | Inclusion of warning note for the reporting of total duration or volume for GPRS | CR | 23.078 | 303 |  | 4.0.0 | approved | Ericsson |
| N2-010472 | CAMEL3 | R99 | F | Indication of gsmSCF Address in Continue GPRS and Connect GPRS IFs | CR | 23.078 | 304 | 1 | 3.8.0 | approved | Alcatel, T-Mobil, Ericsson |
| N2-010473 | CAMEL3 | Rel-4 | A | Indication of gsmSCF Address in Continue GPRS and Connect GPRS Ifs | CR | 23.078 | 305 |  | 4.0.0 | approved | Alcatel, T-Mobil, Ericsson |
| N2-010466 | CAMEL3 | R99 | F | Contradiction and inconsistency among descriptions on SMS | CR | 29.078 | 155 | 3 | 3.7.0 | approved | Siemens AG |
| N2-010467 | CAMEL3 | Rel-4 | A | Contradiction and inconsistency among descriptions on SMS | CR | 29.078 | 156 | 2 | 4.0.0 | approved | Siemens AG |
| N2-010391 | CAMEL3 | R99 | F | Correction to ACR-GPRS procedure description | CR | 29.078 | 157 | 1 | 3.7.0 | approved | Ericsson |
| N2-010408 | CAMEL3 | R99 | F | Correction on the usage of SII2 parameter in CAP | CR | 29.078 | 159 | 1 | 3.7.0 | approved | Ericsson |
| N2-010414 | CAMEL3 | R99 | F | Correction to state transition for Assisting gsmSSF | CR | 29.078 | 160 | 1 | 3.7.0 | approved | Ericsson |
| N2-010384 | CAMEL3 | R99 | F | Correction to IMPORT statements | CR | 29.078 | 161 | 1 | 3.7.0 | approved | Ericsson |
| N2-010456 | CAMEL3 | R99 | F | ASN.1 syntax correction | CR | 29.078 | 162 | 3 | 3.7.0 | approved | Siemens AG |
| N2-010457 | CAMEL3 | Rel-4 | A | ASN.1 syntax correction | CR | 29.078 | 163 | 3 | 4.0.0 | approved | Siemens AG |
| N2-010441 | CAMEL3 | R99 | F | Correction of the MAXIMUM-FOR-FCI-BILLING-CHARGING value | CR | 29.078 | 164 | 2 | 3.7.0 | approved | Nokia |
| N2-010336 | CAMEL3 | Rel-4 | A | Correction of the MAXIMUM-FOR-FCI-BILLING-CHARGING value | CR | 29.078 | 165 |  | 4.0.0 | approved | Nokia |
| N2-010393 | CAMEL3 | R99 | F | Correction of the gprsSSF error handling | CR | 29.078 | 166 | 1 | 3.7.0 | approved | Nokia |
| N2-010338 | CAMEL3 | Rel-4 | A | Correction of the gprsSSF error handling | CR | 29.078 | 167 |  | 4.0.0 | approved | Nokia |
| N2-010394 | CAMEL3 | R99 | F | Clarification of the TC dialogue termination | CR | 29.078 | 168 | 1 | 3.7.0 | approved | Nokia |
| N2-010395 | CAMEL3 | Rel-4 | A | Clarification of the TC dialogue termination | CR | 29.078 | 169 | 1 | 4.0.0 | approved | Nokia |
| N2-010396 | CAMEL3 | R99 | F | The termination of the dialogue is not clear after ActivityTestGPRS Return Result. | CR | 29.078 | 170 | 1 | 3.7.0 | approved | Nokia |
| N2-010397 | CAMEL3 | Rel-4 | A | The termination of the dialogue is not clear after ActivityTestGPRS Return Result. | CR | 29.078 | 171 | 1 | 4.0.0 | approved | Nokia |
| N2-010410 | CAMEL3 | R99 | F | (rev 343) Alignement the 29.078 on the 23.078 | CR | 29.078 | 172 | 1 | 3.7.0 | approved | Alcatel |
| N2-010442 | CAMEL3 | R99 | F | Setting of End User Address Spare Bits | CR | 29.078 | 174 | 1 | 3.7.0 | approved | Alcatel |
| N2-010447 | CAMEL3 | R99 | F | Introduction of Reference Number for MO-SMS | CR | 29.078 | 175 | 2 | 3.7.0 | approved | Ericsson |
| N2-010385 | CAMEL3 | Rel-4 | A | Correction to IMPORT statements | CR | 29.078 | 176 |  | 4.0.0 | approved | Ericsson |
| N2-010392 | CAMEL3 | Rel-4 | A | Correction to ACR-GPRS procedure description | CR | 29.078 | 177 |  | 4.0.0 | approved | Ericsson |
| N2-010409 | CAMEL3 | Rel-4 | A | Correction on the usage of SII2 parameter in CAP | CR | 29.078 | 178 |  | 4.0.0 | approved | Ericsson |
| N2-010411 | CAMEL3 | Rel-4 | A | Alignement the 29.078 on the 23.078 | CR | 29.078 | 179 |  | 4.0.0 | approved | Alcatel |
| N2-010415 | CAMEL3 | Rel-4 | A | Correction to state transition for Assisting gsmSSF | CR | 29.078 | 180 |  | 4.0.0 | approved | Ericsson |
| N2-010443 | CAMEL3 | Rel-4 | A | Setting of End User Address Spare Bits | CR | 29.078 | 181 |  | 4.0.0 | approved | Alcatel |
| N2-010448 | CAMEL3 | Rel-4 | A | Introduction of Reference Number for MO-SMS | CR | 29.078 | 182 |  | 4.0.0 | approved | Ericsson |
| N2-010474 | CAMEL3 | R99 | F | Indication of gsmSCF Address in Continue GPRS and Connect GPRS Ifs | CR | 29.078 | 183 | 1 | 3.7.0 | approved | Alcatel, T-Mobil |
| N2-010475 | CAMEL3 | Rel-4 | A | Indication of gsmSCF Address in Continue GPRS and Connect GPRS Ifs | CR | 29.078 | 184 |  | 4.0.0 | approved | Alcatel, T-Mobil, Ericsson |

## Documents for e-mail discussion

| N2-010469 | Discussion document | CPH: Open Issues | Vodafone | CAMEL4 | noted (e-mail discussion) |
| --- | --- | --- | --- | --- | --- |

## Documents Endorsed by N2

| TDoc # | WI | Rel | Cat | Title | Type | Spec | CR # | Rev | Version | Conclusion |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| N2-010377 | CAMEL3 | R99 |  | Supported CAMEL Phases in VLR is temporary | CR | 23.008 |  |  |  | endorced |
| N2-010378 | CAMEL3 | Rel-4 |  | Supported CAMEL Phases in VLR is temporary | CR | 23.008 |  |  |  | endorced |
| N2-010407 | CAMEL3 | Rel-4 | F | Initialisation of variable to monitor activations of CSIs | CR | 23.018 |  |  | 3.7.0 | endorced |
| N2-010419 | CAMEL3 | R99 | F | Initialisation of variable to monitor activations of CSIs | CR | 23.018 |  |  | 3.7.0 | endorced |
| N2-010438 | CAMEL4 | Rel-5 | B | Introduction of MT-SMS interworking | CR | 23.060 |  | 1 |  | endorced |

## Approved Output Liaison Statements

| TDoc # | To | Title | Type | Conclusion | Source |
| --- | --- | --- | --- | --- | --- |
| N2-010440 | TSG SA WG5 | LS from CN2 to SA5: Inclusion of CAMEL elements in MT-SMS CDR | LS OUT | approved | Ericsson |
| N2-010446 | TSG SA WG5 | Liaison Statement on introduction of SMS Reference Number for SMS | LS OUT | Conditionally approved | Ericsson |
| N2-010465 | TSG SA WG1 | Output LS to SA1: Corrections for CAMEL support of OR | LS OUT | approved | Vodafone |
| N2-010468 | TSG SA WG1, TSG SA WG1 CAMEL AdHoc | LS “Charging and Information concepts for CAMEL Call Party Handling” | LS OUT | approved | Alcatel |

## Other documents approved by CN2

| TDoc # | Type | Title | Source | WI | Rel | Conclusion |
| --- | --- | --- | --- | --- | --- | --- |
| N2-010371 | WID | CAMEL4 scope in Rel-5 for TSG-CN (WID) | CN2 chairman | CAMEL4 | Rel-5 | approved |
| N2-010471 | Work plan | Progress of CAMEL work, changes to Work plan status | CN2 chairman | CAMEL4 | Rel-5 | approved |

## Agreed and endorced Change Requests for CAMEL Phase 4

| TDoc # | WI | Rel | Cat | Title | Type | Spec | CR # | Rev | Version | Conclusion | Source |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| N2-010349 | CAMEL4 | 5 | F | Handling of reconnect after leg2 disconnects | CR | 23.018 |  | 0 | 4.2.0 | approved | Vodafone Group Plc |
| N2-010470 | CAMEL4 | Rel-5 | B | Handling of RNC & ENC operations in gsmSSF | CR | 23.078 |  | 1 | 5d.7.0 | approved | C-DOT |
| N2-010439 | CAMEL4 | Rel-5 | C | Corrections for CAMEL support of OR | CR | 23.078 |  | 3 | 5D.7.0 | approved | Vodafone Group Plc |
| N2-010435 | CAMEL4 | Rel-5 | F | Correction to MT-SMS Trigger Criteria | CR | 23.078 |  | 1 | 5D.7.0 | approved | Ericsson |
| N2-010433 | CAMEL4 | Rel-5 | B | Introduction of Reference Number for MT-SMS | CR | 23.078 |  | 1 | 5D.7.0 | conditonally approved | Ericsson |
| N2-010432 | CAMEL4 | Rel-5 | F | Correction of gsmSCF initiated new calls: CAMEL_ICA_MSC process | CR | 23.078 |  | 9 | 5D.7.0 | approved | Alcatel |
| N2-010431 | CAMEL4 | Rel-5 | F | Corrections to procedure CAMEL_EXPORT_LEG_MSC | CR | 23.078 |  | 1 | 5D.7.0 | approved | Vodafone Group Plc |
| N2-010424 | CAMEL4 | Rel-5 | C | Addition of NC & NP columns to IF tables | CR | 23.078 |  | 1 | 5D.7.0 | approved | Vodafone Group Plc |
| N2-010421 | CAMEL4 | Rel-5 | F | Correction of Call Release | CR | 23.078 |  | 1 | 5D.7.0 | approved | Alcatel |
| N2-010420 | CAMEL4 | Rel-5 | F | Handling of reconnect after leg 2 disconnects | CR | 23.078 |  | 1 | 5D.7.0 | approved | Vodafone Group Plc |
| N2-010436 | CAMEL4 | Rel-5 | F | Correction to MT-SMS Trigger Criteria | CR | 29.002 |  | 1 | 3.8.0 | approved | Ericsson |
| N2-010434 | CAMEL4 | Rel-5 | B | Introduction of Reference Number for MT-SMS | CR | 29.078 |  | 1 | X.5.1 | conditionally approved | Ericsson |
| N2-010317 | CAMEL4 | Rel-5 | B | Introduction of CPH operations (ASN.1) | CR | 29.078 |  | 2 | d5.1.0 | approved | Vodafone Group Plc |

None Endorced

Annex C 			List of Documents

| TDoc # | Type | Title | Source | WI | CR # | Rev | Cat | Spec | Rel | Version | Conclusion |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| N2-010278 | AGENDA | Agenda | CN2 chairman |  |  |  |  |  |  |  | approved |
| N2-010279 | AGENDA | Allocation of documents to agenda items | CN2 chairman |  |  |  |  |  |  |  | noted |
| N2-010280 | WID | CAMEL4 scope in Rel-5 for TSG-CN (WID) | CN2 chairman | CAMEL4 |  |  |  |  | Rel-5 |  | revised to 371 |
| N2-010281 | CALENDAR | CN2 year 2001 meeting calendar | CN2 chairman |  |  |  |  |  |  |  | noted |
| N2-010282 | CR | GGSN address in SGSN to SCP interface | Nokia | CAMEL3 | 286 | 0 | F | 23.078 | R99 | 3.8.0 | approved |
| N2-010283 | CR | GGSN address in SGSN to SCP interface | Nokia | CAMEL3 | 287 | 0 | A | 23.078 | Rel-4 | 4.0.0 | approved |
| N2-010284 | CR | GGSN address in SGSN to SCP interface | Nokia | CAMEL3 |  |  | A | 23.078 | Rel-5 | 5d.7.0 | approved |
| N2-010285 | CR | Mapping of Call Forwarding parameters from CAP-Connect to ISUP-IAM and CAP-InitialDP | Nokia | CAMEL2 | A161 | 0 | F | 03.78 | R97 | 6.8.0 | revised to 379 |
| N2-010286 | CR | Mapping of Call Forwarding parameters from CAP-Connect to ISUP-IAM and CAP-InitialDP | Nokia | CAMEL2 | A162 | 0 | A | 03.78 | R98 | 7.5.0 | revised to 380 |
| N2-010287 | CR | Mapping of Call Forwarding parameters from CAP-Connect to ISUP-IAM and CAP-InitialDP | Nokia | CAMEL2 | 288 | 0 | A | 23.78 | R99 | 3.8.0 | revised to 381 |
| N2-010288 | CR | Mapping of Call Forwarding parameters from CAP-Connect to ISUP-IAM and CAP-InitialDP | Nokia | CAMEL2 | 289 | 0 | A | 23.78 | Rel-4 | 4.0.0 | revised to 382 |
| N2-010289 | CR | Mapping of Call Forwarding parameters from CAP-Connect to ISUP-IAM and CAP-InitialDP | Nokia | CAMEL2 |  |  | A | 23.078 | Rel-5 | 5d.7.0 | revised to 383 |
| N2-010290 | CR | Correction of error implementing CR 23.078-181r2 | Rapporteur | CAMEL3 | 290 |  | F | 23.078 | R99 | 3.8.0 | approved |
| N2-010291 | CR | Correction of error implementing CR 23.078-181r2 | Rapporteur | CAMEL3 | 291 |  | A | 23.078 | Rel-4 | 4.0.0 | approved |
| N2-010292 | CR | Contradiction and inconsistency among descriptions on SMS | Siemens AG | CAMEL3 | 155 |  | F | 29.078 | R99 | 3.7.0 | revised to 399 |
| N2-010293 | CR | Contradiction and inconsistency among descriptions on SMS | Siemens AG | CAMEL3 | 156 |  | A | 29.078 | Rel-4 | 4.0.0 | revised to 462 |
| N2-010294 | TS-INFO | Draft 23.078 V5D.6.0 | Rapporteur | CAMEL4 |  |  |  | 23.078 | Rel-5 |  | noted |
| N2-010295 | CR | For better description of the triggering criteria for MT-SMS | Siemens AG | CAMEL4 |  |  |  | 23.078 | Rel-5 |  | withdrawn |
| N2-010296 | CR | For better description of the triggering criteria for MT-SMS | Siemens AG | CAMEL4 |  |  |  | 29.078 | Rel-5 |  | withdrawn |
| N2-010297 | CR | Mobility management for GPRS subscriber | Siemens AG | CAMEL4 |  |  |  | 23.008 | Rel-5 |  | postponed |
| N2-010298 | CR | Mobility management for GPRS subscriber | Siemens AG | CAMEL4 |  |  |  | 23.016 | Rel-5 |  | postpoed |
| N2-010299 | CR | Mobility management for GPRS subscriber | Siemens AG | CAMEL4 |  |  |  | 23.060 | Rel-5 |  | postponed |
| N2-010300 | CR | Mobility management for GPRS subscriber (chapter 9) | Siemens AG | CAMEL4 |  |  |  | 23.078 | Rel-5 |  | noted |
| N2-010301 | CR | Mobility management for GPRS subscriber in chapter 10 | Siemens AG | CAMEL4 |  |  |  | 23.078 | Rel-5 |  | postponed |
| N2-010302 | CR | Mobility management for GPRS subscriber | Siemens AG | CAMEL4 |  |  |  | 29.002 | Rel-5 |  | postponed |
| N2-010303 | CR | Providing the location information during ongoing call | Siemens AG | CAMEL4 |  |  |  | 23.078 | Rel-5 |  | noted |
| N2-010304 | CR | Providing the location information during ongoing call | Siemens AG | CAMEL4 |  |  |  | 29.078 | Rel-5 |  | postponed |
| N2-010305 | CR | Inclusion of ODB data in ATM | Siemens AG | CAMEL4 |  |  |  | 23.078 | Rel-5 |  | postponed |
| N2-010306 | CR | Inclusion of ODB data in ATM | Siemens AG | CAMEL4 |  |  |  | 29.002 | Rel-5 |  | postponed |
| N2-010307 | CR | Supported CAMEL Phases in VLR is temporary | Vodafone Group Plc | CAMEL3 |  | 0 | F | 23.008 | R99 | 3.5.0 | revised to 377 |
| N2-010308 | CR | Handling of second SIFOC | Vodafone Group Plc | CAMEL3 | 292 | 0 | F | 23.078 | R99 | 3.8.0 | revised to 404 |
| N2-010309 | CR | Handling of second SIFOC | Vodafone Group Plc | CAMEL3 | 293 | 0 | A | 23.078 | Rel-4 | 4.0.0 | revised to 406 |
| N2-010310 | CR | Introduction of CAMEL phase 4 | Vodafone Group Plc | CAMEL4 |  | 4 | B | 23.018 | Rel-5 | 4.2.0 | noted |
| N2-010311 | CR | Introduction of CAMEL phase 4 | Vodafone Group Plc | CAMEL4 |  | 0 | B | 23.083 | Rel-5 | 4.2.0 | noted |
| N2-010312 | CR | Corrections for CAMEL support of OR | Vodafone Group Plc | CAMEL4 |  | 2 | C | 23.078 | Rel-5 | 5D.7.0 | revised to 416 |
| N2-010313 | DISC | CPH: Open Issues | Vodafone Group Plc |  |  |  |  |  |  |  | revised to 422 |
| N2-010314 | CR | Handling of reconnect after leg 2 disconnects | Vodafone Group Plc | CAMEL4 |  | 0 | F | 23.078 | Rel-5 | 5D.7.0 | revised to 420 |
| N2-010315 | CR | Corrections to procedure CAMEL_EXPORT_LEG_MSC | Vodafone Group Plc | CAMEL4 |  | 0 | F | 23.078 | Rel-5 | 5D.7.0 | revised to 431 |
| N2-010316 | CR | Addition of NC & NP columns to IF tables | Vodafone Group Plc | CAMEL4 |  | 0 | C | 23.078 | Rel-5 | 5D.7.0 | revised to 424 |
| N2-010317 | CR | Introduction of CPH operations (ASN.1) | Vodafone Group Plc | CAMEL4 |  | 2 | B | 29.078 | Rel-5 | d5.1.0 | approved |
| N2-010318 | CR | Correction to GPRS SDL:no state transition for QoS-induced ACR-GPRS | Ericsson | CAMEL3 | 294 |  | F | 23.078 | R99 | 3.8.0 | revised to 389 |
| N2-010319 | CR | Correction to ACR-GPRS procedure description | Ericsson | CAMEL3 | 157 |  | F | 29.078 | R99 | 3.7.0 | revised to 391 |
| N2-010320 | CR | Correction to IDP-GPRS & EDP-GPRS: reporting the GGSN Address for signalling | Ericsson | CAMEL3 | 158 |  | F | 29.078 | R99 | 3.7.0 | rejected |
| N2-010321 | CR | Clarification on the usage of SII2 parameter in CAP | Ericsson | CAMEL3 | 159 |  | F | 29.078 | R99 | 3.7.0 | revised to 408 |
| N2-010322 | CR | Correction to state transition for Assisting gsmSSF | Ericsson | CAMEL3 | 160 |  | F | 29.078 | R99 | 3.7.0 | revised to 414 |
| N2-010323 | CR | Correction to IMPORT statements | Ericsson | CAMEL3 | 161 |  | F | 29.078 | R99 | 3.7.0 | revised to 384 |
| N2-010324 | CR | Correction of gsmSCF initiated new calls: CAMEL_ICA_MSC process | Alcatel | CAMEL4 |  | 8 | F | 23.078 | Rel-5 | 5D.7.0 | revised to 432 |
| N2-010325 | CR | Correction of Call Release | Alcatel | CAMEL4 |  |  | F | 23.078 | Rel-5 | 5D.7.0 | revised to 421 |
| N2-010326 | DISC | Charging and Information concepts | Alcatel | CAMEL4 |  |  |  | 23.078 | Rel-5 |  | noted |
| N2-010327 | REPORT | Draft Meeting Report from CN2#17 | MCC |  |  |  |  |  |  |  | approved |
| N2-010328 | REPORT | Draft Meeting Report from CN#11 | MCC |  |  |  |  |  |  |  | noted |
| N2-010329 | REPORT | Draft Meeting Report from SA#11 | MCC |  |  |  |  |  |  |  | noted |
| N2-010330 | LS IN | LS on IMS Service Provision | MCC |  |  |  |  |  |  |  | noted |
| N2-010331 | WORK PLAN | Latest version of the work plan | MCC |  |  |  |  |  |  |  | noted |
| N2-010332 | REPORT | Report from CAMEL4 CPH adHoc Meeting | CN2 Chairman |  |  |  |  |  |  |  | approved |
| N2-010333 | CR | ASN.1 syntax correction | Siemens AG | CAMEL3 | 162 |  | F | 29.078 | R99 | 3.7.0 | revised to 386 |
| N2-010334 | CR | ASN.1 syntax correction | Siemens AG | CAMEL3 | 163 |  | A | 29.078 | Rel-4 | 4.0.0 | revised to 387 |
| N2-010335 | CR | Correction of the MAXIMUM-FOR-FCI-BILLING-CHARGING value | Nokia | CAMEL3 | 164 |  | F | 29.078 | R99 | 3.7.0 | revised to 388 |
| N2-010336 | CR | Correction of the MAXIMUM-FOR-FCI-BILLING-CHARGING value | Nokia | CAMEL3 | 165 |  | A | 29.078 | Rel-4 | 4.0.0 | approved |
| N2-010337 | CR | Correction of the gprsSSF error handling | Nokia | CAMEL3 | 166 |  | F | 29.078 | R99 | 3.7.0 | revised to 393 |
| N2-010338 | CR | Correction of the gprsSSF error handling | Nokia | CAMEL3 | 167 |  | A | 29.078 | Rel-4 | 4.0.0 | approved |
| N2-010339 | CR | Clarification of the TC dialogue termination | Nokia | CAMEL3 | 168 |  | F | 29.078 | R99 | 3.7.0 | revised to 394 |
| N2-010340 | CR | Clarification of the TC dialogue termination | Nokia | CAMEL3 | 169 |  | A | 29.078 | Rel-4 | 4.0.0 | revised to 395 |
| N2-010341 | CR | The termination of the dialogue is not clear after ActivityTestGPRS Return Result. | Nokia | CAMEL3 | 170 |  | F | 29.078 | R99 | 3.7.0 | revised to 396 |
| N2-010342 | CR | The termination of the dialogue is not clear after ActivityTestGPRS Return Result. | Nokia | CAMEL3 | 171 |  | A | 29.078 | Rel-4 | 4.0.0 | revised to 397 |
| N2-010343 | CR | Alignement the 29.078 on the 23.078 | Alcatel | CAMEL3 | 172 |  | F | 29.078 | R99 | 3.7.0 | revised to 410 |
| N2-010344 | CR | Correction on the call-Diversion-Treatment-Indicator at the GMSC | Alcatel | CAMEL3 | 295 |  | F | 23.078 | R99 | 3.8.0 | revised to 412 |
| N2-010345 | CR | Introduction of Reference Number for MT-SMS | Ericsson | CAMEL4 |  |  | B | 23.078 | Rel-5 | 5D.7.0 | revised to 433 |
| N2-010346 | CR | Introduction of Reference Number for MT-SMS | Ericsson | CAMEL4 |  |  | B | 29.078 | Rel-5 | X.5.1 | revised to 434 |
| N2-010347 | CR | Correction to MT-SMS Trigger Criteria | Ericsson | CAMEL4 |  |  | F | 23.078 | Rel-5 | 5D.7.0 | revised to 435 |
| N2-010348 | CR | Correction to MT-SMS Trigger Criteria | Ericsson | CAMEL4 |  |  | F | 29.002 | Rel-5 | 3.8.0 | revised to 436 |
| N2-010349 | CR | Handling of reconnect after leg2 disconnects | Vodafone Group Plc | CAMEL4 |  | 0 | F | 23.018 | Rel-5 | 4.2.0 | approved |
| N2-010350 | Disc | Definition of eventTypeCharging parameter in RNC & ENC operations | C-DOT | CAMEL4 |  |  |  |  |  |  | revised to 425 |
| N2-010351 | CR | Handling of RNC & ENC operations in gsmSSF | C-DOT | CAMEL4 |  |  | B | 23.078 | Rel-5 |  | revised to 426 |
| N2-010352 | CR | Introduction of RNC & ENC operations , procedures & ASN definitions | C-DOT | CAMEL4 |  |  | B | 29.078 | Rel-5 |  | revised to 427 |
| N2-010353 | CR | Handling of a variable to indicate an existing relationship with CSE | C-DOT | CAMEL4 |  |  | C | 23.018 | Rel-5 |  | revised to 428 |
| N2-010354 | CR | Creation of Control/Monitoring relationship with CSE at DP3 | C-DOT | CAMEL4 |  |  | C | 23.078 | Rel-5 |  | revised to 429 |
| N2-010355 | CR | InitialDP modified to indicate existance of relationship with CSE | C-DOT | CAMEL4 |  |  | C | 29.078 | Rel-5 |  | revised to 430 |
| N2-010356 | CR | Introduction of Reference Number for MO-SMS | Ericsson | CAMEL3 | 296 |  | B | 23.078 | R99 | 3.8.0 | revised to 400 |
| N2-010357 | CR | Introduction of Reference Number for MO-SMS | Ericsson | CAMEL3 | 175 |  | B | 29.078 | R99 | 3.7.0 | revised to 402 |
| N2-010358 | CR | Introduction of MT-SMS interworking | Ericsson | CAMEL4 |  |  | B | 23.060 | Rel-5 |  | revised to 438 |
| N2-010359 | LS OUT | LS from CN2 to SA5: Inclusion of CAMEL elements in MT-SMS CDR | Ericsson | CAMEL4 |  |  |  |  | Rel-5 |  | revised to 440 |
| N2-010360 | CR | Correction of gprsSSF TC usage | Alcatel | CAMEL3 | 173 |  | F | 29.078 | R99 | 3.7.0 | revised to 367 |
| N2-010361 | CR | Setting of PDP Type Organization Spare Bits | Alcatel | CAMEL3 | 174 |  | F | 29.078 | R99 | 3.7.0 | revised to 442 |
| N2-010362 | CR | Supported CAMEL Phases in VLR is temporary | Vodafone Group Plc | CAMEL3 |  | 0 | A | 23.008 | Rel-4 | 4.0.0 | revised to 378 |
| N2-010363 | INFO | Status of CN2 specifications after TSG#11 | MCC |  |  |  |  |  |  |  | noted |
| N2-010364 | TDOC LIST | Tdoc list before CN2#18 starts | MCC |  |  |  |  |  |  |  | noted |
| N2-010365 | REPORT | Report from SA1 CAMEL adHoc meeting | MCC |  |  |  |  |  |  |  | revised to 370 |
| N2-010366 | CALENDAR | CN2 year 2002 meeting calendar | CN2 chairman |  |  |  |  |  |  |  | noted |
| N2-010367 | CR | Correction of gprsSSF TC usage | Alcatel | CAMEL3 | 173 | 1 | F | 29.078 | R99 | 3.7.0 | noted |
| N2-010368 | DISC | “Reporting of data volume and duration in excess of 4Gbyte and 24 hours respectively”. | Ericsson |  |  |  |  |  |  |  | noted |
| N2-010369 | LS IN | Charging requirements on Call Party Handling | SA1 |  |  |  |  |  |  |  | noted |
| N2-010370 | REPORT | Report from SA1 CAMEL adHoc meeting |  |  |  |  |  |  |  |  | noted |
| N2-010371 | WID | CAMEL4 scope in Rel-5 for TSG-CN | CN2 chairman | CAMEL4 |  |  |  |  | Rel-5 |  | approved |
| N2-010372 | Work plan | CN2#18 comments on the work plan | CN2 chairman | CAMEL4 |  |  |  |  | Rel-5 |  | revised to 471 |
| N2-010373 | CR | Addition of SCCP information for the interface between gsmSCF and SGSN | Lucent Technologies |  |  |  |  | 29.002 | R99 |  | withdrawn |
| N2-010374 | CR | Addition of SCCP information for the interface between gsmSCF and SGSN | Lucent Technologies |  |  |  |  | 29.002 | Rel-4 |  | withdrawn |
| N2-010375 | CR | Addition of SCCP information for the interface between gsmSCF and SGSN | Lucent Technologies |  |  |  |  | 29.002 | Rel-5 |  | withdrawn |
| N2-010376 | DISC | Implementation of enhancements to subscriber dialled services | Vodafone Group Plc |  |  |  |  |  |  |  | noted |
| N2-010377 | CR | Supported CAMEL Phases in VLR is temporary | Vodafone Group Plc | CAMEL3 |  | 1 | F | 23.008 | R99 | 3.5.0 | endorced |
| N2-010378 | CR | Supported CAMEL Phases in VLR is temporary | Vodafone Group Plc | CAMEL3 |  | 1 | A | 23.008 | Rel-4 | 4.0.0 | endorced |
| N2-010379 | CR | Mapping of Call Forwarding parameters from CAP-Connect to ISUP-IAM and CAP-InitialDP | Nokia | CAMEL2 | A161 | 1 | F | 03.78 | R97 | 6.8.0 | approved |
| N2-010380 | CR | Mapping of Call Forwarding parameters from CAP-Connect to ISUP-IAM and CAP-InitialDP | Nokia | CAMEL2 | A162 | 1 | A | 03.78 | R98 | 7.5.0 | approved |
| N2-010381 | CR | Mapping of Call Forwarding parameters from CAP-Connect to ISUP-IAM and CAP-InitialDP | Nokia | CAMEL3 | 288 | 1 | F | 23.078 | R99 | 3.8.0 | approved |
| N2-010382 | CR | Mapping of Call Forwarding parameters from CAP-Connect to ISUP-IAM and CAP-InitialDP | Nokia | CAMEL3 | 289 | 1 | A | 23.078 | Rel-4 | 4.0.0 | approved |
| N2-010383 | CR | Mapping of Call Forwarding parameters from CAP-Connect to ISUP-IAM and CAP-InitialDP | Nokia | CAMEL3 |  |  | A | 23.078 | Rel-5 | 5d.7.0 | approved |
| N2-010384 | CR | Correction to IMPORT statements | Ericsson | CAMEL3 | 161 | 1 | F | 29.078 | R99 | 3.7.0 | approved |
| N2-010385 | CR | Correction to IMPORT statements | Ericsson | CAMEL3 | 176 |  | A | 29.078 | Rel-4 | 4.0.0 | approved |
| N2-010386 | CR | ASN.1 syntax correction | Siemens AG | CAMEL3 | 162 | 1 | F | 29.078 | R99 | 3.7.0 | revised to 453 |
| N2-010387 | CR | ASN.1 syntax correction | Siemens AG | CAMEL3 | 163 | 1 | A | 29.078 | Rel-4 | 4.0.0 | revised to 454 |
| N2-010388 | CR | Correction of the MAXIMUM-FOR-FCI-BILLING-CHARGING value | Nokia | CAMEL3 | 164 | 1 | F | 29.078 | R99 | 3.7.0 | revised to 441 |
| N2-010389 | CR | Correction to GPRS SDL: no state transition for QoS-induced ACR-GPRS | Ericsson | CAMEL3 | 294 | 1 | F | 23.078 | R99 | 3.8.0 | approved |
| N2-010390 | CR | Correction to GPRS SDL: no state transition for QoS-induced ACR-GPRS | Ericsson | CAMEL3 | 297 |  | A | 23.078 | Rel-4 | 4.0.0 | approved |
| N2-010391 | CR | Correction to ACR-GPRS procedure description | Ericsson | CAMEL3 | 157 | 1 | F | 29.078 | R99 | 3.7.0 | approved |
| N2-010392 | CR | Correction to ACR-GPRS procedure description | Ericsson | CAMEL3 | 177 |  | A | 29.078 | Rel-4 | 4.0.0 | approved |
| N2-010393 | CR | Correction of the gprsSSF error handling | Nokia | CAMEL3 | 166 | 1 | F | 29.078 | R99 | 3.7.0 | approved |
| N2-010394 | CR | Clarification of the TC dialogue termination | Nokia | CAMEL3 | 168 | 1 | F | 29.078 | R99 | 3.7.0 | approved |
| N2-010395 | CR | Clarification of the TC dialogue termination | Nokia | CAMEL3 | 169 | 1 | A | 29.078 | Rel-4 | 4.0.0 | approved |
| N2-010396 | CR | The termination of the dialogue is not clear after ActivityTestGPRS Return Result. | Nokia | CAMEL3 | 170 | 1 | F | 29.078 | R99 | 3.7.0 | approved |
| N2-010397 | CR | The termination of the dialogue is not clear after ActivityTestGPRS Return Result. | Nokia | CAMEL3 | 171 | 1 | A | 29.078 | Rel-4 | 4.0.0 | approved |
| N2-010398 | CR | Inclusion of warning note for the reporting of total duration or volume for GPRS | Ericsson | CAMEL3 | 298 |  | F | 23.078 | R99 | 3.8.0 | revised to 459 |
| N2-010399 | CR | Contradiction and inconsistency among descriptions on SMS | Siemens AG | CAMEL3 | 155 | 1 | F | 29.078 | R99 | 3.7.0 | revised to 461 |
| N2-010400 | CR | Introduction of Reference Number for MO-SMS | Ericsson | CAMEL3 | 296 | 1 | F | 23.078 | R99 | 3.8.0 | revised to 437 |
| N2-010401 | LS OUT | Liaison Statement on introduction of SMS Reference Number for SMS | Ericsson |  |  |  |  |  |  |  | revised to 446 |
| N2-010402 | CR | Introduction of Reference Number for MO-SMS | Ericsson | CAMEL3 | 175 | 1 | F | 29.078 | R99 | 3.7.0 | revised to 447 |
| N2-010403 | PRES | Presentation of outgoing call barring | Lucent Technologies |  |  |  |  |  |  |  | revised to 423 |
| N2-010404 | CR | Handling of second SIFOC | Vodafone Group Plc | CAMEL3 | 292 | 1 | F | 23.078 | R99 | 3.8.0 | approved |
| N2-010405 | CR | Initialisation of variable to monitor activations of CSIs | Vodafone Group Plc | CAMEL3 |  |  | F | 23.018 | R99 | 3.7.0 | revised to 419 |
| N2-010406 | CR | Handling of second SIFOC | Vodafone Group Plc | CAMEL3 | 293 | 1 | A | 23.078 | Rel-4 | 4.0.0 | approved |
| N2-010407 | CR | Initialisation of variable to monitor activations of CSIs | Vodafone Group Plc | CAMEL3 |  |  | A | 23.018 | Rel-4 | 3.2.0 | endorced |
| N2-010408 | CR | Correction on the usage of SII2 parameter in CAP | Ericsson | CAMEL3 | 159 | 1 | F | 29.078 | R99 | 3.7.0 | approved |
| N2-010409 | CR | Correction on the usage of SII2 parameter in CAP | Ericsson | CAMEL3 | 178 |  | A | 29.078 | Rel-4 | 4.0.0 | approved |
| N2-010410 | CR | Alignement the 29.078 on the 23.078 | Alcatel | CAMEL3 | 172 | 1 | F | 29.078 | R99 | 3.7.0 | approved |
| N2-010411 | CR | Alignement the 29.078 on the 23.078 | Alcatel | CAMEL3 | 179 |  | A | 29.078 | Rel-4 | 4.0.0 | approved |
| N2-010412 | CR | Correction on the call-Diversion-Treatment-Indicator at the GMSC | Alcatel | CAMEL3 | 295 | 1 | F | 23.078 | R99 | 3.8.0 | approved |
| N2-010413 | CR | Correction on the call-Diversion-Treatment-Indicator at the GMSC | Alcatel | CAMEL3 | 299 |  | A | 23.078 | Rel-4 | 4.0.0 | approved |
| N2-010414 | CR | Correction to state transition for Assisting gsmSSF | Ericsson | CAMEL3 | 160 | 1 | F | 29.078 | R99 | 3.7.0 | approved |
| N2-010415 | CR | Correction to state transition for Assisting gsmSSF | Ericsson | CAMEL3 | 180 |  | A | 29.078 | Rel-4 | 4.0.0 | approved |
| N2-010416 | CR | Corrections for CAMEL support of OR | Vodafone Group Plc | CAMEL4 |  | 2 | C | 23.078 | Rel-5 | 5D.7.0 | revised to 439 |
| N2-010417 | LS OUT | Liaison Statement on Optimal Routeing of a forwarded call | Vodafone Group Plc | CAMEL4 |  |  |  |  | Rel-5 |  | revised to 465 |
| N2-010418 | LS OUT | LS “Charging and Information concepts for CAMEL Call Party Handling” | Alcatel | CAMEL4 |  |  |  |  | Rel-5 |  | revised to 468 |
| N2-010419 | CR | Initialisation of variable to monitor activations of CSIs | Vodafone Group Plc | CAMEL3 |  |  | F | 23.018 | R99 | 3.7.0 | endorced |
| N2-010420 | CR | Handling of reconnect after leg 2 disconnects | Vodafone Group Plc | CAMEL4 |  | 1 | F | 23.078 | Rel-5 | 5D.7.0 | approved |
| N2-010421 | CR | Correction of Call Release | Alcatel | CAMEL4 |  | 1 | F | 23.078 | Rel-5 | 5D.7.0 | approved |
| N2-010422 | DISC | CPH Open issues | Vodafone Group Plc | CAMEL4 |  |  |  |  | Rel-5 |  | revised to 469 |
| N2-010423 | PRES | Presentation of outgoing call barring | Lucent Technologies |  |  |  |  |  |  |  | noted |
| N2-010424 | CR | Addition of NC & NP columns to IF tables | Vodafone Group Plc | CAMEL4 |  | 1 | C | 23.078 | Rel-5 | 5D.7.0 | approved |
| N2-010425 | Disc | Definition of eventTypeCharging parameter in RNC & ENC operations | C-DOT | CAMEL4 |  |  |  |  |  |  | noted |
| N2-010426 | CR | Handling of RNC & ENC operations in gsmSSF | C-DOT | CAMEL4 |  | 1 | B | 23.078 | Rel-5 |  | revised to 455 |
| N2-010427 | CR | Introduction of RNC & ENC operations , procedures & ASN definitions | C-DOT | CAMEL4 |  | 1 | B | 29.078 | Rel-5 |  | noted |
| N2-010428 | CR | Handling of a variable to indicate an existing relationship with CSE | C-DOT | CAMEL4 |  |  | C | 23.018 | Rel-5 |  | noted |
| N2-010429 | CR | Creation of Control/Monitoring relationship with CSE at DP3 | C-DOT | CAMEL4 |  |  | C | 23.078 | Rel-5 |  | noted |
| N2-010430 | CR | InitialDP modified to indicate existance of relationship with CSE | C-DOT | CAMEL4 |  |  | C | 29.078 | Rel-5 |  | noted |
| N2-010431 | CR | Corrections to procedure CAMEL_EXPORT_LEG_MSC | Vodafone Group Plc | CAMEL4 |  | 1 | F | 23.078 | Rel-5 | 5D.7.0 | approved |
| N2-010432 | CR | Correction of gsmSCF initiated new calls: CAMEL_ICA_MSC process | Alcatel | CAMEL4 |  | 9 | F | 23.078 | Rel-5 | 5D.7.0 | approved |
| N2-010433 | CR | Introduction of Reference Number for MT-SMS | Ericsson | CAMEL4 |  | 1 | B | 23.078 | Rel-5 | 5D.7.0 | conditionally approved |
| N2-010434 | CR | Introduction of Reference Number for MT-SMS | Ericsson | CAMEL4 |  | 1 | B | 29.078 | Rel-5 | X.5.1 | conditonally approved |
| N2-010435 | CR | Correction to MT-SMS Trigger Criteria | Ericsson | CAMEL4 |  | 1 | F | 23.078 | Rel-5 | 5D.7.0 | approved |
| N2-010436 | CR | Correction to MT-SMS Trigger Criteria | Ericsson | CAMEL4 |  | 1 | F | 29.002 | Rel-5 | 3.8.0 | approved |
| N2-010437 | CR | Introduction of Reference Number for MO-SMS | Ericsson | CAMEL3 | 296 | 2 | F | 23.078 | R99 | 3.8.0 | revised to 444 |
| N2-010438 | CR | Introduction of MT-SMS interworking | Ericsson | CAMEL4 |  | 1 | B | 23.060 | Rel-5 |  | endorced |
| N2-010439 | CR | Corrections for CAMEL support of OR | Vodafone Group Plc | CAMEL4 |  | 3 | C | 23.078 | Rel-5 | 5D.7.0 | approved |
| N2-010440 | LS OUT | LS from CN2 to SA5: Inclusion of CAMEL elements in MT-SMS CDR | Ericsson | CAMEL4 |  |  |  |  | Rel-5 |  | approved |
| N2-010441 | CR | Correction of the MAXIMUM-FOR-FCI-BILLING-CHARGING value | Nokia | CAMEL3 | 164 | 2 | F | 29.078 | R99 | 3.7.0 | approved |
| N2-010442 | CR | Setting of End User Address Spare Bits | Alcatel | CAMEL3 | 174 | 1 | F | 29.078 | R99 | 3.7.0 | approved |
| N2-010443 | CR | Setting of End User Address Spare Bits | Alcatel | CAMEL3 | 181 |  | A | 29.078 | Rel-4 | 4.0.0 | approved |
| N2-010444 | CR | Introduction of Reference Number for MO-SMS | Ericsson | CAMEL3 | 296 | 3 | F | 23.078 | R99 | 3.8.0 | approved |
| N2-010445 | CR | Introduction of Reference Number for MO-SMS | Ericsson | CAMEL3 | 300 |  | A | 23.078 | Rel-4 | 4.0.0 | approved |
| N2-010446 | LS OUT | Liaison Statement on introduction of SMS Reference Number for SMS | Ericsson | CAMEL3 |  |  |  |  |  |  | Conditionally approved |
| N2-010447 | CR | Introduction of Reference Number for MO-SMS | Ericsson | CAMEL3 | 175 | 2 | F | 29.078 | R99 | 3.7.0 | approved |
| N2-010448 | CR | Introduction of Reference Number for MO-SMS | Ericsson | CAMEL3 | 182 |  | A | 29.078 | Rel-4 | 4.0.0 | approved |
| N2-010449 | CR | CAMEL Capability Handling in GPRS-CSI | Vodafone | CAMEL3 | 301 |  | F | 23.078 | R99 | 3.8.0 | approved |
| N2-010450 | CR | CAMEL Capability Handling in GPRS-CSI | Vodafone | CAMEL3 | 302 |  | A | 23.078 | Rel-4 | 4.0.0 | approved |
| N2-010451 | CR | Enchancements to Subscribed Dialled Services | Vodafone | CAMEL4 |  |  | B | 23.018 | Rel-5 | 4.2.0 | noted |
| N2-010452 | CR | Enhancements to Subscribed Dialled Services | Vodafone | CAMEL4 |  |  | B | 23.078 | Rel-5 | 5d.7.0 | noted |
| N2-010453 | CR | ASN.1 syntax correction | Siemens AG | CAMEL3 | 162 | 2 | F | 29.078 | R99 | 3.7.0 | revised to 456 |
| N2-010454 | CR | ASN.1 syntax correction | Siemens AG | CAMEL3 | 163 | 2 | A | 29.078 | Rel-4 | 4.0.0 | revised to 457 |
| N2-010455 | CR | Handling of RNC & ENC operations in gsmSSF | C-DOT | CAMEL4 |  | 1 | B | 23.078 | Rel-5 | 5d.7.0 | revised to 470 |
| N2-010456 | CR | ASN.1 syntax correction | Siemens AG | CAMEL3 | 162 | 3 | F | 29.078 | R99 | 3.7.0 | approved |
| N2-010457 | CR | ASN.1 syntax correction | Siemens AG | CAMEL3 | 163 | 3 | A | 29.078 | Rel-4 | 4.0.0 | approved |
| N2-010458 | LS IN | LS not received |  |  |  |  |  |  |  |  | withdrawn |
| N2-010459 | CR | Inclusion of warning note for the reporting of total duration or volume for GPRS | Ericsson | CAMEL3 | 298 | 1 | F | 23.078 | R99 | 3.8.0 | approved |
| N2-010460 | CR | Inclusion of warning note for the reporting of total duration or volume for GPRS | Ericsson | CAMEL3 | 303 |  | A | 23.078 | Rel-4 | 4.0.0 | approved |
| N2-010461 | CR | Contradiction and inconsistency among descriptions on SMS | Siemens AG | CAMEL3 | 155 | 2 | F | 29.078 | R99 | 3.7.0 | revised to 466 |
| N2-010462 | CR | Contradiction and inconsistency among descriptions on SMS | Siemens AG | CAMEL3 | 156 | 1 | A | 29.078 | Rel-4 | 4.0.0 | revised to 467 |
| N2-010463 | CR | Indication of gsmSCF Address in Continue GPRS and Connect GPRS Ifs | Alcatel, T-Mobil | CAMEL3 | 304 |  | F | 23.078 | R99 | 3.8.0 | revised to 472 |
| N2-010464 | CR | Liaison Statement on Optimal Routeing of a forwarded call | Alcatel, T-Mobil | CAMEL3 | 183 |  | F | 29.078 | R99 | 3.7.0 | revised to 474 |
| N2-010465 | LS OUT | Output LS to SA1: Corrections for CAMEL support of OR | Vodafone | CAMEL4 |  |  |  | 23.078 | Rel-5 |  | approved |
| N2-010466 | CR | Contradiction and inconsistency among descriptions on SMS | Siemens AG | CAMEL3 | 155 | 3 | F | 29.078 | R99 | 3.7.0 | approved |
| N2-010467 | CR | Contradiction and inconsistency among descriptions on SMS | Siemens AG | CAMEL3 | 156 | 2 | A | 29.078 | Rel-4 | 4.0.0 | approved |
| N2-010468 | LS OUT | LS “Charging and Information concepts for CAMEL Call Party Handling” | Alcatel | CAMEL4 |  |  |  |  |  |  | approved |
| N2-010469 | DISC | CPH: Open Issues | Vodafone | CAMEL4 |  |  |  |  |  |  | noted |
| N2-010470 | CR | Handling of RNC & ENC operations in gsmSSF | C-DOT | CAMEL4 |  | 1 | B | 23.078 | Rel-5 | 5d.7.0 | approved |
| N2-010471 | Work plan | Progress of CAMEL work, changes to Work plan status | CN2 chairman |  |  |  |  |  |  |  | approved |
| N2-010472 | CR | Indication of gsmSCF Address in Continue GPRS and Connect GPRS IFs | Alcatel, T-Mobil, Ericsson | CAMEL3 | 304 | 1 | F | 23.078 | R99 | 3.8.0 | approved |
| N2-010473 | CR | Indication of gsmSCF Address in Continue GPRS and Connect GPRS Ifs | Alcatel, T-Mobil, Ericsson | CAMEL3 | 305 |  | A | 23.078 | Rel-4 | 4.0.0 | approved |
| N2-010474 | CR | Indication of gsmSCF Address in Continue GPRS and Connect GPRS Ifs | Alcatel, T-Mobil | CAMEL3 | 183 | 1 | F | 29.078 | R99 | 3.7.0 | approved |
| N2-010475 | CR | Indication of gsmSCF Address in Continue GPRS and Connect GPRS Ifs | Alcatel, T-Mobil, Ericsson | CAMEL3 | 184 |  | A | 29.078 | Rel-4 | 4.0.0 | approved |

Annex D 		Joint meeting between CN1/2/3/4

Attendance: CN1: All, CN2: 14, CN3: 8, CN4: 7

The report below is part of the CN1 Meeting report.

## 23.218 issues for joint CN WG session

N1-010504 : SA2 (S2-010798r2), Type: LS IN , Title: Liaison Statement on IMS-Service Provision

Discussion :  Forwarded to this joint session from CN1#17, so for CN1 comments  see also this doc. in chapter 3. Besides agreeing the Cx interface SA2 agreed on a single standardised protocol to be supported by the S-CSCF for service control. Guidelines for further details are summarised in a new chapter to 23.228. These details are given in S2-010797 which is approved by S2 and not attached to this LS.

These new requirements are not contributed to this meeting, so no drafting based on this can be done in CN1 now. But the protocol architectural requirements will be discussed in the S2/N1-4 meeting later this week.

Where is IMS SCF documented? In chapter 6 of 23.218. Mapping between ISC (IM Service Control) standardized proootocol  (or SIP+) to CAMEL was  proposed to be documented in CN2 specifications. But further work needs to be decided upon when more information is available around these topics. Lot of support to change the confusing SIP+ to a recommendation on name and communicate it to SA2, but SA2 will make that decision and design the needed architecture. A liaison to SA2 is agreed to be sent, and additional clarification to the name could be that this is related to the protocol only.

Additionally it was agreed that the structure of 23.218 should be reviewed and any proposals to change the current structure should be provided in the form of written contributions to the CN joint meeting during CN1 #18.

Conclusion: LS OUT in 888 by Magnus

N1-010749 : 23.218,  Lucent, Type:  CR, Title: Service Triggers in SIP telephony network

Discussion : This contribution gives some generic points of interests, at which the S-CSCF will interact with service platform during the session.

Received as agood starting point. The granularity of triggeres are too big, and some other triggers as eg PRACK could be of interest to the service as well. Break up response to classes were also asked for. More generic description is needed in order to avoid modification for every protocol modification. Also registration related responses should be looked at. Another way of handling this is by filtering. It was proposed to move it into an informative annex. Another proposal was introduction to chapter 5 directly.

Conclusion: Agreed to put this in as informative annex

N1-010761 :  23.218,    Motorola, Type: CR , Title: Modification to scope of TS 23.218

Discussion : A proposal to change the scope so that 23.218 should focus on the Interactions between the S-CSCF and Application Servers (IM_SSF, OSA SCS and SIP Application Servers), and the Mappings and Call Models contained in these entities should not contain the functional requirements for Proxy-CSCF, Interogating-CSCF and Serving-CSCF for basic call/session handling which would be best specified in TS 24.229.

IMS in 23.218  (covering the S-CSCF only) was earlier intended as an  analogue to basic call handling in 23.018 and opinions were raised to keep it that way. A new document to handle the service issues, or make 23.218 more service oriented ? Not recomended moving something to the protocol part,-24.229. But if so, then it should preferably be done before taking it to plenary CN#13 for issuing v1.0.0. At least section 5 of 23.218 could be modified to remove P-CSCF and I-CSCF functionality.

Conclusion : Noted

N1-010762 : 23.218,   Motorola, Type: INFO , Title: TS 23.218      v.0.5.0

Discussion : Latest available version. No changes has been done yet since the April meeing in Sophia. The work is in progress and the architecture is beeing modified.

Conclusion : Noted

## 24.228 issues for joint CN WG session

N1-010702 : 24.228,  ATT, Lucent, Motorola, Type:  CR, Title: Move Annex A to Normative text

Discussion :  Please see also 702 under 8.4 since this was a forwarded document from CN1 earlier this week.

TS 24.228  is intended to be input to plenary CN#12 for approval to v1.0.0

Conclusion : Agreed to move annex A to main part except for clause 100 and 101

N1-010706 : 24.228,  ATT, Type:  CR, Title: Call Transfer Procedures

Discussion : It is proposed that the proposed text be added to an informative Annex (TS 24.228 Annex B) as preliminary material for section 10.5. In addition, the following IETF Internet-Drafts is proposed added to the Work Item Description as IETF dependencies:

- Draft-ietf-sip-cc-transfer-04

- Draft-roach-sip-subscribe-notify-03

An alternative architecture to this where all parties are involved, would be that S-CSCF terminates the REFER and does not impact the first leg, transport (network centric). This was contradicted since UE#1 needs to know about the media, a human centric aapproach. What about privacy on UE#3 and who pays for the transferred leg ? Service control boxes should be shown in the flows. Why do we have 2 scenarios here ? Reason is that eg. REFER is different. Call transfer is a basis for fraud and this document must be reviewed by SA3 before going into the informative annex. 23.228 already has a section on call transfer and therefore a LS should be sent to affected groups,- to S3 with copy to S2 and possibly S5.

Conclusion : Agreed to be put in the annex and not the main body of the TS.  LS OUT in 890 by Sunil

N1-010733 : 24.228,   Lucent, Type: CR , Title: More service control tasks in 24.228

Discussion : In this contribution, the positions where the service control boxes shall be inserted when 180 Ringing, COMET and 486 BUSY messages are met in S-CSCF are indicated in the list.

Ringing is optional, and adding a service control box in every possible flow and message could more efficiently be made through some text. This list was intended as editing rule for the 24.228 update.

Conclusion : Revised to 891 for CN1 during this week (see agenda item 8.4)

N1-010746 :  Lucent, Type:  DISCUSSION, Title: An analysis of the requirements for the Max-Forwards header

Discussion : This contribution discusses the handling of ICMP messages by SIP. The contribution concludes that -due to security reasons - the ICMP messages should be ignored by the 3GPP SIP implementations. It is proposed that CN1 sends a liaison statement to the SA3 requesting a clarification pertaining to handling of the ICMP messages in 3GPP SIP implementations.

Both support and not were raised for a liasion doc. This could instead be seen as an implementation issue. The solution should be sought in the routers themselves. A statement of ignoring ICMP is too restrictive. ICMPs from an insecure source could be ignored.

Conclusion : LS OUT in 892 by Milo

N1-010756 : 24.228       Motorola, Type:  INFO, Title: 24.228v050 "Signalling flows for the IP multimedia call control based on SIP and SDP"

Discussion : Latest version available, also stored on the 3GPP server under specs/latest draft

Conclusion : Noted

N1-010852 : 24.228,    Lucent, Type:  CR, Title: Signalling flow for session release

Discussion :

Conclusion : Forwarded to CN1 during the week in 884

N1-010865 : 24.228,    Motorola, Type:  CR, Title: SIP/SDP compression

Discussion : The number of messages coupled with the typical length of a SIP message places a strenuous burden on bandwidth over the air interface, which remains a scarce and expensive resource. It is proposed that CN1 agree that compression of SIP/SDP messages is required in the Rel-5 IM subsystem architecture over the air interface, and that CN1 should investigate the merits of  both text compression and SIP/SDP aware compression schemes.

SA2 still needs to agree on the schemes and where to compress. Building an efficient dictionary are depending on the amount of messages exchanged. The architecture is a way of reducing amount of messages. S-CSCF could limit the number of messages over the radio interface (in case of forked requests) or all messages could be compressed or both. Possibility of compression seems to be reduced since SA3 has an optional security feature between UE and P-CSCF. Should SA4 be involved? If the compression is made in RAN it will appear in the 25 series, and additionally handover aspects need to be handled. A question is if CN1 is a proper place for further contributions ? The working group on algorithm(s) will be dictated with the architectural decisions to be done. In IETF the ROCH group may be taking this up, but 3GPP can not wait for that. This doc is forwarded to CN1 on Friday after the document has been presented in SA2.

Conclusion : Noted. Forwarded to CN1 later this week (see agenda item 8.4)

N1-010881 :   From SIP#04 (N1-010582), Type:  LS IN, Title: LS “on GPRS work covering break in radio transmission”

Discussion : The joint meeting of SA2 and CN1 identified the following item within 23.228 (see extract under 3 in this liaison) which requires enhancement of a number of GPRS specifications under the control of various working groups. Since CN4 delegates are not all present a request to forward this to CN4 was accepted.

Conclusion : Noted. Forwarded to CN4

# Comments

The members take note that they are hereby invited:

to investigate in their company whether their company does own IPRs which are, or are likely to become Essential in respect of the work of the Technical Specification Group.

to notify the Chairman, or the Director-General of their respective Organizational Partners, of all potential IPRs that their company may own, by means of the IPR Statement and the Licensing declaration forms