3GPP TSG-CN WG2 Meeting #18 	Tdoc N2-010408

Puerto Rico, 14th - 18th May 2001														(revision of N2-010321)

| CHANGE REQUEST |
| --- |
| ( | 29.078 | CR | 159 | ( rev | 1 | ( Current version: | 3.7.0 | ( |
| Proposed change affects: ( | (U)SIM |  | ME/UE |  | Radio Access Network |  | Core Network | X |
| Title: ( | Correction on the usage of SII2 parameter in CAP |
| Source: ( | Ericsson |
| Work item code: ( | CAMEL3 |  | Date: ( | 15 May 2001 |
| Category: ( | F | (agreed by concensus) | Release: ( | R99 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) | Use one of the following releases: 2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) REL-4 (Release 4) REL-5 (Release 5) |
| Reason for change: ( | The data type definition of the parameter “ServiceInteractionIndicatorsTwo” (SII2) lacks a clear description in which CAP operations the sub-parameters of SII2 may be included. For the sub-parameters “forwardServiceInteractionInd”, “backwardServiceInteractionInd” and “nonCUGCall” it is indicated in which CAP operations they may be included. Such indication is missing for “bothwayThroughConnectionInd”, “connectedNumberTreatmentInd”, “holdTreatmentIndicator”, “cwTreatmentIndicator” and “ectTreatmentIndicator”. The lack of this indication leads to ambiguity as to when the SII2 parameter may be included in the CAP operations. For “backwardServiceInteractionInd”, it is indicated that this parameter may be included in “InitialDP”. This is not correct. According to 23.078, this parameter shall not be included in InitialDP. The present CR proposes corrective text that clarifies when these sub-parameters may be included. This text is in alignment with the functional description of the SII2 parameter in 3G TS 23.078. |
| Summary of change: ( | Adding corrective and clarifying text to the “ServiceInteractionIndicatorsTwo” data type definition in section 5.1. |
| Consequences if ( not approved: | Ambiguity concerning the usage of the ServiceInteractionIndicatorsTwo parameter. This may result in situations that this parameter is not included when service designers or MSC designers expect it and vice versa. This may affect Service behaviour. |
| Clauses affected: ( | 5.1 |
| Other specs ( |  | Other core specifications ( |  |
| affected: |  | Test specifications |  |
|  |  | O&M Specifications |  |
| Other comments: ( | Terms like “CON” and “CWA” are semi-official abbreviations for CAMEL operations. The present CR uses the formal CAP operation names instead. |

*** First Change ***

# 5	Common CAP Types

## 5.1	Data types

-- The Definition of Common Data Types follows

CAP-datatypes {ccitt(0) identified-organization(4) etsi(0) mobileDomain(0) umts-network(1) modules(3) cap-datatypes(52) version3(2)}

-- This module contains the type definitions for the CAP v.3 data types.

# DEFINITIONS IMPLICIT TAGS ::= BEGIN

# IMPORTS

...

< unmodified text >

...

ServiceInteractionIndicatorsTwo 						::= SEQUENCE {

forwardServiceInteractionInd		[0]	ForwardServiceInteractionInd		OPTIONAL,

-- applicable to operations InitialDP, Connect and ContinueWithArgument.

backwardServiceInteractionInd		[1]	BackwardServiceInteractionInd		OPTIONAL,

-- applicable to operations Connect and ContinueWithArgument.

bothwayThroughConnectionInd			[2] BothwayThroughConnectionInd			OPTIONAL,

-- applicable to ConnectToResource and EstablishTemporaryConnection

connectedNumberTreatmentInd			[4]	ConnectedNumberTreatmentInd			OPTIONAL,

-- applicable to Connect and ContinueWithArgument

nonCUGCall							[13] NULL								OPTIONAL,

-- applicable to Connect and ContinueWithArgument

-- indicates that no parameters for CUG shall be used for the call (i.e. the call shall

-- be a non-CUG call).

-- If not present, it indicates one of three things:

--  a) continue with modified CUG information (when one or more of either CUG Interlock Code

--     and Outgoing Access Indicator are present), or

--  b) continue with original CUG information (when neither CUG Interlock Code or Outgoing

--     Access Indicator are present), i.e. no IN impact.

--  c) continue with the original non-CUG call.

holdTreatmentIndicator				[50] OCTET STRING (SIZE(1))				OPTIONAL,

-- applicable to InitialDP, Connect and ContinueWithArgument

-- acceptHoldRequest	'xxxx xx01'B

-- rejectHoldRequest	'xxxx xx10'B

-- network default is accept hold request

cwTreatmentIndicator				[51] OCTET STRING (SIZE(1))				OPTIONAL,

-- applicable to InitialDP, Connect and ContinueWithArgument

-- acceptCw	'xxxx xx01'B

-- rejectCw	'xxxx xx10'B

-- network default is accept cw

ectTreatmentIndicator				[52] OCTET STRING (SIZE(1))				OPTIONAL,

-- applicable to InitialDP, Connect and ContinueWithArgument

-- acceptEctRequest	'xxxx xx01'B

-- rejectEctRequest	'xxxx xx10'B

-- network default is accept ect request

...

}

...

< unmodified text >

...

*** End of Document ***

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.3gpp.org/3G_Specs/3G_Specs.htm

Mark one or more of the boxes with an X.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. Work item acronyms are listed in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "3GPP working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.