3GPP TSG-CN WG2 Meeting #20	Tdoc N2-010804

Brighton, UK, 15th - 19th October  2001

| CR-Form-v4 |
| --- |
| CHANGE REQUEST |
| Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc. | 23.078 | CR | 324 | Enter the CR number here. This number is allocated by the 3GPP support team. rev | 1 | Enter the revision number of the CR here. If it is the first version, use a "-". Current version: | 3.10.0 | Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.3gpp.org/3G_Specs/3G_Specs.htm |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question. symbols. |
| Proposed change affects: Mark one or more of the boxes with an X. | (U)SIM |  | ME/UE |  | Radio Access Network |  | Core Network | X |
| Title: Enter a concise description of the subject matter of the CR. It should be no longer than one line. | Indication of deletion of CSI in Notify Subscriber Data Change |
| Source: Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source. | Lucent Technologies |
| Work item code: Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/ | CAMEL Phase 3 |  | Date: Enter the date on which the CR was last revised. | 15th October 2001 |
| Category: Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "3GPP working methods". | F (essential Correction) |  | Release: Enter a single release code from the list below. | R99 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: 2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) REL-4 (Release 4) REL-5 (Release 5) |
| Reason for change: Enter text which explains why the change is necessary. | The notify subscriber data change feature in CAMEL Phase 3 provides a facility for the HLR to notify the gsmSCF about changes in CSI, Call Forwarding, call baring data or ODB (provided that the notification flag is set). A notification is triggered when subscriber data changes. One process that triggers such a notification is subscriber data change by the administrator. A deletion of a CSI constitutes a change in subscriber data, but the current messages are unable to convey the fact that a CSI for a subscriber has been deleted. It is essential for the HLR to indicate the difference between when a CSI is deactivated and when it is deleted. |
| Summary of change: Enter text which describes the most important components of the change. i.e. How the change is made. | The change outlined in this document adds a parameter to the Notify Subscriber Data Change information between the HLR and the gsmSCF. This parameter, the SpecificCSIDeleted indicate which CSI has been deleted for a subscriber. |
| Consequences if Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction). not approved: | An HLR would not be able to indicate to a gsmSCF that a particular CSI has been deleted. |
| Clauses affected: Enter each the number of each clause which contains changes. | 10.3.2.3 |
| Other specs Enter an X in the box if any other specifications are affected by this change. | X | Other core specifications List here the specifications which are affected or the CRs which are linked. | 29.002 (CR#317) |
| affected: |  | Test specifications |  |
|  |  | O&M Specifications |  |
| Other comments: Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above. |  |

10.3.2.3	Notify Subscriber Data Change

10.3.2.3.1	Description

This IF is used by the HLR to notify to the gsmSCF of the change of subscriber data.

10.3.2.3.2	Information Elements

The following information elements are required:

| Information element name | Required | Description |
| --- | --- | --- |
| IMSI | M | The IMSI is used to identify the subscriber. |
| MSISDN | M | The MSISDN is used to identify the subscriber. |
| Call Forwarding SS data | C | This IE is described in a table below. |
| Call Barring SS data | C | This IE is described in a table below. |
| Operator Determined Barring data | C | This IE is described in a table below. |
| CAMEL Subscription Information | C | This IE is described in a table below. |

M	Mandatory (The IE shall always be sent).

C	Conditional (The IE shall be sent, if  available)

Call Forwarding SS data contains the following information:

| Information element name | Required | Description |
| --- | --- | --- |
| SS Code | C | This IE indicates Call Forwarding supplementary service as defined in 3GPP TS 22.004 [25]. |
| Forwarding Feature List | C | See the table below. |
| Notification-to-CSE Flag | C | This IE indicates whether the gsmSCF is notified of a change of Call Forwarding SS data. |

C	Conditional (The IE shall be sent, if available)

Forwarding Feature List contains 1 to 32 items of the following information:

| Information element name | Required | Description |
| --- | --- | --- |
| Basic Service | C | See 3GPP TS 22.002 [24]. Also compound basic service codes can be used in this operation if the subscriber has used a compound code when modifying the SS (e.g. all bearer services compound code). |
| SS Status | C | See 3GPP TS 23.011 [26]. |
| Forwarded-to Number | C | See 3GPP TS 23.082 [27]. |
| Forwarded-to Subaddress | C | See 3GPP TS 23.082 [27]. |
| Subscription Options | C | See 3GPP TS 23.082 [27]. |
| No Reply Condition Time | C | See 3GPP TS 23.082 [27]. |

C	Conditional (The IE shall be sent, if available and applicable)

Call Barring SS data contains the following information:

| Information element name | Required | Description |
| --- | --- | --- |
| SS Code | C | This IE indicates Call Barring supplementary service as defined in 3GPP TS 22.004 [25]. |
| Call Barring Feature List | C | See the table below. |
| Password | C | See 3GPP TS 23.011 [26]. |
| Wrong password attempts counter | C | See 3GPP TS 23.011 [26]. |
| Notification-to-CSE flag | C | This IE indicates whether the gsmSCF is notified of a change of Call Barring SS data. |

C	Conditional (The IE shall be sent, if available)

Call Barring Feature List contains 1 to 32 items of  the following information:

| Information element name | Required | Description |
| --- | --- | --- |
| Basic Service | C | See 3GPP TS 22.002 [24]. Also compound basic service codes can be used in this operation if the subscriber has used a compound code when modifying the SS (e.g. all bearer services compound code). |
| SS Status | C | See 3GPP TS 23.011 [26]. |

C	Conditional (The IE shall be sent, if available and applicable)

Operator determined barring data contains the following information:

| Information element name | Required | Description |
| --- | --- | --- |
| ODB General Data | C | This IE indicates the set of subscribers features that the network operator or the service provider can regulate. |
| ODB HPLMN Specific Data | C | This IE indicates the set of subscribers features that the network operator or the service provider can regulate only when the subscriber is registered in the HPLMN. |
| Notification-to-CSE flag | C | This IE indicates whether the gsmSCF is notified of a change of ODB data. |

C	Conditional (The IE shall be sent, if available and applicable)

CAMEL Subscription Information contains the following information:

| Information element name | Required | Description |
| --- | --- | --- |
| O-CSI | C | See subclause 4.3.1. |
| D-CSI | C | See subclause 4.3.2. |
| T-CSI | C | See subclause 4.3.4. |
| VT-CSI | C | See subclause 4.3.5. |
| TIF-CSI | C | See subclause 4.3.6.2. |
| GPRS-CSI | C | See subclause 6.3.1. |
| SMS-CSI | C | See subclause 7.3.1. |
| SS-CSI | C | See subclause 8.2.1. |
| M-CSI | C | See subclause 9.2.1 |
| Specific CSI Deleted List | C1 | This IE indicates that one or more specific elements of CAMEL Subscription Information have been deleted from the HLR. It shall indicate any of the following : - O-CSI (with TDP criteria for O-CSI); - T-CSI (with TDP criteria for T-CSI); - TIF-CSI; - D-CSI; - VT-CSI with TDP criteria for VT-CSI; - GPRS-CSI; - SMS-CSI; - SS-CSI; - M-CSI. |

C	Conditional (The IE shall be sent, if it was modified)

C1	Conditional (The IE shall be sent, if CSI is/are deleted).