3GPP TSG CN WG2 Meeting #31	N2-030536

Bangkok, Thailand, 27th – 31th October 2003

Title:	Contents of each CAMEL phase

Source:	CN2 Chairman

This is an informative document to summarise functionalities of each CAMEL phase.

# CAMEL phase 1:

## CAMEL phase 1 functionality:

| Functionality | Purpose / supports | Restrictions |
| --- | --- | --- |
| Triggering on MO and MT calls. | Call screening Simple VPN Call Forwarding Call Redirection Call Rerouting Homing of pre-paid calls to HPLMN | No IN announcements supported No charging operations Limited set of detection points, e.g. the hunting services are not possible. MT calls trigger in the GMSC only. Not possible to activate Call Forwardings with VPN short codes. |
| Any Time Interrogation | The SCP may whenever request HLR to provide subscriber status and/or location information. | The location is not up-to-date unless the mobile has an active call ongoing. |

# CAMEL phase 2:

## CAMEL phase 2 functionality:

| Functionality | Purpose / supports | Restrictions |
| --- | --- | --- |
| Triggering on MO and MT calls. | Call screening Simple VPN Call Forwarding Call Redirection Call Rerouting In-band user interaction (DTMF) Tones and announcements | MT calls trigger in the GMSC only. |
| Charging operations | Pre-paid (MO, MT, CF) Free-phone Premium rate Personal Discount Location Dependent discount Reverse Charging |  |
| SCP provided e-parameters | MO AoC | Inter-vendor inter-working problems. |
| New detection points (Abandon, Busy, NotReachable, NoAnswer, RouteSelectFailure cases) | Cleaner termination of relationship. Better pre-paid service. Hunting type of services. |  |
| Triggering criteria | To reduce SCP & SSP load |  |
| Any Time Interrogation | The SCP may whenever request HLR to provide subscriber status and/or location information. | The location is not up-to-date unless the mobile has an active call ongoing. |
| USSD communication between MS and SCP | USSD call-back for pre-paid roaming Control & enquiry of IN services |  |
| Control of north American carrier information | Enhances pre-paid SCP based carrier selection Selecting correct long distance network for user interaction |  |
| Notification of supplementary service (ECT, CD and MPTY) invocation to SCP | Fraud control |  |

# CAMEL phase 3:

## CAMEL phase 3 functionality:

| Functionality | Purpose / supports | Restrictions |
| --- | --- | --- |
| Triggering on MO and MT calls. | Call screening Simple VPN Call Forwarding Call Redirection Call Rerouting In-band user interaction (DTMF) Tones and announcements |  |
| Charging operations | Pre-paid (MO, MT, CF) Free-phone Premium rate Personal Discount Location Dependent discount Reverse Charging |  |
| SCP provided e-parameters | MO & MT AoC |  |
| CAMEL2 new detection points (Abandon, Busy, NotReachable, NoAnswer, RouteSelectFailure cases) | Cleaner termination of relationship. Better pre-paid service. Hunting type of services. |  |
| CAMEL3 new trigger detection points. | To trigger on demand only, e.g. for hunting services. |  |
| Triggering criteria | To reduce SCP & SSP load |  |
| Any Time Interrogation. Enhanced with CAMEL3 current location retrieval. | The SCP may whenever request HLR to provide subscriber status and/or location information. |  |
| USSD communication between MS and SCP | USSD call-back for pre-paid roaming Control & enquiry of IN services |  |
| Control of north American carrier information | Enhances pre-paid SCP based carrier selection Selecting correct long distance network for user interaction |  |
| Notification of supplementary service (ECT, CD and MPTY) invocation to SCP | Fraud control |  |
| Call Gapping | To control SCP overload situations within HPLMN | For CS calls only. Not for SMS or GPRS. |
| MT call triggering in VMSC-B | To control MT supplementary services (CW, hold, CF, CD, ECT, MPTY) Pre-paid for MT air-time charge (1st minute free, e.g. in USA) |  |
| Abandon as an EDP-R | Improves charging |  |
| Enhanced FreeFormatCharging data (40 octets -> 160 octets) | Makes the SCP service logic easier |  |
| Reporting of MSRN/FTN to SCP | Charging control of optimally routed calls |  |
| SCP-HLR interface: ATM/ATSI/NSDC | Multiple Subscriber Profile phase 2 SCP can control CF, barring supplementary services. Off-line subscription control based on VPLMN / time-of-day Virtual operators |  |
| Subscribed dialled services (D-CSI) | HPLMN specific service numbers |  |
| Serving Network Dialled services (N-CSI) | VPLMN specific service numbers |  |
| MO SMS control (CS+PS) | Enhances pre-paid. Enhances VPN | No MT SMS control. Not content based |
| Inter-working with GPRS | GPRS pre-paid | Not content based |
| CS Mobility management notifications | SCP can monitor location / reachability |  |
| Service Interaction Indicators | SCP can control inter-working with supplementary services (CW, hold, CF, CD, ECT, MPTY). |  |

# CAMEL phase 4:

## CAMEL phase 4 functionality in Release 5:

| Functionality | Purpose / supports | Restrictions |
| --- | --- | --- |
| Triggering on MO and MT calls. | Call screening Simple VPN Call Forwarding Call Redirection Call Rerouting In-band user interaction (DTMF) Tones and announcements |  |
| Charging operations | Pre-paid (MO, MT, CF) Free-phone Premium rate Personal Discount Location Dependent discount Reverse Charging |  |
| SCP provided e-parameters | MO & MT AoC |  |
| CAMEL2 new detection points (Abandon, Busy, NotReachable, NoAnswer, RouteSelectFailure cases) | Cleaner termination of relationship. Better pre-paid service. Hunting type of services. |  |
| CAMEL3 new trigger detection points. | To trigger on demand only, e.g. for hunting services. |  |
| Triggering criteria | To reduce SCP & SSP load |  |
| Any Time Interrogation. Enhanced with CAMEL3 current location retrieval. CAMEL4 enhances this to PS domain. | The SCP may whenever request HLR to provide subscriber status and/or location information. |  |
| USSD communication between MS and SCP | USSD call-back for pre-paid roaming Control & enquiry of IN services |  |
| Control of north American carrier information | Enhances pre-paid SCP based carrier selection Selecting correct long distance network for user interaction |  |
| Notification of supplementary service (ECT, CD and MPTY) invocation to SCP | Fraud control |  |
| Call Gapping | To control SCP overload situations within HPLMN | For CS calls only. Not for SMS or GPRS. |
| MT call triggering in VMSC-B | To control MT supplementary services (CW, hold, CF, CD, ECT, MPTY) Pre-paid for MT air-time charge (1st minute free, e.g. in USA) |  |
| Abandon as an EDP-R | Improves charging |  |
| Enhanced FreeFormatCharging data (40 octets -> 160 octets) | Makes the SCP service logic easier |  |
| Reporting of MSRN/FTN to SCP | Charging control of optimally routed calls |  |
| SCP-HLR interface: ATM/ATSI/NSDC | Multiple Subscriber Profile phase 2 SCP can control CF, barring supplementary services. Off-line subscription control based on VPLMN / time-of-day Virtual operators |  |
| Subscribed dialled services (D-CSI) | HPLMN specific service numbers |  |
| Serving Network Dialled services (N-CSI) | VPLMN specific service numbers |  |
| SMS control (CS+PS) | Enhances pre-paid. Enhances VPN | Not content based |
| Inter-working with GPRS | GPRS pre-paid | Not content based |
| CS Mobility management notifications | SCP can monitor location / reachability |  |
| Service Interaction Indicators | SCP can control inter-working with supplementary services (CW, hold, CF, CD, ECT, MPTY). |  |
| Interactions with Optimal Routing | SCP can control usage of OR |  |
| Call Party Handling | Wake-up calls Conference calling Parallel hunting Click-to dial IN based CCBS |  |
| Mid call procedure for MO and MT calls | Control CPH configuration during call. Automatic call collect |  |
| CAMEL for IMS | IMS pre-paid Convergence to CS and GPRS services |  |
| Inclusion of flexible tone injection | Enhancements of pre-paid warning tones Various informative tones |  |
| Provision of location information of called subscriber (Alerting phase) | The location of B-subscriber at the beginning of the call provided to service logic |  |
| Notification of GPRS mobility management to CSE | SCP can monitor location / reachability in PS side |  |
| Inclusion of ODB data in the CSE-HLR interface | Enhancement of MSP ph 2 |  |
| Location information during an ongoing call (Handover DP) | Charging based on current location, for inter-PLMN and/or inter-system handovers |  |
| Transfer of the IMEI (with software version) to the CSE | allow the gsmSCF to determine information about the capabilities of the ME |  |
| Partial implementation of CAMEL phase 4 | A functional entity (VMSC, GMSC or SGSN) may support the complete CAMEL phase 4 functionality or, as a network option, it may support the complete CAMEL phase 3 functionality and a partial implementation of CAMEL phase 4. |  |

## CAMEL phase 4 additions in Release 6

| Enhancements of Dialled Services | Full control of Dialled Services |  |
| --- | --- | --- |
| Full CAMEL4 prepay support for SCUDIF | The capability to report basic service code changes during ongoing call. Prepay service can work with SCUDIF so that correct rate is applied to CS call depending whether it is speech or multimedia. Applies to all call cases (MO, MT, CF). |  |
| Change of position procedure armed with criteria | Technical enhancement to reduce the signalling load |  |