3GPP TSG CN WG2 Meeting #31	N2-030541

N2-030525rev

Bangkok, Thailand, 27th – 31th October 2003

| CR-Form-v7 |
| --- |
| CHANGE REQUEST |
| ( | 23.078 | CR | CRNum | ( rev | - | ( Current version: | 5.5.1 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Change of position armed with criteria (check criteria in SSF) |
| --- | --- |
| Source: ( | Siemens AG |
| Work item code: ( | TEI_6 |  | Date: ( | 21/01/2003 |
| Category: ( | F |  | Release: ( | Rel-6 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: 2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) |
| Reason for change: ( | Change due to the stage 1 changes (CR 22.078-160, S1-030727, approved by SA1#21 Sofia Antipolis, 7 - 11 July 2003, and CR 22.078-xxx, approved by SA1#22 Bangkok, 27 - 11 October 2003). |
| Summary of change: ( | Process CS_gsmSSF: - When Request Report BCSM Event is received, the process CS_gsmSSF stores the criterion which are included in this IF. - When the event, Change_Of_Position occurs, the procedure "Check_Criteria_Chenge_Of_Position" is called. Only if the result is "Pass", the event is reported to the gsmSCF via Event Report BCSM IF. - To realise the checking the criteria fulfilled, a new procedure "Check_Criteria_Chenge_Of_Position" is added. Request Report BCSM Event IF: - DP Specific Criteria IE is enhanced, to include "Change of Position Control Info" which contains up to 10 criterion. Each criteria contains either Location (value of LAI, SAI or CellGlobalID -- see CR 29.078-yyy), indication of Inter-system handover, indication of Inter-PLMN handover or indication of Inter-MSC handover. |
| Consequences if ( not approved: | Service requirement is not technically realised. Signalling load would increase drastically and the CSE (gsmSCF) mightbe overloaded by the unnecessary information for the service. |
| Clauses affected: ( | 4 |
|  | Y | N |  |  |
| Other specs ( | x |  | Other core specifications ( | 29.078-yyy |
| affected: |  | x | Test specifications |  |
|  |  | x | O&M Specifications |  |
| Other comments: ( | This CR includes provisional change in the assumption that S1-031128 (N2-030523) which includes a new proposal "Inter-MSC handover" is approved. |

Figure 4.95-22: Process CS_gsmSSF (sheet 22)

Figure 4.95-35: Process CS_gsmSSF (sheet 35)

Figure 4.95-43: Process CS_gsmSSF (sheet 43)

Figure 4.95-44: Process CS_gsmSSF (sheet 44)

Figure 4.xx-1: Procedure Check_Criteria_Chenge_Of_Position (sheet 1)

*** Next modified part ***

#### 4.6.2.19	Request Report BCSM Event

##### 4.6.2.19.1	Description

This IF is used to request the gsmSSF to monitor for a call-related event, then send a notification back to the gsmSCF when the event is detected (see Event Report BCSM).

##### 4.6.2.19.2	Information Elements

| Information element name | MO | MF | MT | VT | NC | NP | Description |
| --- | --- | --- | --- | --- | --- | --- | --- |
| BCSM Event | M | M | M | M | M | M | This IE specifies the event or events for which a report is requested. |

BCSM Event contains the following information elements:

| Information element name | MO | MF | MT | VT | NC | NP | Description |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Event type | M | M | M | M | M | M | This IE specifies the type of event for which a report is requested. |
| Leg ID | C | C | C | C | C | M | This IE indicates the party in the call for which the event shall be armed or disarmed. |
| Monitor Mode | M | M | M | M | M | M | If this IE is "interrupted" then the event shall be reported as a request, if this IE is "notify and continue" then the event shall be reported as a notification, if this IE is "transparent" then the event shall not be reported. |
| DP Specific Criteria | O | O | O | O | O | O | This IE is described in a table below. |
| Automatic Rearm | O | - | - | O | - | - | This IE indicates that the detection point shall be automatically rearmed by the gsmSSF when it is encountered. This IE may be present only if the Event Type is O_Mid_Call, T_Mid_Call, O_Change_Of_Position or T_Change_Of_Position and the Monitor Mode is "notify and continue". |

DP Specific Criteria contains the following information elements:

| Information element name | MO | MF | MT | VT | NC | NP | Description |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Application Timer | O | O | O | O | O | O | This IE carries additional timer duration information (timer values for No_Answer event) required for arming the No_Answer EDPs in the gsmSSF. The TNRy timer (value defined between 10 seconds and 40 seconds) shall be shorter than the network no answer timer. |
| Mid Call Control Info | O | - | - | O | - | - | This IE is described in a table below. This IE carries the criterion for the detection and reporting of the mid-call event. If this IE is absent, then mid-call triggering shall take place when the first digit has been entered by the user. |
| Change of Position Control Info | O | - | - | O | - | - | This IE is described in a table below. It carries the list of criteria for the reporting of the change of position event. If the DP Specific Criteria IE is absent, then the criteria for any change of position shall be regarded as fulfilled. |
| NOTE If a Request Report BCSM Event information flow overwrites previous Request Report BCSM Event information flow which contained Application Timer IE for No_Answer DP, the behaviour of the gsmSSF is unpredictable. |

Mid Call Control Info contains the following information elements:

| Information element name | MO | MF | MT | VT | NC | NP | Description |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Minimum Number Of Digits | M | - | - | M | - | - | This IE indicates the minimum number of digits to be collected. The value of this IE includes the length of the Start digit string, if present, and the length of the End of reply digit string, if present. |
| Maximum Number Of Digits | M | - | - | M | - | - | This IE indicates the maximum number of digits to be collected. The value of this IE includes the length of the Start digit string, if present, and the length of the End of reply digit string, if present. If triggering takes place due to the detection of the maximum number of digits and the End of reply digit string, if present, is partially detected, then the partially detected End of reply digit string shall be included in the digit string to be reported to the gsmSCF. |
| End of Reply Digit String | O | - | - | O | - | - | This IE, if present, indicates the digit string that denotes the end of the digits to be collected. If triggering takes place due to the detection of the End of reply digit string, then this string shall be included in the digit string to be reported to the gsmSCF. If the interdigit timeout expires when the Start Digit String, if present, is complete and the Minimum Number Of Digits has been detected and the End Digit String, if present, has been partially detected then triggering shall take place. The partially detected End Of Reply Digit String shall be included in the string to be reported to the gsmSCF. |
| Cancel Digit String | O | - | - | O | - | - | This IE, if present, indicates the digit string that indicates that the input shall be erased and that digit collection, including the start digit string, if present, shall start afresh. |
| Start Digit String | O | - | - | O | - | - | This IE, if present, indicates the digit string that denotes the start of the digits to be collected. If this IE is absent, then the first digit entered forms part of the digits to be collected. When triggering takes place, then the Start digit string shall be included in the digit string to be reported to the gsmSCF. |
| Inter Digit Timeout | M | - | - | M | - | - | This IE indicates the maximum duration allowed between receipt of successive digits from the MS |

Change of Position Control Info contains a list of up to 10 instances of the following information element:

| Information element name | MO | MF | MT | VT | NC | NP | Description |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Change Of Location | M | - | - | M | - | - | Each Change Of Location IE is one of the 6 possibilities indicated in the table below. If multiple instances of the Change Of Location IE have the same value, this is not an error. |

Each instance of the Change Of Location IE contains one of the following information elements:

| Information element name | MO | MF | MT | VT | NC | NP | Description |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Cell Global ID | O,E | - | - | O,E | - | - | This IE indicates that the criteria are fulfilled if the mobile station performs handover across the boundary of the cell specified in this IE, i.e. handover into or out of the cell. |
| Service Area ID | O,E | - | - | O,E | - | - | This IE indicates that the criteria are fulfilled if the mobile station performs handover across the boundary of the service area specified in this IE, i.e. handover into or out of the service area. |
| Location Area ID | O,E | - | - | O,E | - | - | This IE indicates that the criteria are fulfilled if the mobile station performs handover across the boundary of the location area specified in this IE, i.e. handover into or out of the location area. |
| Inter-System Handover | O,E | - | - | O,E | - | - | This IE indicates that the criteria are fulfilled if the mobile station performs inter-system handover. |
| Inter-PLMN Handover | O,E | - | - | O,E | - | - | This IE indicates that the criteria are fulfilled if the mobile station performs inter-PLMN handover. |
| Inter-MSC Handover | O,E | - | - | O,E | - | - | This IE indicates that the criteria are fulfilled if the mobile station performs inter-MSC handover. |

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least three digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/ .
The list is also included in a MS Excel file included in the zip file containing the CR cover sheet template.

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2002.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. correction).

Enter the number of each clause which contains changes.

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.