| 3GPP TSG CN2 WG2 meeting | Document | N2-000136 |
| --- | --- | --- |
| Rotenburg, Germany, 22-26 Mai 2000 |  | e.g. for 3GPP use the format TP-99xxx or for SMG, use the format P-99-xxx |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 23.012 | CR | 006 | Current Version: | 3.2.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submission to: | CN#08 | for approval | X |  | strategic |  | (for SMG |
| list expected approval meeting # here ( | for information |  |  | non-strategic |  | Use only) |
| Form: CR cover sheet, version 2 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CR-Form-v2.doc |
| Proposed change affects: | (U)SIM |  | ME |  | UTRAN / Radio |  | Core Network | x |
| (at least one should be marked with an X) |
| Source: | Alcatel | Date: | 18/05/00 |
| Subject: | Introduction of Mobility Management event notification into 23.012 procedures |
| Work item: | Camel phase 3 |
| Category: | F Correction | X | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature |  |  | Release 97 |  |
| shall be marked | C Functional modification of feature |  |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 | x |
|  |  |  |  | Release 00 |  |
| Reason for change: | Introduction of Mobility Management event notification into 23.012 procedures. |
| Clauses affected: | Figure 4.1.2.1(sheet2 of 4), process Update_Location_Area_VLR Figure 4.1.2.1(sheet 4 of 4):process Update_Location_Area_VLR Figure 4.3.1.1(sheet 1 of 1): process Detach_IMSI_VLR |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: | This CR shall be read in page mode |

<--------- double-click here for help and instructions on how to create a CR.

## 1.1	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies.

- A non-specific reference to an ETS shall also be taken to refer to later versions published as an EN with the same number.

[1]	3G TS 21.905: "3G Vocabulary".

[2]	3G TS 23.002: "Network architecture".

[3]	3G TS 23.003: "Numbering, addressing and identification".

[4]	3G TS 23.007: "Restoration procedures".

[5]	3G TS 23.008: "Organization of subscriber data".

[6]	3G TS 23.022: "Functions related to Mobile Station (MS) in idle mode".

[7]	3G TS 23.116: "Super-Charger Technical Realisation; Stage 2".

[8]	3G TS 29.002: "Mobile Application Part (MAP) specification".

[9]	3G TS 29.007: "General requirements on interworking between the Public Land Mobile Network (PLMN) and the Integrated Services Digital Network (ISDN) or Public Switched Telephone Network (PSTN)".

[10]	GSM 03.20: "Digital cellular telecommunication system (Phase 2+); Security related network functions".

[11]	3G TS 23.078:”CAMEL phase3 – stage2 “

### 4.1.2	Detailed procedure in the VLR

#### 4.1.2.1	Process Update_Location_Area_VLR

General comment: at any stage in the location updating process the MSC may receive an indication from the BSS that the MM transaction has been released. The MSC then sends an Abort signal to the VLR. Upon receipt of this message, the VLR shall follow one of two possible courses of action.

The two possible courses of action and the conditions determining which course shall be taken are as follows:

- If a successfully authenticated radio connection is already established before the Abort message is received, the VLR shall ignore the message.

- If a successfully authenticated radio connection has not been established before the Abort message is received, the VLR shall abort the Update Location Area process and return to the idle state.

Sheet 1: the location area updating process will be activated by receiving an Update Location Area indication from the MSC. If there are parameter errors in the indication, the process is terminated with the appropriate error sent in the Update Location Area response to the MSC. Else, the behaviour will depend on the subscriber identity received, either an IMSI or a TMSI.

Sheet 2: at the decision "HLR updating required?" the "True" branch shall be taken if and only if one or more of the following conditions is true:

(1) Location Info Confirmed in HLR is false.

(2) Data Confirmed by HLR is false.

The type of Location Update is retrieved in 3G TS 23.078 procedure ‘Set_Notification_Type’ and is returned into the ‘Notify’ variable; this information is necessary for the CAMEL Mobility Management event notification procedure 3G TS 23.078 ‘Notify_gsmSCF’.

# Figure 4.1.2.1 (sheet 1 of 4): Process Update_Location_Area_VLR

# Figure 4.1.2.1 (sheet 2 of 4): Process Update_Location_Area_VLR

# Figure 4.1.2.1 (sheet 3 of 4): Process Update_Location_Area_VLR

# Figure 4.1.2.1 (sheet 4 of 4): Process Update_Location_Area_VLR

# Figure 4.1.2.1 (sheet 4 of 4): Process Update_Location_Area_VLR

### 4.3.2	Detailed procedure in the VLR

#### 4.3.2.1	Process Detach_IMSI_VLR

Sheet 1: The signal "Authenticated Radio Contact Terminated" is sent to Process Detach_IMSI_VLR from RR handling in the MSC whenever authenticated radio contact is terminated, e.g. at the release of a call.

The 3G TS 23.078 procedure ‘Notify_gsmSCF’ with ‘Notify’ variable set either to ‘explicit’ or to ‘implicit detach’ allows the handling of CAMEL Mobility Management events notification.

# Figure 4.3.1.1 (Sheet 1 of 1): Process Detach_IMSI_VLR

# Text boxes

Notify_gsmSCF with Notify =explicit or implicit IMSI detach

3G TS 23.078