3GPP TSG-N2 #4

Seattle, USA

28 Aug – 1 Sep 2000

# Tdoc 3GPP N2-000404
revision of N2-000361

To: 	TSG-N4

From: 	TSG-N2

Title:	LS on CAMEL control of Optimal Routeing

WI:		CAMEL Phase 4

Source:	Vodafone

TSG-S1 agreed a CR to TS 22.078 stating that

"…

When a subscriber who is provided with CAMEL based services originates a call, the CSE shall be able to instruct VPLMN-A to interrogate a remote HPLMN for information to route the call to the destination mobile subscriber, instead of using the destination address to route the call to the HPLMN of the destination mobile subscriber.

…"

The technical realisation of this is as follows:

On receipt of an Initial DP for an MO call, the gsmSCF can determine whether Basic Optimal Routeing could be applied for the call. If Basic Optimal Routeing could be applied, the gsmSCF sends a Basic OR interrogation requested indicator in either the Connect or Continue With Argument message. On receipt of this indication, the VMSC routes the call to a GMSC which sends an SRI to the called party's HLR.

It is anticipated that this feature will require changes to TS 23.018, TS 23.078, TS 23.079 and TS 29.078. The change requests to TS 23.078 and TS 29.078 incorporate the Basic OR interrogation requested indicator in the Connect and Continue With Argument messages.

The remainder of the work for this feature falls under TSG-N4's remit. TSG-N2 asks TSG-N4 to work on this feature for completion in Release 2000.

# Footnotes

Contact: Ian Park, tel: +44 1635 673 527, email: ian.park@vf.vodafone.co.uk