Source:	Lucent Technologies

Title:	Suggestion for Detailed Parameter Mapping from CAMEL-to-API

in TR29.998

Agenda item:	API Mapping

Document for:	Approval

# Introduction

The Technical Report 3G TR 29.998 proposes a mapping from OSA API methods to CAP and MAP protocol operations and their parameters. Version 1.0.0 of this TR was presented at the TSG-CN#7 Plenary which took place in Madrid from the 13th till 17th of March. The CN Plenary has decided to accept OSA for Release 99, but to extend its approval to the TSG-CN#8 Plenary, which will take place in Dusseldorf on 21st till the 23rd of June.

Whereas Tdoc N5-000013 deals with potential issues and problems with the parameter mapping, this paper suggests more detailed parameter mappings in cases where it is possible to convey all possible values for the CAP and MAP parameters to the applications.

Lucent would like to kindly request CN5 to review these detailed parameter mappings and approve that these be added to TR 29.998.

# TpCallSuperviseTreatment: to be included in part 2.

The treatment parameter of superviseCallReq can carry all possible treatment values of the timeDurationCharging element of AchBillingChargingCharacteristics in the CAP ApplyCharging operation.

| TpCallSuperviseTreatment | timeDurationCharging |
| --- | --- |
| P_CALL_SUPERVISE_RELEASE | releaseIfDurationExceeded |
| P_CALL_SUPERVISE_RESPOND |  |
| P_CALL_SUPERVISE_APPLY_TONE | tone |

# TpAocInfoL: By CR

The aOCInfo parameter of setAdviceOfCharge can carry all possible values of the SCIBillingChargingCharacteristics parameter in the CAP SendChargingInformation operation.

| TpAocInfo | SCIBillingChargingCharacteristics |
| --- | --- |
| AoCSet1 | AOCBeforeAnswer |
| AoCSet2 | aOCAfterAnswer |

# TpCallFaultDetected: ok

The fault parameter of callFaultDetected can carry all possible values of the TC Primitive.

| TpCallFault | TC Primitive |
| --- | --- |
| P_CALL_FAULT_UNDEFINED |  |
| P_CALL_FAULT_USER_ABORTED | TC_U_ABORT |
| P_TIMEOUT_ON_RELEASE |  |
| P_TIMEOUT_ON_INTERRUPT |  |

# TpUIResponseRequested: more detailed mapping by CR see also TD13.

The responseRequested parameter of sendInfoReq can carry all possible values of the RequestAnnouncementComplete parameter of the CAP PlayAnnouncement operation.

| TpUIResponseRequested |  |
| --- | --- |
| P_UI_RESPONSE_REQUIRED | RequestAnnouncementComplete |
| P_UI_LAST_ANNOUNCEMENT_IN_A_ROW |  |
| P_UI_FINAL_REQUEST |  |