TDoc N5-000024

Title: 	Comparison of defined methods and parameters in 
Stage 2 and Stage 3 Revision 2, dated 7/3/00

Agenda Item:		‘VHE/OSA’

Source:			Ericsson

Document for:		Discussion / Decision

# Introduction

A comparison has been made between methods and parameters specified in the latest drafts of the VHE/OSA stage 2 and stage 3 documents. The documents used in the comparison are:

Stage 2: 	all		23.127 v.1.3.0 			(dated 2000-02-28)

Stage 3:	Framework	3G TS 23.xxx version 1.4.0	(dated 2000-02-22)
		Common	3G TS 29.xxx version 0.2.0 	(dated 2000-02-18)
 		Call control		  “”     version 0.4.0	(dated 2000-02-22)
 		Location		  “”     version 0.1.0	(dated 2000-01-23)

The result is listed in the following sections. The document is structured as follows:

- framework SCF related methods and parameters

- network SCF related methods and parameters

Within these sections, the different SCF’s are identified. The differences are marked in bold. If a difference between S2 and S3 is identified, this is reported from the perspective of the stage 2 document.

Dated 7/3/00:

After the request made to S3, to propose a resolution of the differences mentioned in this document, the S3 meeting produced two sets of documents: a new S3 spec and a new proposed S2 spec:

- S3 documents: OSA-00120.doc and TR 29.9xx_v0.3.0.doc

- S2 documents: OSA-00104, sent as part of S2-000500.doc

Unfortunately, not all the differences mentioned in this document are resolved in the above mentioned S2- and S3 documents. I have been going through the list again, and comparing whether the changes have been made, and to which stage they have been proposed (S2 or S3). The result of this exercise is shown in the following document in red and green comments.

A red comment indicates a difference between S2 and S3, still to be resolved. A green comment indicates a resolved difference.

# Framework SCF method- and parameter comparison

## Initial Contact

| Method/Params | Stage 2 | Stage 3 |
| --- | --- | --- |
| method | initiateAuthentication | initiateAuthentication |
| params | clientAppID fwAuthInterface | ClientAPPID fwAuth not changed in S2 or S3 |

## Service Discovery

| Method/Params | Stage 2 | Stage 3 |
| --- | --- | --- |
| method | listSubscribedServices | listSubscribedServices |
| params | serviceIDList | serviceList not changed in S2 or S3 |

## Load Manager already aligned

| Method/Params | Stage 2 | Stage 3 |
| --- | --- | --- |
| method | disableLoadControl | disableLoadControl |
| params | ServiceIds | serviceIDs not changed in S2 or S3 |
| method | queryLoadReq | queryLoadReq |
| params | serviceIds | serviceIDs not changed in S2 or S3 |
| method | queryAppLoadReq | queryAppLoadReq |
| params | serviceIds | serviceIDs not changed in S2 or S3 |
| method | registerLoadController | registerLoadController |
| params | serviceIds | serviceIDs not changed in S2 or S3 |
| method | unregisterLoadController | unregisterLoadController |
| params | serviceIds | serviceIDs not changed in S2 or S3 |
| method | resumeNotification | resumeNotification |
| params | serviceId | serviceIDs not changed in S2 or S3 |
| method | suspendNotification | suspendNotification |
| params | serviceId | serviceIDs not changed in S2 or S3 |

## Fault Manager change required for stage 3

| Method/Params | Stage 2 | Stage 3 |
| --- | --- | --- |
| method | svcUnavailableInd | serviceUnavailableInd not changed in S2 or S3 |
| params | serviceID | serviceId not changed in S2 or S3 |
| method | svcUnavailableInd | svcUnavailableInd not changed in S2 or S3 |
| params | serviceID | serviceId not changed in S2 or S3 |
| method | genFaultStatsRecordRes | genFaultStatsRecordRes |
| params | serviceIDList | serviceIDs not changed in S2 or S3 |

## Hearbeat Management: change in stage 3

| Method/Params | Stage 2 | Stage 3 |
| --- | --- | --- |
| method | enableAppHeartBeat | enableAppHeartBeat |
| params | appInterface | interface not changed in S2 or S3 |

# Network SCF method- and parameter comparison

## Call Manager

| Method/Params | Stage 2 | Stage 3 |
| --- | --- | --- |
| method | disableCallNotification | disableCallNotification |
| params | EventCriteria stage 2 cr | not present not changed in S2 or S3 |
| method | callEventNotify | callEventNotify |
| params | call | callReference changed in S2 |
| method | allAborted (should probably be callAborted) | callAborted |
| params | call callSessionID stage 2 cr to be made | callSessionID now called callReference in S3 doc. not changed in S2 |
| method | routeCallToDestination_Req stage 2 cr to be made | routeCallToDestinationReq not changed in S2 or S3 |
| method | routeCallToDestination_Res stage 2 cr to be made | routeCallToDestinationRes not changed in S2 or S3 |
| params | stage 2 cr to be made | extra parameter: assignmentID not changed in S2 or S3 |
| method | routeCallToDestination_Err stage 2 cr to be made | routeCallToDestinationErr not changed in S2 or S3 |
| params | Error | errorIndication changed in S2 |
| params | stage 2 cr to be made | extra parameter: assignmentID not changed in S2 or S3 |
| method | getCallInfo_Req stage 2 cr to be made | getCallInfoReq not changed in S2 or S3 |
| method | getCallInfo_Res stage 2 cr to be made | getCallInfoRes not changed in S2 or S3 |
| method | getCallInfo_Err stage 2 cr to be made | getCallInfoErr not changed in S2 or S3 |
| params | error | errorIndication changed in S2 |
| method | superviseCall_Req stage 2 cr to be made | superviseCallReq not changed in S2 or S3 |
| params | CallSessionID duration tariffSwitch treatment | callsessionID time treatment bytes changed in S2 |
| method | superviseCall_Res stage 2 cr to be made | superviseCallRes not changed in S2 or S3 |
| params |  | extra parameter: usedVolume (added in S2) bytes (removed in S3) changed in S2 and S3 |
| method | superviseCall_Er stage 2 cr to be made r | superviseCallErr not changed in S2 or S3 |
| params | error | errorIndication changed in S2 |
| method | callFaultDetected stage 2 cr to be made | callFaultDetected |
| params | call | not present changed in S2 |
| method |  | extra methods: createCall routeCallToOriginationReq routeCallToOriginationRes routeCallToOriginationErr changed in S3 (removed) |

## User Interaction

| Method/Params | Stage 2 | Stage 3 |
| --- | --- | --- |
| method | userInteractionAborted | userInteractionAborted |
| params | userInteractionIdentifier | userInteraction changed in S2 |
| method | sendInfoErr | sendInfoErr |
| params | error | errorIndication changed in S3 |
| method | sendInfoAndCollectReq | sendInfoAndCollectReq |
| params | infoID response stage 2 cr | info responseRequested not changed in S2 or S3 |
| method | userInteractionFaultDetected | userInteractionFaultDetected |
| params | userInteractionIdentifier | userInteractionSessionID changed in S2 |
| method |  | extra methods: recordMessageReq recordMessageRes recordMessageErr changed in S3 (removed) |

## Charging

All methods seem to be missing in stage 3 already taken care off..

## Network  User Location

| Method/Params | Stage 2 | Stage 3 |
| --- | --- | --- |
| method | locationReportReq | locationReportReq |
| params | appLocationCamel | appLocationNetwork changed in S3 |
| method | periodicLocationReportingStartReq | periodicLocationReportingStartReq |
| params | appLocation stage 2 cr request | appLocationNetwork S3 changed this into: appLocationCamel not present changed in S3 (removed) |
| method | triggeredLocationReportingStartReq | triggeredLocationReportingStartReq |
| params | appLocation request triggers stage 2 cr to be made | appLocationNetwork S3 changed this into: appLocationCamel not present not changed in S2 or S3 trigger not changed in S2 or S3 |

## User Status

all OK

## Terminal Capabilities

Missing in stage 3 docs. Already  fixed