# 3GPP TSG CT WG1 Meeting 125-e	TDoc C1-205xxx

# Electronic meeting, 20-28 August 2020

Title:	LS on clarifications for on-network MCVideo recording capability applicabality

Response to:

Release:	Release 17

Work Item:	MCProtoc17

Source:	3GPP TSG CT WG1

To:	3GPP TSG SA WG6

Cc:

Contact Person:

#### Name:	Kiran Kapale

Tel. Number:	+919886088631

E-mail Address:	kiran dot kapale at samsung dot com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:

1. Overall Description:

CT1 is working on MCVideo enhancements for Rel-17 and one major area of focus is sharing current status of MCVideo UE activity (e.g. receiving video, transmitting video, or recording video) between the members of a selected group. We have found the following relevant requirements from Stage 1 22.281 and  Stage 2 23.281:

3GPP TS 22.281:

[R-5.1.8.2-002] Subject to permissions and authorizations, the MCVideo service shall provide a means to share current status of MCVideo UE activity (e.g. receiving video, transmitting video, or recording video) between the members of a selected group.

3GPP TS 23.281:

7.5.3.2.4	Activity status announcement

Table 7.5.3.2.4-1 describes the information flow for the activity status announcement sent from the MCVideo client to other MCVideo client(s).

| Information Element | Status | Description |
| --- | --- | --- |
| Activity status | M | Current status of MCVideo UE's activities (e.g. receiving video, transmitting video, or recording video) |

CT1 would like to get clarifications from SA6 for the following issues:

- In stage 2, the UE activity procedures included in off-network case although the stage -1 requirement doesn’t explicitly say that it’s applicable only to off-network. We CT1 group would like to get the clarification that whether similar capabaility of sharing UE activity is applicable or expected in on-network?

- The stage 2, has already implemented the activities such as receiving media and transmitting media but not the recording video. The off-network and on-network has both transmitting media and receiving media activity status announcement in a call but no indication of recording.

- If SA6 agrees that it is required then CT1 can continue the work to implement it ?

CT1 thanks SA6 to provide clarifications for the above issues in a timely manner so that appropriate MCVideo enhancements in Release 17 can be developed.

2. Actions:

To SA1 group.

ACTION: 	CT1 asks SA6 to kindly provide clarifications on the issues listed above to help guide CT1 in MCVideo stage 3 Technical Specification development.

3. Date of Next SA6 Meetings:

CT1#126 15th – 23th October 2020	e-meeting