3GPP TSG-CT WG1 Meeting #126-e	C1-205912

# Electronic meeting; 15-23 October 2020

Source:	Qualcomm Incorproated

Title:	Key Issue #2: LI requirements

Spec:	3GPP TR 24.821

Agenda item:	17.2.4

Document for:	Agreement

1. Introduction

This contribution proposed to add Key Issue #2: LI requirements to TR 24.821

2. Reason for Change

In [1], SA3-LI has established the requirement to “enforce the use of a Core Network of PLMN in the country where the UE is physically located”. Based on this requirement, the selected PLMN must be in the country of the UE location.

An important thing to note is that the requirement that the selected PLMN must have a core network in the same country may be impossible to satisfy during PLMN selection procedure because the UE has no way of knowing the location of the core network of a PLMN. The core network location verification can take place during the registration procedure (by AS or NAS). However, from the protocol efficiency and resource utilization efficiency point of view, the UE should still select a PLMN in a way that minimizes the possibility of registration rejection due to wrong country.

The LI requirement above does not apply to PLMN selection in international areas (e.g. international waters and airspace).

PLMN selection for satellite access, the selection of a PLMN in the country of the UE’s physical location is a valid issue for which the solution needs to be provided.

3. Proposal

It is proposed to agree the following changes to 3GPP TS 24.821.

4. References

[1]	S3i200056 Response LS on the “LS OUT on Location of UEs and associated key issues”

* * * First Change * * * *

## 5.2	Key issue #2: LI requirements

In [1], SA3-LI has established the requirement to “enforce the use of a Core Network of PLMN in the country where the UE is physically located”.

The requirement that the selected PLMN must have a core network in the same country may be difficult to satisfy during PLMN selection procedure. The core network location verification can take place during the registration procedure (by AS or NAS). However, from the protocol efficiency and resource utilization efficiency point of view, the UE should still select a PLMN in a way that minimizes the possibility of registration rejection due to wrong country.

The following questions are expected to be studied within this key issue:

-	how the UE determines which PLMN(s) can be selected in determined country of its physical location (if it is determined that the UE is not in an international area);

-	what information could be available to the UE to help in selecting, in a given country, a PLMN that meets the LI requirements of that country:

-	pre-configured in the UE; and

-	provided by PLMN;

-	what modifications are needed, if any, to the PLMN selelction procedure to take the LI requirement into account.

The LI requirement above does not apply to PLMN selection in international areas (e.g. international waters and airspace). Hence this key issue is not relevant for international areas.

This key issue is related to Key issue #1.