3GPP TSG-CT WG1 Meeting #126-e	C1-206303

# Electronic meeting; 15-23 October 2020

Source:	Huawei, HiSilicon

Title:	Key issue on Routing of IMS traffic via a localized UPF

Spec:	3GPP TR 23.700-10 v0.0.0

Agenda item:	17.3.3

Document for:	Agreement

1. Introduction

<Introduction part >

2. Reason for Change

This pCR proposes to introduce a key issue on Routing of IMS traffic via a localized UPF. This key issue is based on the key issue 1 of TR 23.794.

3. Conclusions

<Conclusion part (optional)>

4. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-10 v0.0.0.

* * * First Change * * * *

## 5.x	Key issue #X: Routing of IMS traffic via a localized UPF

### 5.x.1	Description

The 5GC enables traffic to route via localized UPF close to the edge of the network (in some cases adjacent to the RAN nodes). Some services offered by the IMS network may be able to benefit from the lower latency and/or lower backhaul requirements that such deployments can enable, however current IMS applications and services are not able to leverage these capabilities. This key issue investigates the interactions required to leverage localized routing of IMS media and signalling traffic, the changes to enable effective control and management of such routing, and impacts of mobility and roaming.

### 5.x.2	Requirements

Example Use Case A:

Routing of IMS traffic (e.g. video) between two (or more) users using an efficient UP path.

Example Use Case B:

A "best effort video service" where the IMS video traffic from UE is offloaded at a UPF closer to the UE to minimize the backhaul resource usage based on a decision by the IMS.

The following is a partial list of the issues to be addressed:

-	How can the IMS network influence or control how the 5GC selects the UP path.

-	Which IMS node interacts with the 5GC (i.e. IMS AS, S-CSCF, or other IMS node).

-	How does an AS request traffic to route using a local UPF.

-	How does IMS request traffic to route using (or prevent routing using) a local UPF.

-	How is the mobility of the UE considered, and how is service continuity ensured.

-	If the UE is roaming, how can the localized routing be extended into the VPLMN (if supported).

-	How does IMS request Data channel media to route using (or prevent using) a local UPF.

* * * End of Change * * * *