3GPP TSG-CT WG1 Meeting #126-e	C1-206312

Electronic meeting, 15-23 October 2020

| CR-Form-v12.0 |
| --- |
| CHANGE REQUEST |
|  | 23.122 | CR | 0611 | rev | - | Current version: | 17.0.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps | X | ME | x | Radio Access Network |  | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Initial CAG information list |
| --- | --- |
| Source to WG: | Ericsson |
| Source to TSG: | C1 |
| Work item code: | 5GProtoc17 |  | Date: | 2020-10-07 |
| Category: | B |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | As discussed during CT1#125-e, there is a deployment demand to enable a UE supporting CAG but without CAG information list to access a CAG cell in automatic network selection mode to get the up-to-date CAG information list: 1. Special industrial MEs cannot be pre-configured with CAG information list when leaving factory, as it’s an operator dependent information. 2. These special industrial MEs cannot camp on a non-CAG cell to get CAG information list, as machine-only zones are not permitted to deploy non-CAG cell and thus non-CAG cell are not available to these MEs. 3. These special industrial MEs arrive in batches irregularly.The dates are business sensitive information.The customers disagree to notify the operator to do the configuration of these MEs for every purchase. 4. Manual selection mode is seen as unsafe factor by customers. The above demand can be solved by: - enabling HPLMN to configure the initial CAG information list in the USIM; and - enabling the ME to configure the CAG information list stored in the ME with the initial CAG information list stored in the USIM when a new USIM is inserted. |
| Summary of change: | The "initial CAG information list" can be stored in the USIM. When a new USIM is inserted, if the "initial CAG information list" is stored in the USIM, the ME supporting CAG configures the "CAG information list" stored in the ME with the "initial CAG information list" stored in the USIM. |
| Consequences if not approved: | The deployment demand not met. |
| Clauses affected: | 3.8 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |
| This CR's revision history: |  |

***** change *****

## 3.8	CAG selection (N1 mode only)

The MS may support CAG.

If the MS supports CAG, the ME of the MS can store a "CAG information list", consisting of zero or more entries, each containing:

a)	a PLMN ID;

b)	an "Allowed CAG list". The "Allowed CAG list" contains zero or more CAG-IDs; and

c)	an optional "indication that the MS is only allowed to access 5GS via CAG cells".

The "CAG information list" stored in the ME is kept when the UE enters 5GMM-DEREGISTERED state. The "CAG information list", if available, is stored in the non-volatile memory in the ME as specified in annex C of 3GPP TS 24.501 [x]. This "CAG information list" stored in the ME is deleted when the USIM is changed or removed.

NOTE 	When the UE is registering or registered to a PLMN other than the HPLMN, a PLMN equivalent to the HPLMN or EHPLMN, then the HPLMN will send a "CAG information list" consisting of CAG subscription information related to the serving PLMN only. When the UE is registering or registered to the HPLMN, a PLMN equivalent to the HPLMN or EHPLMN then the HPLMN or EHPLMN may send CAG subscription information related to any PLMN in the "CAG information list".

The USIM can be provisioned with a "CAG information list", consisting of zero or more entries, each containing:

a)	a PLMN ID;

b)	an "Allowed CAG list". The "Allowed CAG list" contains zero or more CAG-IDs; and

c)	an optional "indication that the MS is only allowed to access 5GS via CAG cells".

If both a "CAG information list" stored in the ME and a "CAG information list" provisioned in the USIM are available, the MS shall ignore the "CAG information list" provisioned in the USIM.

If the MS supports CAG and a PLMN is selected as described in subclause 4.4.3.1.1, the automatic CAG selection is performed as part of subclause 4.4.3.1.1.

If the MS supports CAG and a PLMN is selected as described in subclause 4.4.3.1.2, the manual CAG selection is performed as part of subclause 4.4.3.1.2.

The NAS shall provide the AS with a "CAG information list", if available. If the contents of the "CAG information list" have changed, the NAS shall provide an updated "CAG information list" to the AS.