# 3GPP TSG CT WG1 Meeting 126-e	TDoc C1-206507

# Electronic meeting, 15-23 October 2020

Title:	New RAT type(s) for satellite access for PLMN selection

Response to:	-

Release:	Rel-17

Work Item:	5GSAT_ARCH-CT

Source:	CT1

To:	SA1

Cc:	SA2

Contact person:	Amer Catovic

amerc@qti.qualcomm.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	none

# 1	Overall description

CT1 is working on the TR 24.821 Study on PLMN selection for satellite access. One of the key issues in the TR is handling of new RAT type(s) for satellite access. SA2 has agreed on introducing new RAT types for satellite access: NR(LEO), NR(MEO), NR(GEO) and NR(OTHERSAT).

CT1 would like to ask the following questions to SA1:

Question 1: Should the PLMN selection procedure consider whether a PLMN supports a satellite RAT or not, e.g. allow for PLMN prioritization that considers PLMN support for satellite RAT type(s)?

Question 2: If the answer to Question 1 is yes, is there a need to differentiate the four satellite RAT types defined by SA2 in the PLMN selection procedure?

# 2	Actions

To SA1

ACTION: 	3GPP CT WG1 kindly asks SA1 group to provide the answers to the above questions.

# 3	Dates of next TSG CT WG1 meetings

TSG CT WG1 Meeting 127e (electronic)	13-20 November 2020

TSG CT WG1 Meeting 127-bis-e (electronic)	25-29 January 2021