# 3GPP TSG CT WG1 Meeting 126-e	TDoc C1-206507

# Electronic meeting, 15-23 October 2020

Title:	New satellite radio access technologies for PLMN selection

Response to:	-

Release:	Rel-17

Work Item:	5GSAT_ARCH-CT

Source:	CT1

To:	SA1

Cc:	SA2

Contact person:	Amer Catovic

amerc@qti.qualcomm.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	none

# 1	Overall description

CT1 is working on the TR 24.821 Study on PLMN selection for satellite access. SA2 has agreed on introducing new Core Network RAT types for satellite access: NR(LEO), NR(MEO), NR(GEO) and NR(OTHERSAT) for use within 5G core network.

CT1 would like to ask the following questions to SA1:

Question 1: Is there a service requirement to differentiate between “NG-RAN” and “satellite access to 5GC" for the purpose of PLMN selection?

Question 2: Does SA1 intend to introduce new associated Access Technology identifier(s) for "satellite access" for the Operator Controlled PLMN Selector list and a User Controlled PLMN Selector list (stored on the SIM/USIM card). If yes, how many different identifiers?

# 2	Actions

To SA1

ACTION: 	3GPP CT WG1 kindly asks SA1 group to provide the answers to the above questions.

# 3	Dates of next TSG CT WG1 meetings

TSG CT WG1 Meeting 127e (electronic)	13-20 November 2020

TSG CT WG1 Meeting 127-bis-e (electronic)	25-29 January 2021