3GPP TSG-CT WG1 Meeting #127-e	C1-207107

Electronic meeting, 13-20 November 2020

| CR-Form-v12.0 |
| --- |
| CHANGE REQUEST |
|  | 23.122 | CR | 0625 | rev | - | Current version: | 17.0.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps | X | ME | x | Radio Access Network |  | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | [Solution Option 2.4] Initial CAG information list stored in the USIM and CAG-access-indication in CAG information list |
| --- | --- |
| Source to WG: | Mediatek Inc., China Mobile |
| Source to TSG: | C1 |
| Work item code: | 5GProtoc17 |  | Date: | 2020-11-05 |
| Category: | B |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | As discussed in CT1-124e, Due to the following limitations,there is a deployment demand to enable a UE supporting CAG but without CAG information list to access a CAG-only cell in the automatic network selection mode: The special industrial terminals cannot be pre-configured with CAG information list stored in the ME when leaving factory.(It’s an operator dependent information.) They cannot be moved to a non CAG-only cell to get CAG information list. (Due to transportation issue of, e.g., heavy machinery; or privacy issue, e.g., machine-only zones are not permitted to deploy non CAG-only cell. These terminals arrive in batches irregularly.The dates are business sensitive information.The PNI-NPN customers disagree to notify the operator to do customized configuration for every purchase. Manual operation(such as manual selection mode) are regarded as unsafe/risky factor by customers. It is discussed in CT1-126e that one way to address this use case is to enable the storage of a pre-configured "CAG information list" in the USIM (e.g., C1-206733). However with this approach there are still additional concerns from operators: Additional concern 1) It is difficult to predict and pre-configure different number of CAG-IDs into different number of USIMs based on different customers' requirements in advance. Additional concern 2) It is technically correct and theoretically feasible that an operator can define a CAG-ID as proprietary "default CAG-ID" (e.g., operator A can define 0xFFFFFFFF as "default CAG-ID" while operator B can define 0x00000000 as "default CAG-ID"), and an operator can pre-configure all PNI-NPN USIMs having its "default CAG-ID" and configure all/partial CAG cells to broadcast the "default CAG-ID". However this technically correct and theoretically feasible soltuion is not practically feasible (does not meet the real deployment requirements) from some operaotrs’ view (see C1-20XXXX discussion paper for further detail). To further satisfy operators practical deployment requirements, based on the solution specified in e.g., C1-206733, additionally a new "CAG-access-indication" is added in the entry of "CAG information list". This new indication, if configured, makes the UE able to access all available CAG-IDs it can find from HPLMN cells, which can better meet the requirements of real-field PNI-NPN deployment. |
| Summary of change: | 1. The "CAG information list" can be stored in USIM (same/similar as C1-206733) 2. When a USIM is inserted, if the UE has a "CAG information list" stored in the USIM, the UE copies the "CAG information list" from the USIM to the ME. (same/similar as C1-206733) 3. New "CAG-access-indication" is added into the entry of "CAG information list". (new, also can be merged into new revision of C1-206733) |
| Consequences if not approved: | A device not configured with any CAG information list in automatic network selection mode cannot receive a CAG information list from a CAG cell. |
| Clauses affected: | 3.8 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |
| This CR's revision history: |  |

***** change *****

## 3.8	CAG selection (N1 mode only)

The MS may support CAG.

If the MS supports CAG, the MS can be provisioned by the network with a "CAG information list". In addition, the MS can be pre-configured with a "CAG information list" stored in the USIM (see 3GPP TS 31.102 [40]).

Editor's note (WI 5GProtoc17, CR#0625):	"CAG information list" stored in the USIM is to be specified by CT6.

The "CAG information list" consists of zero or more entries, each containing:

a)	a PLMN ID;

b)	an "Allowed CAG list". The "Allowed CAG list" contains zero or more CAG-IDs;

c)	an optional "indication that the MS is only allowed to access 5GS via CAG cells"; and

d)	an optional "CAG-access-indication".

NOTE X:	In this release of specification, the "CAG-access-indication" is only applicable for the pre-configured "CAG information list" in the USIM.

The "CAG information list" provisioned by the network is stored in the ME.

NOTEX:	When the MS is registering or registered to a PLMN other than the HPLMN, a PLMN equivalent to the HPLMN or EHPLMN, then the HPLMN will send a "CAG information list" consisting of CAG subscription information related to the serving PLMN only. When the MS is registering or registered to the HPLMN, a PLMN equivalent to the HPLMN or EHPLMN then the HPLMN or EHPLMN may send CAG subscription information related to any PLMN in the "CAG information list".When a USIM is inserted, if:

-	no "CAG information list" is stored in the non-volatile memory of the ME as specified in 3GPP TS 24.501 [64] annex C; or

-	the SUPI from the USIM does not match the SUPI stored together with the "CAG information list" in the non-volatile memory of the ME as specified in 3GPP TS 24.501 [64] annex C;

and the MS has a "CAG information list" stored in the USIM (see 3GPP TS 31.102 [22]), the MS shall delete the "CAG information list" stored in the ME, if any, and store the "CAG information list" from the USIM in the ME as specified in 3GPP TS 24.501 [64] annex C.

NOTE X:	The MS ignores the "CAG information list" stored in the USIM except when the USIM is inserted.

If the MS supports CAG and a PLMN is selected as described in subclause 4.4.3.1.1, the automatic CAG selection is performed as part of subclause 4.4.3.1.1.

If the MS supports CAG and a PLMN is selected as described in subclause 4.4.3.1.2, the manual CAG selection is performed as part of subclause 4.4.3.1.2.

The NAS shall provide the AS with a "CAG information list", if available. The "CAG-access-indication" is not provided to the AS; when the automatic CAG selection is performed, if for an entry in the "CAG information list" the "CAG-access-indication" is included and:

a)	the PLMN of the entry is HPLMN;

b)	the "Allowed CAG list" in the entry does not contain any CAG-ID; and

c)	there exists available CAG cell(s) (reported from AS to NAS as specified in 3GPP TS 38.304 [61] subclause 5.1.1) of the PLMN of the entry;

the NAS replaces the "Allowed CAG list" in the entry with CAG-ID(s) from existing available CAG cell(s) before the "CAG information list" is provided to the AS.

If the contents of the "CAG information list" have changed, the NAS shall provide an updated "CAG information list" to the AS.

***** end of change *****