# 3GPP TSG CT WG1 Meeting 126-e	TDoc C1-205945

# Electronic meeting, 15-23 October 2020

Title:	LS on MINT requirements

Release:	Rel-17

Work Item:	MINT

Source:	CT1

To:	SA1

Cc:	SA2

Contact person:	Lena Chaponniere

lguellec@qti.qualcomm.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	None

# 1	Overall description

CT1 has agreed a Rel-17 Study Item on MINT (TBC) and has started discussing the related requirements. As a result of this discussion, CT1 would like to ask SA1 the following questions:

Question 1: Which level of services are the PLMNs not subject to disaster required to provide to “Disaster Inbound Roamers”? Emergency services only, a limited set of services hosted by the PLMN not subject to disaster (e.g. internet connectivity provided using local break-out), or the same set of services that the “Disaster Inbound Roamers” would receive in their HPLMN?

Question 2: If the answer to Question 1 is: a limited set of services hosted by the PLMN not subject to disaster, can it be assumed that the NFs of the PLMM subject to disaster required to support those services (the UDM and the AUSF) are still operational?

Question 3: If the answer to Question 1 is: the same set of services that the “Disaster Inbound Roamers” would receive in their HPLMN, can it be assumed that the NFs of the PLMM subject to disaster required to support those services (the UDM, the AUSF, the SMF and UPF for any DNN requiring home-routed PDU session, and the IMS) are still operational?

# 2	Actions

To SA1

ACTION: 	3GPP TSG CT WG1 asks SA1 group to provide answers to Questions 1, 2 and 3 above.

# 3	Dates of next TSG CT WG1 meetings

TSG CT WG1 Meeting 127e (electronic)	13-20 November 2020

TSG CT WG1 Meeting 127-bis-e (electronic)	25-29 January 2021