# 3GPP TSG CT WG1 Meeting 126-e	TDoc C1-20xxxx

# Electronic meeting, 15-23 October 2020

Title:	LS on Cell Configuration within TA/RA to Support Allowed NSSAI

Response to:	LS S2-2006526/C1-205894 on Cell Configuration within TA/RA to Support Allowed NSSAI from SA2

Release:	Rel-17

Work Item:	FS_eNS_Ph2

Source:	CT1

To:	SA2

Cc:	RAN2, RAN3

Contact person:	Sung Hwan WON

sung.won@nokia.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	-

# 1	Overall description

CT1 would like to thank SA2 for the LS, which includes Questions 1), 2a), and 2b) where Questions 2a) and 2b) are valid if the answer to Question 1) is “no.”

CT1’s answer to Question 1) is as follows:

Based on information from SA2 in S2-1811546 (copied below), CT1 has assumed that all S-NSSAIs in the allowed NSSAI are supported in all tracking areas of the registration area even if the registration area includes tracking areas belonging to multiple PLMNs (that are equivalent to each other).

Text in S2-1811546 The Allowed NSSAI is applicable for the Registration Area which may include PLMNs from one or more PLMNs. It is required that these PLMNs have the same network slicing configuration for the S-NSSAIs in the Allowed NSSAI at least. It is also assumed these are equivalent PLMNs.

It is noteworthy that CT1 did not discuss the possibility of inhomogeneous support of S-NSSAIs across the cells of a tracking area In Rel-15/16.

CT1’s answer to Questions 2a) and 2b) is as follows:

Since CT1’s answer to Question 1) is not “no,” CT1 decided not to provide an answer to Questions 2a) and 2b).

# 2	Actions

To SA2

ACTION: 	CT1 kindly asks SA2 to take the answers in this LS into account.

# 3	Dates of next TSG CT WG1 meetings

TSG CT WG1 Meeting 127e (electronic)	13-20 November 2020

TSG CT WG1 Meeting 127-bis-e (electronic)	25-29 January 2021