3GPP TSG-CT WG1 Meeting #126-e	C1-20aabb

Electronic meeting, 15-23 October 2020                                                   was C1-206438

| CR-Form-v12.0 |
| --- |
| CHANGE REQUEST |
|  | 24.501 | CR | 2814 | rev | 1 | Current version: | 17.0.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Deregistration before initial registration in SNPN selection |
| --- | --- |
| Source to WG: | MediaTek Inc. |
| Source to TSG: | C1 |
| Work item code: | 5GProtoc17 |  | Date: | 2020-10- |
| Category: | F |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) Rel-17 (Release 17) |
| Reason for change: | As per Section 5.2.3.2.5,(5GMM-REG.PLMN-SEARCH) The UE shall perform PLMN selection or SNPN selection. If a new PLMN is selected, the UE shall reset the registration attempt counter and initiate a registration procedure for mobility and periodic registration update (see subclause 5.5.1.3). If a new SNPN is selected, the UE shall reset the registration attempt counter and initiate a registration procedure for initial registration (see subclause 5.5.1.2.2). In REG state, UE should perform deregistration to perform initial registration since initial registration is possible in DEREG state. |
| Summary of change: | Clarification about de-registration locally before initiating a initial registration in SNPN selection |
| Consequences if not approved: | Inconsistency in current spec. may lead to ambigous result. |
| Clauses affected: | 5.2.3.2.5 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |
| This CR's revision history: |  |

**** FIRST CHANGE ****

##### 5.2.3.2.5	PLMN-SEARCH

The UE shall perform PLMN selection or SNPN selection. If a new PLMN is selected, the UE shall reset the registration attempt counter and initiate a registration procedure for mobility and periodic registration update (see subclause 5.5.1.3). If a new SNPN is selected, the UE shall reset the registration attempt counter, may perform de-registration locally and shall initiate a registration procedure for initial registration (see subclause 5.5.1.2.2).

If the selected cell in the new PLMN is known not to be able to provide normal service, the UE may perform de-registration locally and initiate an initial registration for emergency services.

**** END OF CHANGES ****