3GPP TSG-CT WG1 Meeting #126-e	C1-206164

Electronic meeting, 15-23 October 2020

| CR-Form-v12.0 |
| --- |
| CHANGE REQUEST |
|  | 23.040 | CR | 0156 | rev | 3 | Current version: | 16.0.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME |  | Radio Access Network |  | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Message Waiting Data for SMSF |
| --- | --- |
| Source to WG: | Nokia, Nokia Shanghai Bell |
| Source to TSG: | C1 |
| Work item code: | TEI17 |  | Date: | 2020-10-06 |
| Category: | F |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) Rel-17 (Release 17) |
| Reason for change: | When support for SMS in 5GS was defined in Rel-15, the approach taken was to limit the amount of documentation and only provide a mapping table in Annex K of the spec. As a consequence, requirments for UDM are the same as for HLR/HSS when it comes to serving a 5G subscriber. This include the flags in the Message Waiting Data. However, CT4 has explicitly specified the support for 5G specific MWD flags for MAP and DIAMETER interfaces used for SMS support. It is therefore proposed to align with stage-3 specs and explicitly describe 5G specific data in MWD, see e.g.29.338 for the DIAMETER enhancements. It is to note that CT4 brought the changes back in Rel-15. However, the CR against 23.040 is seen as an alignment/clarificaiton and not FASMO. So it is only proposed for Rel-17. |
| Summary of change: | Introduce UNRF-SMSF and UNRR-SMSF as part of the MWD for HLR/HSS/UDM and AMF. |
| Consequences if not approved: | Misalignment between stage 2 and stage 3 specifications |
| Clauses affected: | K.1 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |
| This CR's revision history: | Revision 3: Some corrections in the terminologies |

*****************first change********************

# K.1	General

A 5GS network delivers short message services over 5GS NAS signalling.

For the architecture and the definition of reference points for SMS in 5GS see 3GPP TS 23.501 [51], subclause 4.2.

Between the architecture and the reference points for SMS in 5GS and the architecture and the reference points shown in subclause 4.1, and figure 5, of the present specification the following mapping is used:

Table K.1: Mapping between architecture, reference points, and flags for SMS in 5GS and the present specification

|  | SMS in 5GS | present specification |
| --- | --- | --- |
|  | UDM | HLR |
| Network entities | SMSF | MSC + VLR |
|  | UE | MS |
|  | AMF | MME (NOTE 1) |
|  | N20/Namf/Nsmsf | (not shown in figure 5) |
|  | N21/Nsmsf | (not shown in figure 5) |
|  | N8/Nudm | (not shown in figure 5) |
|  | Not shown in 3GPP TS 23.501 (NOTE 3) | 2 |
| Reference points | Not shown in 3GPP TS 23.501 (NOTE 2) | 3 |
|  | (not applicable) | 4 |
|  | N1 | 5 |
|  | (not applicable) | 6 |
| Flags | UE Not Reachable Flag-for-SMSF (UNRF-SMSF) | Mobile Station Not Reachable Flag (MNRF) |
|  | UE Not Reachable-via-the-SMSF-Reason (UNRR-SMSF) | Mobile Station Not Reachable-Reason (MNRR) |
| NOTE 1: In figure 5, the MME is only acting as a relay for SMS transfer via the SGs. NOTE 2: Reference point 3 is used as reference from SMSF to/from SMS-GMSC/IWMSC and SMS Router. NOTE 3: Reference point 2 is used as reference from UDM to/from SMS-GMSC and SMS Router. |

For the purpose of supporting SMS in 5GS, the SMSF shall implement the requirements specified in the present specification for the MSC and the VLR with the following modifications:

1)	"GSM/UMTS system" is to be replaced with "5GS".

2)	Throughout the text and in the figures, message names, parameter names and cause values:

"MSC" is to be replaced with "SMSF";

"VLR" is to be replaced with "SMSF internal subscriber register";

"HLR" is to be replaced with "UDM/HLR";

"MS" is to be replaced with "UE"; and

"non GPRS" is to be replaced with "5GS".

3)	The protocol used on reference point 2 is based on MAP as specified in 3GPP TS 29.002 [15]. In addition, it optionally may be based on Diameter as specified for reference point S6c (see 3GPP TS 29.338 [50]).

4)	The protocol used on reference point 3 is based on MAP as specified in 3GPP TS 29.002 [15]. In addition, it optionally may be based on Diameter as specified for reference point SGd (see 3GPP TS 29.338 [50]).

5)	Reference point 4 is SMSF internal, and operations performed on this reference point are not standardized. In the message flows of clause 10, the SMSF replaces the combination of MSC and VLR, and messages exchanged between MSC and VLR are replaced with SMSF internal communication.

The architecture for SMS in 5GS is defined in 3GPP TS 23.501 [51] and uses the following reference points:

N1:	Reference point between the UE and the AMF.

N8:	Reference point between the UDM and the AMF.

N20:	Reference point between the AMF and the SMSF.

N21:	Reference point between SMSF and the UDM.

The following service-based interfaces are used for SMS in 5GS:

Namf:	Service-based interface exhibited by AMF. Usage of Namf service operations for SMS in 5GS is defined in 3GPP TS 23.502 [52].

Nsmsf:	Service-based interface exhibited by SMSF. Usage of Nsmsf service operations for SMS in 5GS is defined in 3GPP TS 23.502 [52].].

Nudm:	Service-based interface exhibited by UDM. Usage of Nudm service operations for SMS in 5GS is defined in 3GPP TS 23.502 [52].

The following flags are used for SMS in 5GS:

Mobile Station Not Reachable Flag-for-SMSF (MNRF-SMSF):
Part of the MWI to be stored in the UDM and AMF when SMS in SMSF is used

NOTE:	MNRF-SMSF is a Boolean parameter indicating if the address list of MWD contains one or more entries because an attempt to deliver a short message to an MS has failed with a cause of Absent Subscriber.

Mobile Station Not Reachable-via-the-SMSF-Reason (MNRR-SMSF):
Part of the MWI in the UDM which stores the reason for an MS being absent when an attempt to deliver a short message to an MS fails at the SMSF with a cause of Absent Subscriber

*****************end of changes********************