3GPP TSG-CT WG1 Meeting #126-e	C1-20abcd

Electronic meeting, 15-23 October 2020

| CR-Form-v12.0 |
| --- |
| CHANGE REQUEST |
|  | 24.501 | CR | 2764 | rev | 1 | Current version: | 17.0.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | x | Radio Access Network |  | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | IE length style in message definition |
| --- | --- |
| Source to WG: | Ericsson, Huawei |
| Source to TSG: | C1 |
| Work item code: | 5GProtoc17 |  | Date: | 2020-10-07 |
| Category: | D |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) Rel-17 (Release 17) |
| Reason for change: | At variable length IEs in NAS messages, the style of the NAS protocol specification (24.008, 24.301 and 24.501) is to capture the minimum length and maximum length. Details on possible lengths can be found in the IE definition. For PDU address IE in PDU SESSION ESTABLISHMENT ACCEPT message the length has however been captured as a list of possible values. This style is not used in any other cases even if there are several IEs whith same type of lengh restriction properties. It is proposed to align length of PDU address IE in PDU SESSION ESTABLISHMENT ACCEPT message to other NAS specifications which used style of a min-max range. Note that the full details are still specified in the IE definition. Also, there is no other IE in the specification with variable length which is described by using all possible lengths in message definitions. |
| Summary of change: | Length of PDU address IE in PDU SESSION ESTABLISHMENT ACCEPT message is indicated using the minimum and maximum range as other NAS specifications. |
| Consequences if not approved: | Style misalignment in NAS specifications which makes message definition more cluttered and maintenance effort to keep the IE definition and message definition aligned in unnecessary detail. |
| Clauses affected: | 8.3.2.1 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |
| This CR's revision history: |  |

*** First change ***

#### 8.3.2.1	Message definition

The PDU SESSION ESTABLISHMENT ACCEPT message is sent by the SMF to the UE in response to PDU SESSION ESTABLISHMENT REQUEST message and indicates successful establishment of a PDU session. See table 8.3.2.1.1.

Message type:	PDU SESSION ESTABLISHMENT ACCEPT

Significance:	dual

Direction:		network to UE

Table 8.3.2.1.1: PDU SESSION ESTABLISHMENT ACCEPT message content

| IEI | Information Element | Type/Reference | Presence | Format | Length |
| --- | --- | --- | --- | --- | --- |
|  | Extended protocol discriminator | Extended protocol discriminator 9.2 | M | V | 1 |
|  | PDU session ID | PDU session identity 9.4 | M | V | 1 |
|  | PTI | Procedure transaction identity 9.6 | M | V | 1 |
|  | PDU SESSION ESTABLISHMENT ACCEPT message identity | Message type 9.7 | M | V | 1 |
|  | Selected PDU session type | PDU session type 9.11.4.11 | M | V | 1/2 |
|  | Selected SSC mode | SSC mode 9.11.4.16 | M | V | 1/2 |
|  | Authorized QoS rules | QoS rules 9.11.4.13 | M | LV-E | 6-65538 |
|  | Session AMBR | Session-AMBR 9.11.4.14 | M | LV | 7 |
| 59 | 5GSM cause | 5GSM cause 9.11.4.2 | O | TV | 2 |
| 29 | PDU address | PDU address 9.11.4.10 | O | TLV | 7-31 |
| 56 | RQ timer value | GPRS timer 9.11.2.3 | O | TV | 2 |
| 22 | S-NSSAI | S-NSSAI 9.11.2.8 | O | TLV | 3-10 |
| 8- | Always-on PDU session indication | Always-on PDU session indication 9.11.4.3 | O | TV | 1 |
| 75 | Mapped EPS bearer contexts | Mapped EPS bearer contexts 9.11.4.8 | O | TLV-E | 7-65538 |
| 78 | EAP message | EAP message 9.11.2.2 | O | TLV-E | 7-1503 |
| 79 | Authorized QoS flow descriptions | QoS flow descriptions 9.11.4.12 | O | TLV-E | 6-65538 |
| 7B | Extended protocol configuration options | Extended protocol configuration options 9.11.4.6 | O | TLV-E | 4-65538 |
| 25 | DNN | DNN 9.11.2.1B | O | TLV | 3-102 |
| 17 | 5GSM network feature support | 5GSM network feature support 9.11.4.18 | O | TLV | 3-15 |
| 18 | Serving PLMN rate control | Serving PLMN rate control 9.11.4.20 | O | TLV | 4 |
| 77 | ATSSS container | ATSSS container 9.11.4.22 | O | TLV-E | 3-65538 |
| C- | Control plane only indication | Control plane only indication 9.11.4.23 | O | TV | 1 |
| 66 | IP header compression configuration | IP header compression configuration 9.11.4.24 | O | TLV | 5-257 |
| 1F | Ethernet header compression configuration | Ethernet header compression configuration 9.11.4.28 | O | TLV | 3 |

*** End of changes ***