3GPP TSG-CT WG1 Meeting #128-e	C1-211122

# Electronic meeting; 25 February – 5 March 2021

Source:	Samsung, AT&T, Qualcomm Incorporated, Intel, Ericsson

Title:	EEC Registration API

Spec:	3GPP TS 24.558 v0.0.0

Agenda item:	17.2.10

Document for:	Agreement

1. Introduction

This pCR provides details for Eees_EECRegistration API.

2. Reason for Change

The Eees_EECRegistration API is defined in clause 6.4.2.4 of 3GPP TS 23.558. It is required to implement the API in stage#3 specification.

3. Proposal

It is proposed to agree the following changes to 3GPP TS 24.558 v0.0.0.

* * * First Change * * * *

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[r29500]	3GPP TS 29.500: "5G System; Technical Realization of Service Based Architecture; Stage 3".

[r29571]	3GPP TS 29.571: "5G System; Common Data Types for Service Based Interfaces; Stage 3".

[r29572]	3GPP TS 29.572: "5G System; Location Management Services; Stage 3".

* * * Next Change * * * *

## 6.x	Eees_EECRegistration API

### 6.x.1	API URI

The request URI used in each HTTP request from the EEC towards the EES shall have the structure as defined in clause 6.1.5 with the following clarifications:

-	The <apiName> shall be "ees-eecregistration".

-	The <apiVersion> shall be "v1".

-	The <apiSpecificResourceUriPart> shall be set as described in clause 6.x.2.

### 6.x.2	Resources

#### 6.x.2.1	Overview

Figure 6.x.2.1-1: Resource URI structure of the Eees_EECRegistration API

Editor’s note: Inclusion of {ueId} in the URL path before the {eecId} is TBD and requires further direction from SA3. In the absence of {ueId} in the URL path, the need for having {eecId} in the path is questionable

Table 6.x.2.1-1 provides an overview of the resources and applicable HTTP methods.

Table 6.x.2.1-1: Resources and methods overview

| Resource name | Resource URI | HTTP method or custom operation | Description |
| --- | --- | --- | --- |
| EEC Registrations | {apiRoot}/ees-eecregistration /v1/{eecid}/registrations | POST | Create a new registration |
| Individual EEC registration | {apiRoot}/ees-eecregistration /v1/{eecid}/registrations/{registrationId} | PUT | Modify an existing registration |
|  |  | DELETE | Delete an existing registration |

#### 6.x.2.2	Resource: EEC Registrations

##### 6.x.2.2.1	Description

This resource represents a collection of EEC registrations with an EES.

##### 6.x.2.2.2	Resource Definition

Resource URI: {apiRoot}/ees-eecregistration/v1/{eecid}/registrations

This resource shall support the resource URI variables defined in table 6.x.2.2.2-1.

Table 6.x.2.2.2-1: Resource URI variables for this resource

| Name | Definition |
| --- | --- |
| apiRoot | See clause 6.1.5 |

##### 6.x.2.2.3	Resource Standard Methods

###### 6.x.2.2.3.1	POST

This method creates a new registration. This method shall support the URI query parameters specified in table 6.x.2.2.3.1-1.

Table 6.x.2.2.3.1-1: URI query parameters supported by the POST method on this resource

| Name | Data type | P | Cardinality | Description |
| --- | --- | --- | --- | --- |
| n/a |  |  |  |  |

This method shall support the request data structures specified in table 6.x.2.2.3.1-2 and the response data structures and response codes specified in table 6.x.2.2.3.1-3.

Table 6.3.2.2.3.1-2: Data structures supported by the POST Request Body on this resource

| Data type | P | Cardinality | Description |
| --- | --- | --- | --- |
| EecRegistration | M | 1 | Create a Individual EEC registration resource. |

Table 6.3.2.2.3.1-3: Data structures supported by the POST Response Body on this resource

| Data type | P | Cardinality | Response codes | Description |
| --- | --- | --- | --- | --- |
| EecRegistration | M | 1 | 201 Created | Individual EEC registration resource created successfully. The URI of the created resource shall be returned in the "Location" HTTP header |
| NOTE: The manadatory HTTP error status code for the <method 1> method listed in Table 5.2.7.1-1 of 3GPP TS 29.500 [r29500] also apply. |

Table 6.x.2.2.3.1-4: Headers supported by the POST method on this resource

| Name | Data type | P | Cardinality | Description |
| --- | --- | --- | --- | --- |
| n/a |  |  |  |  |

Table 6.x.2.2.3.1-5: Headers supported by the 201 response code on this resource

| Name | Data type | P | Cardinality | Description |
| --- | --- | --- | --- | --- |
| Location | string | M | 1 | Contains the URI of the newly created resource, according to the structure: {apiRoot}/ees-eecregistration/v1/{eecid}/registrations/{registrationId} |

##### 6.x.2.2.4		Resource Custom Operations

None.

#### 6.x.2.3	Resource: Individual EEC registration

##### 6.x.2.3.1	Description

This resource represents an individual registration of an EEC.

##### 6.x.2.3.2	Resource Definition

Resource URI: {apiRoot}/ees-eecregistration/v1/{eecid}/registrations/{registrationId}

This resource shall support the resource URI variables defined in table 6.x.2.3.2-1.

Table 6.x.2.3.2-1: Resource URI variables for this resource

| Name | Definition |
| --- | --- |
| apiRoot | See clause 6.1.5 |
| registrationId | Identifier of a specific EEC registration. |

##### 6.x.2.3.3	Resource Standard Methods

###### 6.x.2.3.3.1	PUT

This method updates the EEC registration data by completely replacing the existing registration data (except registrationId). This method shall support the URI query parameters specified in table 6.x.2.3.3.1-1.

Table 6.x.2.3.3.1-1: URI query parameters supported by the PUT method on this resource

| Name | Data type | P | Cardinality | Description |
| --- | --- | --- | --- | --- |
| n/a |  |  |  |  |

This method shall support the request data structures specified in table 6.x.2.3.3.1-2 and the response data structures and response codes specified in table 6.x.2.3.3.1-3.

Table 6.x.2.3.3.1-2: Data structures supported by the PUT Request Body on this resource

| Data type | P | Cardinality | Description |
| --- | --- | --- | --- |
| EecRegistration | M | 1 | An Individual registration resource to be updated. |

Table 6.x.2.3.3.1-3: Data structures supported by the PUT Response Body on this resource

| Data type | P | Cardinality | Response codes | Description |
| --- | --- | --- | --- | --- |
| EecRegistration | M | 1 | 200 OK | An individual EEC registration resource updated successfully. |
| NOTE: The manadatory HTTP error status code for the PUT method listed in Table 5.2.7.1-1 of 3GPP TS 29.500 [r29500] also apply. |

###### 6.x.2.3.3.2	DELETE

This method deregisters (removes) an existing EEC registration. This method shall support the URI query parameters specified in table 6.x.2.3.3.2-1.

Table 6.x.2.3.3.2-1: URI query parameters supported by the DELETE method on this resource

| Name | Data type | P | Cardinality | Description |
| --- | --- | --- | --- | --- |
| n/a |  |  |  |  |

This method shall support the request data structures specified in table 6.x.2.3.3.2-2 and the response data structures and response codes specified in table 6.x.2.3.3.2-3.

Table 6.x.2.3.3.1-2: Data structures supported by the DELETE Request Body on this resource

| Data type | P | Cardinality | Description |
| --- | --- | --- | --- |
| n/a |  |  |  |

Table 6.x.2.3.3.1-3: Data structures supported by the DELETE Response Body on this resource

| Data type | P | Cardinality | Response codes | Description |
| --- | --- | --- | --- | --- |
| n/a |  |  | 204 No Content | An individual EEC registration resource deleted successfully. |
| NOTE: The manadatory HTTP error status code for the DELETE method listed in Table 5.2.7.1-1 of 3GPP TS 29.500 [r29500] also apply. |

##### 6.x.2.3.4		Resource Custom Operations

None.

### 6.x.3	Custom Operations without associated resources

None.

### 6.x.4	Notifications

None.

### 6.x.5	Data Model

#### 6.x.5.1	General

This clause specifies the application data model supported by the Eees_EECRegistration API.

Table 6.x.5.1-1 specifies the data types defined specifically for the Eees_EECRegistration API service.

Table 6.x.5.1-1: Eees_EECRegistration API specific Data Types

| Data type | Section defined | Description | Applicability |
| --- | --- | --- | --- |
| EecRegistration | 6.x.5.2.2 | Describes the parameters to perform EEC Registration related operations (Create, Modify, Delete) |  |
| ACProfile | 6.x.5.2.3 | Describes information about AC used to determine services and service characteristics required |  |
| EasDetail | 6.x.5.2.4 | Describes EAS along with service KPIs that serves the AC |  |
| ACServiceKPIs | 6.x.5.2.5 | Describes the KPIs required by the AC in order to receive required services |  |

Table 6.x.45.1-2 specifies data types re-used by the Eees_EECRegistration API service.

Table 6.x.5.1-2: Re-used Data Types

| Data type | Reference | Comments | Applicability |
| --- | --- | --- | --- |
| DateTime | 3GPP TS 29.571 [r29571] |  |  |
| ScheduledCommunicationTime | 3GPP TS 29.571 [r29571] |  |  |
| GeographicArea | 3GPP TS 29.572 [r29572] |  |  |
| Uinteger | 3GPP TS 29.571 [r29571] |  |  |
| DurationSec | 3GPP TS 29.571 [r29571] |  |  |

#### 6.x.5.2	Structured data types

##### 6.x.5.2.1	Introduction

##### 6.x.5.2.2	Type: EecRegistration

Table 6.x.5.2.2-1: Definition of type EecRegistration

| Attribute name | Data type | P | Cardinality | Description | Applicability |
| --- | --- | --- | --- | --- | --- |
| eecId | string | M | 0..1 | Represents a unique identifier of the EEC. |  |
| ueId | string | O | 0..1 | Represents the identifier of the UE. |  |
| acProfs | array(ACProfile) | O | 1..N | Profiles of ACs for which the EEC provides edge enabling services. |  |
| expTime | DateTime | O | 0..1 | Represents an expiration time for the registration. This attribute shall be present in the response of the HTTP POST message from EEC to create a new registration or in the response of the HTTP PUT message from EEC to update a specific registration. |  |
| eecCntxId | string | O | 0..1 | Identifier of the EEC context obtained from a previous registration. |  |
| srcEesId | string | O | 0..1 | Identifier of the EES that provided EEC context ID. |  |
| srcEesEndpoint | string | O | 0..1 | The endpoint address (e.g. URI, IP address) of the EES that provided EEC context ID. |  |

Editor’s Note: The security credentials of EEC depends on SA3 WG and is FFS.

##### 6.x.5.2.3	Type: ACProfile

Table 6.x.5.2.2-1: Definition of type ACProfile

| Attribute name | Data type | P | Cardinality | Description | Applicability |
| --- | --- | --- | --- | --- | --- |
| acId | string | M | 1 | Identity of the AC. |  |
| acType | string | O | 0..1 | The category or type of AC. |  |
| preferredEcsps | array(string) | O | 1..N | Indicates to the ECS which ECSPs are preferred for the AC. The ECS may use this information in the selection of EESs. |  |
| acSchedule | ScheduledCommunicationTime | O | 0..1 | Indicates the expected operation schedule of the AC (e.g. time windows) |  |
| expectedAcGeoServiceArea | GeographicArea | O | 0..1 | Indicates the expected location(s) (e.g. route) of the hosting UE during the AC's operation schedule. |  |
| serviceContinuitySupport | boolean | O | 0..1 | Indicates if service continuity support is required or not for the application. |  |
| eass | Array(EasDetail) | O | 1..N | Provides the list of EAS that serve the AC along with the service KPIs required by the AC |  |

##### 6.x.5.2.4	Type: EasDetail

Table 6.x.5.2.2-1: Definition of type EasDetail

| Attribute name | Data type | P | Cardinality | Description | Applicability |
| --- | --- | --- | --- | --- | --- |
| easId | string | M | 1 | Identifier of the EAS |  |
| expectedServiceKPIs | ACServiceKPIs | O | 0..1 | Describes the KPIs expected in order for ACs to receive currently required services from the EAS |  |
| minimumRequiredServiceKPIs | ACServiceKPIs | O | 0..1 | Describes the minimum KPIs required in order for ACs to receive meaningful services from the EAS |  |

##### 6.x.5.2.5	Type: ACServiceKPIs

Table 6.x.5.2.2-1: Definition of type ACServiceKPIs

| Attribute name | Data type | P | Cardinality | Description | Applicability |
| --- | --- | --- | --- | --- | --- |
| connectionBW | Uinteger | O | 0..1 | The required connection bandwidth in Kbit/s for the application. |  |
| ReqRate | Uinteger | O | 0..1 | The request rate to be generated by the AC. |  |
| ResponseTime | DurationSec | O | 0..1 | Response time (NOTE) required for the server servicing the requests. |  |
| availability | Uinteger | O | 0..1 | Percentage of time the server is required to be available for the AC's use. |  |
| compute | string | O | 0..1 | The compute resources required by the AC. |  |
| graphicalCompute | string | O | 0..1 | The graphical compute resources required by the AC. |  |
| memory | string | O | 0..1 | The memory resources required by the AC. |  |
| storage | string | O | 0..1 | The storage resources required by the AC. |  |
| acTypeSpecificInfo | string | O | 0..1 | Information specific to each AC type e.g. video, VR, etc. |  |

### 6.x.6	Error Handling

Editor’s Note: The error handling for Eees_EECRegistration API is FFS.

### 6.x.7	Feature negotiation

Editor’s Note: The Feature negotiation for Eees_EECRegistration API is FFS.

* * * End of Change * * * *

# Comments

Changes over changes will be removed before submission to portal