3GPP TSG-CT WG1 Meeting #128-e	C1-211050

# Electronic meeting; 25 February – 5 March 2021

Source:	AT&T, Samsung, Deutsche Telekom, Qualcomm, Intel, Ericsson

Title:	Adding Subscription Resources to Eecs_ServiceProvisioning API

Spec:	3GPP TS 24.558 v0.0.0

Agenda item:	17.2.10

Document for:	Agreement

1. Introduction

This pCR provides details of the notification subscription resources for Eecs_ServiceProvisioning API.

2. Reason for Change

The Eecs_ServiceProvisioning API and the ability for EEC to subscribe to changes in ECS provisioing data is defined in clause 8.3.3.4 of 3GPP TS 23.558. It is reqired to further specify the API as part of the stage#3 specification.

3. Proposal

It is proposed to agree to the following changes to 3GPP TS 24.558 v0.0.0.

* * * First Change * * * *

### B.1.3.2	Resources

##### B.1.3.2.1	Overview

Figure B.1.3.2.1-1: Resource URI structure of the Eecs_ServiceProvisioning API

Editor’s Note: Inclusion of {ueId} in the URL path before the {eecId} is TBD and requires further direction from SA3. In the absence of {ueId} in the URL path, the need for having {eecId} in the path is questionable.

Table B.1.3.2.1-1 provides an overview of the resources and applicable HTTP methods.

Table B.1.3.2.1-1: Resources and methods overview

| Resource name | Resource URI | HTTP method or custom operation | Description |
| --- | --- | --- | --- |
| subscriptions (Collection) | /{eecId}/subscriptions | POST | Creates a new subscription in ECS in order to be notified of provisioning data changes of interest. |
| subscription (Document) | /{eecId /subscriptions/{subscriptionId} | PUT | Updates an existing subscription in ECS. |
|  |  | DELETE | Deletes an existing subscription from ECS. |

##### B.1.3.2.2 	Resource: subscriptions

###### B.1.3.2.2.1	Description

This resource represents a collection of subscriptions of EECs interested in receiving provisioning data related notifications from ECS. The resource is modelled as a collectin archetype (see Annex C.2 of 3GPP TS 29.501 [r29501]).

###### B.1.3.2.2.2	Resource Definition

Resource URI: {apiRoot}/ecs_serviceprovisioning/v1/{eecId}/subscriptions

This resource shall support the resource URI variables defined in table B.1.3.2.2.2-1.

Table B.1.3.2.2.2-1: Resource URI variables for this resource

| Name | Definition |
| --- | --- |
| apiRoot | See clause 7.5 |
| eecId | EEC Identifier which uniquely identifies an EEC |

###### B.1.3.2.2.3	Resource Standard Methods

Editor’s Note: The resource standard methods for Eecs_ServiceProvisioning API is FFS.

#### B.1.3.3	Custom Operations without associated resources

None.

#### B.1.3.4	Notifications

Editor’s Note: The notifications for Eecs_ServiceProvisioning API is FFS.

#### B.1.3.5	Data Model

Editor’s Note: The data model for Eecs_ServiceProvisioning API is FFS.

#### B.1.3.6	Error Handling

General error responses are defined in clause 7.xx.

#### B.1.3.7	Feature negotiation

Editor’s Note: The Feature negotiation for Eecs_ServiceProvisioning API is FFS.

* * * End of Change * * * *