3GPP TSG-CT WG1 Meeting #128-e	C1-21xxxx

# Electronic meeting; 25 February – 5 March 2021

Source:	Nokia, Nokia Shanghai Bell

Title:	New solution to Scenario 3 of KI #1

Spec:	3GPP TR 23.700-10 V0.3.0

Agenda item:	17.3.3

Document for:	Agreement

1. Introduction

A new solution to Scenario 3 of KI #1 is proposed.

2. Reason for Change

In order to resolve the issue, a solution needs to be provided.

3. Conclusions

<Conclusion part (optional)>

4. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-10.

* * * First Change * * * *

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	3GPP TS 23.502: "Procedures for the 5G System".

[x]	3GPP TS 23.501: "System architecture for the 5G System (5GS); Stage 2".

* * * Next Change * * * *

### 6.2.2	Impacts on existing nodes and functions

Editor's note:	This clause describes impacts to existing entities and interfaces.

### The UE provides information related to home IMS network to the SMF during 5GC PDU session establishment procedure.

### 6.2.3	Solution Evaluation

Editor's note:	This clause provides an evaluation of the solution.

* * * Next Change * * * *

## 6.x	Solution #X: P-CSCF discovery using information available in 5GC slice

### 6.x.1	Description

This solution addresses the scenario depicted in figure 5.1-5 to support P-CSCF discovery when a 5GC slice is connected to multiple IMS networks.

In the scenario, even if a 5GC slice is connected to multiple IMS networks, there exists a single IMS network for a single UE. Therefore, when P-CSCF needs to be discovered by a 5GC slice for a single UE, there is no confusion in the 5GC slice if an SMF in the 5GC slice uses the P-CSCF selection functionality as described in clause 5.16.3.11 of 3GPP TS 23.501 [x].

NOTE:	It is noteworthy that currently the UE IP address is taken into account during the P-CSCF discovery. See clause 5.16.3.11 of 3GPP TS 23.501 [x] for further details.

### 6.x.2	Impacts on existing nodes and functions

None.

### 6.x.3	Solution Evaluation

This solution does not impact any protocol. Therefore, compared to Solution 2 described in clause 6.2 which requires information related to the home IMS network provided by the UE to the SMF, this solution is better from the perspective that both solutions achieve the same target.