3GPP TSG-CT WG1 Meeting #128-e	C1-21xxxx

# Electronic meeting; 25 February – 5 March 2021

Source:	Nokia, Nokia Shanghai Bell

Title:	Clarification in the number of PLMNs sharing an NG-RAN node

Spec:	3GPP TR 24.811 V0.2.0

Agenda item:	17.2.9

Document for:	Agreement

1. Introduction

A restriction in Solution #10 is described.

2. Reason for Change

The exact number should be provided for accurate evaluation.

3. Conclusions

<Conclusion part (optional)>

4. Proposal

It is proposed to agree the following changes to 3GPP TR 24.811 V0.2.0.

* * * First Change * * * *

### 6.10.2	Impacts on existing nodes and functionality

NG-RAN

Because the NG-RAN node is shared to a PLMN to which a disaster condition applies, there is a restriction in the number of networks that can share the NG-RAN node.

NOTE:	The maximum number of networks (i.e. PLMNs and NPNs) broadcast by a cell is 12 and 6 for an NR cell and an E-UTRA cell, respectively. For example, if an NG-RAN node is shared to three other PLMNs for handling of disaster condition according to Solution #9, the NG-RAN node can be shared to eight other networks.