3GPP TSG-CT WG1 Meeting #129-e	C1-212153

# Electronic meeting; 19-23 April 2021							  was C1-211426 was C1-211122

Source:	Samsung, AT&T, Qualcomm Incorporated, Intel, Apple, Verizon, KDDI, Convida Wireless LLC, Charter Communications

Title:	EEC Registration API

Spec:	3GPP TS 24.558 v0.1.0

Agenda item:	17.2.16

Document for:	Agreement

1. Introduction

This pCR provides details for Eees_EECRegistration API.

2. Reason for Change

The Eees_EECRegistration API is defined in clause 6.4.2.4 of 3GPP TS 23.558. It is required to implement the API in stage#3 specification.

3. Proposal

It is proposed to agree the following changes to 3GPP TS 24.558 v0.1.0.

* * * First Change * * * *

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[r29500]	3GPP TS 29.500: "5G System; Technical Realization of Service Based Architecture; Stage 3".

[r29571]	3GPP TS 29.571: "5G System; Common Data Types for Service Based Interfaces; Stage 3".

[r29572]	3GPP TS 29.572: "5G System; Location Management Services; Stage 3".

[r29558]	3GPP TS 29.558: "Enabling Edge Applications; Application Programming Interface (API) specification; Stage 3".

* * * Next Change * * * *

## 6.x	Eees_EECRegistration API

### 6.x.1	API URI

The Eees_EECRegistration service shall use the Eees_EECRegistration API.

The request URI used in each HTTP request from the EEC towards the EES shall have the Resource URI structure as defined in clause 6.1.5 with the following clarifications:

-	The <apiName> shall be "eees-eecregistration".

-	The <apiVersion> shall be "v1".

-	The <apiSpecificResourceUriPart> shall be set as described in clause 6.x.2.

### 6.x.2	Resources

#### 6.x.2.1	Overview

Figure 6.x.2.1-1: Resource URI structure of the Eees_EECRegistration API

Table 6.x.2.1-1 provides an overview of the resources and applicable HTTP methods.

Table 6.x.2.1-1: Resources and methods overview

| Resource name | Resource URI | HTTP method or custom operation | Description |
| --- | --- | --- | --- |
| EEC Registrations | /registrations | POST | Registers a new EEC at the Edge Enabler Server. |
| Individual EEC registration | /registrations/{registrationId} | GET | Fetch an individual EEC registration resource. |
|  |  | PUT | Update an individual EEC registration resource. |
|  |  | DELETE | Remove an individual EEC registration resource. |

Editor’s Note: It is FFS, to obtain the EEC registration information from the "EEC Registrations" collection resource.

Editor’s Note: Whether PATCH method will be used to partially update the EEC registration information is FFS.

Editor’s Note: Inclusion of the EEC identifier in the resource URI structure is FFS.

#### 6.x.2.2	Resource: EEC Registrations

##### 6.x.2.2.1	Description

This resource represents all the Edge Enabler Clients that are registered at a given Edge Enabler Server.

##### 6.x.2.2.2	Resource Definition

Resource URI: {apiRoot}/eees-eecregistration/<apiVersion>/registrations

This resource shall support the resource URI variables defined in table 6.x.2.2.2-1.

Table 6.x.2.2.2-1: Resource URI variables for this resource

| Name | Data Type | Definition |
| --- | --- | --- |
| apiRoot | string | See clause 6.1.5 |
| apiVersion | string | See clause 6.x.1 |

##### 6.x.2.2.3	Resource Standard Methods

###### 6.x.2.2.3.1	POST

This method creates a new registration. This method shall support the URI query parameters specified in table 6.x.2.2.3.1-1.

Table 6.x.2.2.3.1-1: URI query parameters supported by the POST method on this resource

| Name | Data type | P | Cardinality | Description |
| --- | --- | --- | --- | --- |
| n/a |  |  |  |  |

This method shall support the request data structures specified in table 6.x.2.2.3.1-2 and the response data structures and response codes specified in table 6.x.2.2.3.1-3.

Table 6.x.2.2.3.1-2: Data structures supported by the POST Request Body on this resource

| Data type | P | Cardinality | Description |
| --- | --- | --- | --- |
| EECRegistration | M | 1 | EEC registration request information. |

Table 6.x.2.2.3.1-3: Data structures supported by the POST Response Body on this resource

| Data type | P | Cardinality | Response codes | Description |
| --- | --- | --- | --- | --- |
| EECRegistration | M | 1 | 201 Created | EEC information is registered successfully at EES. EEC information registered with EES is provided in the response body The URI of the created resource shall be returned in the "Location" HTTP header |
| NOTE: The manadatory HTTP error status code for the POST method listed Table 5.2.6-1 of 3GPP TS 29.122 [r29122] also apply. |

Table 6.x.2.2.3.1-4: Headers supported by the POST method on this resource

| Name | Data type | P | Cardinality | Description |
| --- | --- | --- | --- | --- |
| n/a |  |  |  |  |

Table 6.x.2.2.3.1-5: Headers supported by the 201 response code on this resource

| Name | Data type | P | Cardinality | Description |
| --- | --- | --- | --- | --- |
| Location | string | M | 1 | Contains the URI of the newly created resource, according to the structure: {apiRoot}/eees-eecregistration/<apiVersion>/registrations/{registrationId} |

Table 6.x.2.2.3.1-6: Links supported by the 201 Response Code on this endpoint

| Name | Resource name | HTTP method or custom operation | Link parameter(s) | Description |
| --- | --- | --- | --- | --- |
| n/a |  |  |  |  |

##### 6.x.2.2.4		Resource Custom Operations

None.

#### 6.x.2.3	Resource: Individual EEC registration

##### 6.x.2.3.1	Description

This Individual EEC Registration resource represents an individual EEC registered at a given Edge Enabler Server.

##### 6.x.2.3.2	Resource Definition

Resource URI: {apiRoot}/ees-eecregistration/<apiVersion>/registrations/{registrationId}

This resource shall support the resource URI variables defined in table 6.x.2.3.2-1.

Table 6.x.2.3.2-1: Resource URI variables for this resource

| Name | Data Type | Definition |
| --- | --- | --- |
| apiRoot | string | See clause 6.1.5 |
| apiVersion | string | See clause 6.x.1 |
| registrationId | string | The EEC registration identifier. |

##### 6.x.2.3.3	Resource Standard Methods

###### 6.x.2.3.3.1	GET

This method retrieves the EEC information registered at Edge Enabler Server. This method shall support the URI query parameters specified in table 6.x.2.3.3.1-1.

Table 6.x.2.3.3.1-1: URI query parameters supported by the GET method on this resource

| Name | Data type | P | Cardinality | Description |
| --- | --- | --- | --- | --- |
| n/a |  |  |  |  |

This method shall support the request data structures specified in table 6.x.2.3.3.1-2 and the response data structures and response codes specified in table 6.x.2.3.3.1-3.

Table 6.x.2.3.3.1-2: Data structures supported by the GET Request Body on this resource

| Data type | P | Cardinality | Description |
| --- | --- | --- | --- |
| n/a |  |  |  |

Table 6.x.2.3.3.1-3: Data structures supported by the GET Response Body on this resource

| Data type | P | Cardinality | Response codes | Description |
| --- | --- | --- | --- | --- |
| EECResgistration | M | 1 | 200 OK | The EEC registration information at the Edge Enabler Server. |
| NOTE: The manadatory HTTP error status code for the GET method listed in Table 5.2.6-1 of 3GPP TS 29.122 [r29122] also apply. |

Table 6.x.2.3.3.1-4: Headers supported by the GET method on this resource

| Name | Data type | P | Cardinality | Description |
| --- | --- | --- | --- | --- |
| n/a |  |  |  |  |

Table 6.x.2.3.3.1-5: Headers supported by the 200 response code on this resource

| Name | Data type | P | Cardinality | Description |
| --- | --- | --- | --- | --- |
| n/a |  |  |  |  |

Table 6.x.2.3.3.1-6: Links supported by the 200 Response Code on this endpoint

| Name | Resource name | HTTP method or custom operation | Link parameter(s) | Description |
| --- | --- | --- | --- | --- |
| n/a |  |  |  |  |

###### 6.x.2.3.3.2	PUT

This method updates the EEC registration information at Edge Enabler Server by completely replacing the existing registration data. This method shall support the URI query parameters specified in table 6.x.2.3.3.2-1.

Table 6.x.2.3.3.2-1: URI query parameters supported by the PUT method on this resource

| Name | Data type | P | Cardinality | Description |
| --- | --- | --- | --- | --- |
| n/a |  |  |  |  |

This method shall support the request data structures specified in table 6.x.2.3.3.2-2 and the response data structures and response codes specified in table 6.x.2.3.3.2-3.

Table 6.x.2.3.3.2-2: Data structures supported by the PUT Request Body on this resource

| Data type | P | Cardinality | Description |
| --- | --- | --- | --- |
| EECRegistration | M | 1 | Details of the EEC registration information to be updated |

Table 6.x.2.3.3.2-3: Data structures supported by the PUT Response Body on this resource

| Data type | P | Cardinality | Response codes | Description |
| --- | --- | --- | --- | --- |
| EECRegistration | M | 1 | 200 OK | The EEC registration information updated successfully and the updated EEC registration information is returned in the response. |
| NOTE: The manadatory HTTP error status code for the PUT method listed in Table 5.2.6-1 of 3GPP TS 29.122 [r29122] also apply. |

Editor’s Note: It is FFS, if 204 No Content response message is applicable.

Table 6.x.2.3.3.2-4: Headers supported by the PUT method on this resource

| Name | Data type | P | Cardinality | Description |
| --- | --- | --- | --- | --- |
| n/a |  |  |  |  |

Table 6.x.2.3.3.2-5: Headers supported by the 200 response code on this resource

| Name | Data type | P | Cardinality | Description |
| --- | --- | --- | --- | --- |
| n/a |  |  |  |  |

Table 6.x.2.3.3.2-6: Links supported by the 200 Response Code on this endpoint

| Name | Resource name | HTTP method or custom operation | Link parameter(s) | Description |
| --- | --- | --- | --- | --- |
| n/a |  |  |  |  |

###### 6.x.2.3.3.3	DELETE

This method deregisters (removes) an EEC registration from the EES. This method shall support the URI query parameters specified in table 6.x.2.3.3.3-1.

Table 6.x.2.3.3.3-1: URI query parameters supported by the DELETE method on this resource

| Name | Data type | P | Cardinality | Description |
| --- | --- | --- | --- | --- |
| n/a |  |  |  |  |

This method shall support the request data structures specified in table 6.x.2.3.3.3-2 and the response data structures and response codes specified in table 6.x.2.3.3.3-3.

Table 6.x.2.3.3.3-2: Data structures supported by the DELETE Request Body on this resource

| Data type | P | Cardinality | Description |
| --- | --- | --- | --- |
| n/a |  |  |  |

Editor’s Note: Details of how the EEC security credentials are submitted in the HTTP DELETE message is FFS and to be updated based on security aspects defined by SA3.

Table 6.x.2.3.3.3-3: Data structures supported by the DELETE Response Body on this resource

| Data type | P | Cardinality | Response codes | Description |
| --- | --- | --- | --- | --- |
| n/a |  |  | 204 No Content | An individual EEC registration information matching the registrationId is deleted. |
| NOTE: The manadatory HTTP error status code for the DELETE method listed in Table 5.2.6-1 of 3GPP TS 29.122 [r29122] also apply. |

Table 6.x.2.3.3.3-4: Headers supported by the DELETE method on this resource

| Name | Data type | P | Cardinality | Description |
| --- | --- | --- | --- | --- |
| n/a |  |  |  |  |

Table 6.x.2.3.3.3-5: Headers supported by the 204 response code on this resource

| Name | Data type | P | Cardinality | Description |
| --- | --- | --- | --- | --- |
| n/a |  |  |  |  |

Table 6.x.2.3.3.3-6: Links supported by the 204 Response Code on this endpoint

| Name | Resource name | HTTP method or custom operation | Link parameter(s) | Description |
| --- | --- | --- | --- | --- |
| n/a |  |  |  |  |

##### 6.x.2.3.4		Resource Custom Operations

None.

### 6.x.3	Custom Operations without associated resources

None.

### 6.x.4	Notifications

None.

### 6.x.5	Data Model

#### 6.x.5.1	General

This clause specifies the application data model supported by the API. Data types listed in clause 6.1.2 apply to this API.

Table 6.x.5.1-1 specifies the data types defined specifically for the Eees_EECRegistration API service.

Table 6.x.5.1-1: Eees_EECRegistration API specific Data Types

| Data type | Section defined | Description | Applicability |
| --- | --- | --- | --- |
| EECRegistration | 6.x.5.2.2 | The EEC registration information on EES. |  |
| ACProfile | 6.x.5.2.3 | The profile information related to the AC in the EECRegistration data type. |  |
| EASDetail | 6.x.5.2.4 | Describes EAS along with service KPIs that serves the AC |  |
| ACServiceKPIs | 6.x.5.2.5 | Describes the KPIs required by the AC in order to receive required services |  |

Table 6.x.5.1-2 specifies data types re-used by the Eees_EECRegistration API service.

Table 6.x.5.1-2: Re-used Data Types

| Data type | Reference | Comments | Applicability |
| --- | --- | --- | --- |
| BitRate | 3GPP TS 29.571 [r29571] | Used to define connection bandwidth |  |
| DateTime | 3GPP TS 29.571 [r29571] | Used to capture the expiration time of EEC registration. |  |
| ScheduledCommunicationTime | 3GPP TS 29.571 [r29571] | Used to define the schedule of AC. |  |
| EndPoint | 3GPP TS 29.558 [r29558] | Used to define the end point information of the EES. |  |
| LocationArea5G | 3GPP TS 29.122 [r29122] | Used to define Expected AC Geographical Service Area |  |
| Uinteger | 3GPP TS 29.571 [r29571] | Used to define availability |  |
| DurationSec | 3GPP TS 29.571 [r29571] | Used to define response time |  |

#### 6.x.5.2	Structured data types

##### 6.x.5.2.1	Introduction

##### 6.x.5.2.2	Type: EecRegistration

Table 6.x.5.2.2-1: Definition of type EecRegistration

| Attribute name | Data type | P | Cardinality | Description | Applicability |
| --- | --- | --- | --- | --- | --- |
| eecId | string | M | 0..1 | Represents a unique identifier of the EEC. |  |
| ueId | string | O | 0..1 | Represents the identifier of the UE. |  |
| acProfs | array(ACProfile) | O | 1..N | Profiles of ACs for which the EEC provides edge enabling services. |  |
| expTime | DateTime | O | 0..1 | Represents an expiration time for the registration. This attribute shall be present in the response of the HTTP POST message from EEC to create a new registration or in the response of the HTTP PUT message from EEC to update a specific registration. |  |
| eecCntxId | string | O | 0..1 | Identifier of the EEC context obtained from a previous registration. |  |
| srcEesId | string | O | 0..1 | Identifier of the EES that provided EEC context ID. |  |
| srcEesEndpoint | EndPoint | O | 0..1 | The endpoint address (e.g. URI, IP address) of the EES that provided EEC context ID. |  |

Editor’s Note: The security credentials of EEC depends on SA3 WG and is FFS.

##### 6.x.5.2.3	Type: ACProfile

Table 6.x.5.2.2-1: Definition of type ACProfile

| Attribute name | Data type | P | Cardinality | Description | Applicability |
| --- | --- | --- | --- | --- | --- |
| acId | string | M | 1 | Identity of the AC. |  |
| acType | string | O | 0..1 | The category or type of AC. |  |
| prefEcsps | array(string) | O | 1..N | Indicates to the ECS which ECSPs are preferred for the AC. The ECS may use this information in the selection of EESs. |  |
| acSch | ScheduledCommunicationTime | O | 0..1 | Indicates the expected operation schedule of the AC (e.g. time windows) |  |
| expAcGeoSerArea | LocationArea5G | O | 0..1 | Indicates the expected location(s) (e.g. route) of the hosting UE during the AC's operation schedule. |  |
| svcContSupp | boolean | O | 0..1 | Indicates if service continuity support is required or not for the application. |  |
| eass | Array(EasDetail) | O | 1..N | Provides the list of EAS that serve the AC along with the service KPIs required by the AC |  |

##### 6.x.5.2.4	Type: EasDetail

Table 6.x.5.2.2-1: Definition of type EasDetail

| Attribute name | Data type | P | Cardinality | Description | Applicability |
| --- | --- | --- | --- | --- | --- |
| easId | string | M | 1 | Identifier of the EAS |  |
| expSvcKPIs | ACServiceKPIs | O | 0..1 | Describes the KPIs expected in order for ACs to receive currently required services from the EAS |  |
| minReqSvcKPIs | ACServiceKPIs | O | 0..1 | Describes the minimum KPIs required in order for ACs to receive meaningful services from the EAS |  |

##### 6.x.5.2.5	Type: ACServiceKPIs

Table 6.x.5.2.2-1: Definition of type ACServiceKPIs

| Attribute name | Data type | P | Cardinality | Description | Applicability |
| --- | --- | --- | --- | --- | --- |
| connBand | BitRate | O | 0..1 | The required connection bandwidth in Kbit/s for the application. |  |
| reqRate | Uinteger | O | 0..1 | The request rate to be generated by the AC. |  |
| respTime | DurationSec | O | 0..1 | Response time required for the server servicing the requests. This includes the round-trip time of the request and response packet, the processing time at the server and the time required by the server to consume 3GPP Core Network capabilities, if any. |  |
| avail | Uinteger | O | 0..1 | Percentage of time the server is required to be available for the AC's use. |  |
| reqComp | string | O | 0..1 | The compute resources required by the AC. |  |
| reqGraComp | string | O | 0..1 | The graphical compute resources required by the AC. |  |
| reqMem | string | O | 0..1 | The memory resources required by the AC. |  |
| reqStrg | string | O | 0..1 | The storage resources required by the AC. |  |

### 6.x.6	Error Handling

General error responses are defined in clause 6.1.7.

### 6.x.7	Feature negotiation

General feature negotiation procedures are defined in clause 6.1.8. Table 6.x.7-1 lists the supported features for Eees_EECRegistration API.

Table 6.x.7-1: Supported Features

| Feature number | Feature Name | Description |
| --- | --- | --- |

* * * End of Change * * * *