3GPP TSG-CT WG1 Meeting #129-e	C1-212216

Electronic meeting, 19-23 April 2021

Title:	LS on integrity protection between the UE and the HPLMN of additional fields in SOR transparent container carrying SOR acknowledgement

Release:	Rel-17

Work Item:	eCPSOR_CON

Source:	CT1

To:	SA3

Contact person:	Ivo Sedlacek

ivo dot sedlacek at ericsson dot com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

# 1	Overall description

TS 23.122 requires the UE to include the "ME support of SOR-CMCI" indicator in the SOR header of the SOR transparent container carrying the UE acknowledgement. If the "ME support of SOR-CMCI" indicator is included, the UDM can include SOR-CMCI in the SOR information sent to the UE otherwise the UDM shall not include SOR-CMCI in the SOR information sent to the UE.

In TS 33.501, the SOR header of the SOR transparent container carrying the SOR acknowledgement is not integrity protected between the UE and the HPLMN.

If the "ME support of SOR-CMCI" indicator value is changed from "supported" to "not supported" while transported over the VPLMN to the UDM, then the HPLMN will be unable to control when the UE, that is in 5GMM-CONNECTED mode and with specific PDU session(s) or ongoing service(s), leaves the current VPLMN for a higher priority VPLMN. Instead, the UE stays in the current VPLMN for an UE implementation dependent time, which is advantageous for the current VPLMN.

If the "ME support of SOR-CMCI" indicator value is changed from "not supported" to "supported" while transported over the VPLMN to the UDM, and UDM includes SOR-CMCI in the SOR information sent to the UE, the UE decodes the SOR information incorrectly.

CT1 would also like to point out that further fields can be added in the SOR transparent container carrying the UE acknowledgement in future.

# 2	Actions

To SA3

ACTION:	CT1 would like to ask SA3:

- whether the "ME support of SOR-CMCI" indicator in the SOR header of the SOR transparent container carrying the UE acknowledgement, needs to be integrity protection between the UE and the HPLMN;

- if deemed necessary, to specify a backward compatible mechanism enabling integrity protection between the UE and the HPLMN of:

-	the SOR header of the SOR transparent container carrying the SOR acknowledgement; and

-	fields, if any, placed after the SOR-MAC-Iue in the SOR transparent container carrying the SOR acknowledgement.

# 3	Dates of next TSG CT WG1 meetings

TSG CT WG1 Meeting 130-e (electronic)	20 – 28 May 2021

TSG CT WG1 Meeting 130bis-e (electronic)	12 - 16 July 2021