3GPP TSG-CT WG1 Meeting #129-e	C1-212108

Electronic meeting; 19-23 April 2021

Source:	Huawei, HiSilicon

Title:	Evaluation of Solutions for KI#9

Spec:	3GPP TR 24.811

Agenda item:	17.2.9

Document for:	Agreement

1. Introduction

This pCR attempts to provide an evaluation of the solutions for key issue #9

2. Reason for Change

To evaluate the solutions for KI#9

3. Conclusions

4. Proposal

It is proposed to agree the following changes to 3GPP TR 24.811.

* * * First Change * * * *

## 7.9	Evaluation on solutions of Key Issue #9

Solutions #51, #56 and #60 and part of solution #25 aim at solving the key issue #9

Solution #56 and #60 proposes that if during manual PLMN selection, all the available PLMNs are forbidden PLMNs and there are PLMNs that supports disaster roaming, then the UE may indicate to upper layers that the PLMN support disaster roaming.

Solution #25 proposes that if during manual PLMN selection, all the available PLMNs are forbidden PLMNs and if there are PLMNs that supports disaster roaming, then the NAS layer provide information about those PLMNs as not in the list of forbidden PLMNs to the upper layer. In addition to this, Solution #25 also proposes that in manual PLMN selection, the NAS layer may also provide information that the PLMN that is in disaster condition has a disaster condition.

However, in rel-17, the assumption is that the disaster condition is due to the unavailability of RAN. In that case the PLMN that is in disaster condition will not be available for PLMN selection. If that PLMN is available, it can be safely assumed that the disaster condition is over and so no need to send any indication.

Solution #51 proposes that no changes are needed if the RAN is RAN is shared between the PLMN that is in disaster condition and PLMN that supports disaster roaming.

### 8.9	Conclusion on the solutions for Key Issue #9

TBD

* * * End of Change * * * *