3GPP TSG-CT WG1 Meeting #129-e	C1-212097

# Electronic meeting; 19-23 April 2021

Source:	InterDigital

Title:	Configuration parameters for 5G ProSe Direct Discovery

Spec:	3GPP TS 24.554

Agenda item:	17.2.18

Document for:	Agreement

1. Introduction

In this CR the “Configuration parameters for 5G ProSe Direct Discovery” are proposed according to TS 23.304 clause 5.1.2.

2. Reason for Change

SA2 has proposed that TS 24.554 should follow the same procedure as specied in TS 24.587 by adopting the changes proposed in TS 23.304 clause 5.1.2.

3. Proposal

It is proposed to agree the following changes to 3GPP TS 24.554.

* * * First Change * * * *

## 5.2	Configuration and precedence of 5G ProSe configuration parameters

## 5.2.1	Configuration parameters for 5G ProSe Direct Discovery

The configuration parameters for ProSe Direct Discovery over PC5 reference point consist of:

- a validity timer for the validity of the configuration Parameter for ProSe Direct Discovery over PC5 interface;

- a list of PLMNs in which the UE is authorised to perform open ProSe Direct Discovery Model A monitoring when the UE is served by NG-RAN;

- a list of PLMNs in which the UE is authorized to perform open ProSe Direct Discovery Model A announcing when the UE is served by NG-RAN and an Authorised discovery range for announcing per PLMN;

- a list of PLMNs in which the UE is authorised to perform restricted ProSe Direct Discovery Model A monitoring when the UE is served by NG-RAN;

- a list of PLMNs in which the UE is authorized to perform restricted ProSe Direct Discovery Model A announcing when the UE is served by NG-RAN and an Authorised discovery range for announcing per PLMN;

- a list of PLMNs in which the UE is authorized to perform restricted Model B Discoverer operation when the UE is served by NG-RAN and an Authorised discovery range for announcing per PLMN;

- a list of PLMNs in which the UE is authorized to perform restricted Model B Discoveree operation when the UE is served by NG-RAN and an Authorised discovery range for announcing per PLMN;

- an indication of whether the UE is authorized to perform ProSe Direct Discovery for Model A or Model B when "not served by NG-RAN";

- radio parameters for ProSe direct discover per NR PC5 applicable per geographical area(s) with an indication of whether these radio parameters are "operator managed" or "non-operator managed" when "not served by NG-RAN";

NOTE 1:	Whether a frequency band is "operator managed" or "non-operator managed" in a given Geographical Area is defined by local regulations.

- a ProSe Direct Discovery UE ID for Restricted Direct Discovery;

- a list of Group Member Discovery parameters that enable the Group Member Discovery. For each group the list consists of, one or more Application Layer Group ID, Layer-2 Group ID, 	User Info ID and Discovery Group ID;

NOTE 2:	User Info ID is expected to be assigned uniquely to a user within the discovery group.

- a list of Application identifiers to be used for direct discovery over PC5 interface; and

- a list of Security parameters used for direct discovery over PC5.

Editor's note:	Whether the security parameters can be provided by the PCF and details of security parameters will be determined by SA3 WG.

* * * End of Change * * * *