3GPP TSG-CT WG1 Meeting #129-e	C1-21xxxx

# Electronic meeting; 19 – 23 April 2021

Source:	Nokia, Nokia Shanghai Bell

Title:	Update in Solution 16: Entering the no cell available state

Spec:	3GPP TR 24.821 V1.0.0

Agenda item:	17.2.4

Document for:	Agreement

1. Introduction

There exists an EN in Section 6.17.

Editor's note:	The behaviour of a UE unable to obtain normal service when there is no PLMN allowed in the country where the UE is physically located, is FFS.

2. Reason for Change

The EN needs to be resolved.

3. Conclusions

The EN is resolved.

4. Proposal

It is proposed to agree the following changes to 3GPP TR 24.821 V1.0.0.

* * * First Change * * * *

### 6.17.2	Solution description

When a UE is unable to obtain normal service from a PLMN and needs to attempt to camp on an acceptable cell and the UE is capable of determining whether a PLMNs is allowed in the country where the UE is physically located, the UE can camp on an acceptable cell with RAT satellite NG-RAN only if the acceptable cell with RAT satellite NG-RAN belongs to a PLMN allowed in the country where the UE is physically located.

If only PLMN not allowed in the country where the UE is physically located associated with satellite NG-RAN is available and the UE is capable of determining whether a PLMN is allowed in the country where the UE is physically located, the UE shall enter the 5GMM-DEREGISTERED.NO-CELL-AVAILABLE state.

If the UE is not capable of determining whether a PLMN is allowed in the country where the UE is physically located, the UE shall select an acceptable cell to camp on as-is.

NOTE:	How a UE can determine whether a PLMN is allowed in the country where the UE is physically located is covered by Key Issues #1 and #2.

* * * Next Change * * * *

### 6.17.3	Impacts to existing procedures due to the solution

UE

If only PLMN not allowed in the country where the UE is physically located associated with satellite NG-RAN is available and the UE is capable of determining whether a PLMN is allowed in the country where the UE is physically located, a UE enters the 5GMM-DEREGISTERED.NO-CELL-AVAILABLE state.