3GPP TSG-CT WG1 Meeting #130-e	C1-212909

# Electronic meeting; 20th – 28th April

Source:	Qualcomm Incorporated

Title:	Evaluations of solutions for key issue 3

Spec:	3GPP TR 24.821

Agenda item:	17.2.4

Document for:	Agreement

1. Introduction

TR 24.821 contains two solutions for key issue #3: PLMN selection in international areas. No new solutions for this key issue is expected to be added to the TR.

2. Reason for Change

There is a need for evalution of the solutions for key issue #3.

3. Proposal

It is proposed to agree the following changes to 3GPP TR 24.821 v1.1.0.

* * * First Change * * * *

## 7.3	Evaluation of Solutions for Key Issue #3

Table 7.3-1  Evaluation of the solutions to KI#3

| Solution | Summary | Evaluation |
| --- | --- | --- |
| 4 | How the UE selects PLMN if it is determined that the UE is in an international area - The UE determines that it is inside international area as per the solution to key issue #1. - As implementation option, upon a transition in and out of international areas, the UE may trigger a PLMN selection. - UE selects a PLMN using legacy procedure, taking into account optional adiditonal configuration in USIM indicating if a PLMN is allowed to provide service inside international areas. What information could be available to aid the UE in the PLMN selection in international areas: - Optionally, the USIM may carry adidtional configuration indicating if a PLMN is allowed to provide service inside international areas. - Optionally, the USIM may carry additional configuration indicating PLMN prioritization inside international areas, which could be diferent from the prioritization outside international areas. | The HPLMN has the flexibility to assign different PLMN priorities inside international areas vs. outside international areas. The HPLMN has the flexibility to designate some PLMNs as not allowed to provide service inside international areas. The UE impact is the new USIM configuration. This solution is not compatible with Solution 5. |
| 5 | How the UE selects PLMN if it is determined that the UE is in an international area The UE follows the legacy PLMN selection procedure inside international areas. What information could be available to aid the UE in the PLMN selection in international areas None | UE’s presence inside international areas or the transition in/out of intenrtional areas has no impact on legacy PLMN selection. The UE follows the legacy PLMN selection procedure inside international areas. The solution has no UE impact. This solution is not compatible with Solution 4. |

Questions for discussion:

1.	Should it be possible for HPLMN to configure, optionally, which PLMNs can be selected inside international areas?

2.	Should it be possible for HPLMN to configure, optionally, different Operator-controlled PLMN selector with access technology files in USIM for inside international areas vs. outside international areas?

* * * No more changes * * * *