3GPP TSG-CT WG1 Meeting #130-e	C1-213482

# Electronic meeting; 20-28 May 2021							  was C1-21242 was C1-212158

Source:	Samsung

Title:	Eees_EECRegistration_Update Service Operation

Spec:	3GPP TS 24.558 v0.2.0

Agenda item:	17.2.16

Document for:	Agreement

1. Introduction

This pCR specifies Eees_EECRegistration_Update Service Operation.

2. Reason for Change

The Eees_EECRegistration_Update operation is defined in clause 8.4.2.4.3 of 3GPP TS 23.558. It is required to provide service operations details in stage#3.

4. Proposal

It is proposed to agree the following changes to 3GPP TS 24.558 v0.2.0.

* * * First Change * * * *

#### 5.x.2.2	Eees_EECRegistration_Update

##### 5.x.2.2.1	General

This service operation is used by EEC to update its registration information at a given EES.

##### 5.x.2.2.2	EEC updating registration information using Eees_EECRegistration_Update operation

To update the EEC registration information at the EES, the EEC shall send a HTTP PUT message to the EES on resource URI identifying the Individual EEC registration resource representation as specified in clause 6.x.2.3.3.2, requesting to replace all properties in the existing resource with the EEC registration information in the request. The body of the HTTP PUT message may include proposed expiration time to update the registration and AC profile(s). This request shall not modify the eecId property of the existing resource.

Upon receiving the HTTP PUT message from the EEC, if the resource URI does not exist, the EES shall respond 404 Not Found error to the EEC. Otherwise, the EES shall:

a)	check the registration update message from the EEC to see if the EEC is authorized to modify the requested registration resource; and

b)	if the EEC is authorized to update the registration information and the eecId information in the request and the resource match, then the EES shall;

1)	update the resource identified by Resource URI of the EEC registration information with the updated EEC registration information received in the HTTP PUT request message; and

2)	if the AC Profile(s) is included in the HTTP PUT message, the EES further determines whether the registered EAS(s) fulfils the requirements that were indicated in the AC Profile(s) as follows:

i)	For the requirements not included in the List of EASs, the EAS has to be matched to one of the requirements.

ii)	For the requirements included in the List of EASs, the EAS has to be matched to all requirements included in the Minimum required Service KPIs and one of the requirements included in the Expected Service KPIs.

When a matching EAS is identified, the EES determines that the corresponding requirements are fulfilled and are supported for the new resource.

Editor’s note: When the HTTP PUT message includes multiple AC Profile(s), it is FFS how EES determines the requirements in the AC Profile(s) are fulfilled and how EES indicates to the EEC for which AC Profile the requirement is fulfilled.

3)	return the updated EEC registration information in the response. In the response message, the EES may provide an updated expiration time to indicate to the EEC when the updated registration will automatically expire.

If the expiration time is provided, then to maintain the registration, the EEC shall send a registration update request prior to the expiration time. If a registration update request is not received prior to the expiration time, the EES shall treat the EEC as implicitly de-registered and remove the corresponding EEC registration resource.

Editor’s note: Whether eecCntxId can be replaced or not is FFS.

* * * End of Change * * * *