3GPP TSG-CT WG1 Meeting #130-e	C1-213702

# Electronic meeting; 20-28 May 2021									was C1-213480, 2460, 2156

Source:	Samsung, Huawei

Title:	Eees_EECRegistration Service Description and Service Operations Introduction

Spec:	3GPP TS 24.558 v0.2.0

Agenda item:	17.2.16

Document for:	Agreement

1. Introduction

This pCR introduces Eees_EECRegistration Service Description and Service Operations Introduction.

2. Reason for Change

The Eees_EECRegistration API is defined in clause 8.4.2 of 3GPP TS 23.558. It is required to provide service description and service operations introduction as the skeleton.

4. Proposal

It is proposed to agree the following changes to 3GPP TS 24.558 v0.2.0.

* * * First Change * * * *

# 5	Services offered by Edge Enabler Server

## 5.1	Introduction

The table 5.1-1 lists the Edge Enabler Server APIs below the service name. A service description clause for each API gives a general description of the related API.

Table 5.1-1: List of EES Service APIs

| Service Name | Service Operations | Operation Semantics | Consumer(s) |
| --- | --- | --- | --- |
| Eees_EECRegistration | Request | Request/Response | EEC |
|  | Update | Request/Response | EEC |
|  | Deregister | Request/Response | EEC |

Table 5.1-2 summarizes the corresponding Edge Enabler Server APIs defined in this specification.

Table 5.1-2: API Descriptions

| Service Name | Clause | Description | OpenAPI Specification File | apiName | Annex |
| --- | --- | --- | --- | --- | --- |

* * * Next Change * * * *

## 5.x	Eees_EECRegistration Service

### 5.x.1	Service Description

The Eees_EECRegistration API, as defined in 3GPP TS 23.558 [2], allows an EEC via Eees interface to register, update its registration and deregister at a given EES.

Editor’s Note: Details about the security credentials of the EEC, verification and authorization of Eees_EECRegistration Request, Update and Deregister by the EES depend on SA3 WG security requirements and are FFS.

### 5.x.2	Service Operations

#### 5.x.2.1	Introduction

The service operation defined for Eees_EECRegistration API is shown in the table 5.x.2.1-1.

Table 5.x.2.1-1: Operations of the Eees_EECRegistration API

| Service operation name | Description | Initiated by |
| --- | --- | --- |
| Eees_EECRegistration_Request | This service operation is used by the EEC to register itself to a given EES. | EEC |
| Eees_EECRegistration_Update | This service operation is used by the EEC to update its registration information at EES. | EEC |
| Eees_EECRegistration_Deregister | This service operation is used by the EEC to deregister itself from a given EES. | EEC |

* * * End of Change * * * *