3GPP TSG-CT WG1 Meeting #130-e	C1-213705

# Electronic meeting; 20-28 May 2021									was C1-213483, 2463, 2159

Source:	Samsung

Title:	Eees_EECRegistration_Deregister Service Operation

Spec:	3GPP TS 24.558 v0.2.0

Agenda item:	17.2.16

Document for:	Agreement

1. Introduction

This pCR specifies Eees_EECRegistration_Deregister Service Operation.

2. Reason for Change

The Eees_EECRegistration_Deregister operation is defined in clause 8.4.2.4.4 of 3GPP TS 23.558. It is required to provide service operations details in stage#3.

4. Proposal

It is proposed to agree the following changes to 3GPP TS 24.558 v0.2.0.

* * * First Change * * * *

#### 5.x.2.3	Eees_EECRegistration_Deregister

##### 5.x.2.3.1	General

This service operation is used by EEC to deregister itself from a given EES.

##### 5.x.2.3.2	EEC deregistering from EES using Eees_EECRegistration_Deregister operation

To deregister itself from the EES, the EEC shall send HTTP DELETE message to the EES, on the resource URI identifying the Individual EEC registration resource representation as specified in clause 6.x.2.3.3.3. Upon receiving the HTTP DELETE request, the EES shall:

a)	verify the identity of the EEC and check if the EEC is authorized to deregister the EEC registration information;

b)	if the EEC is authorized to deregister the EEC registration information, then the EES shall

1)	if the resource identified by registrationId is not found, return "404 Not Found" error message to the EEC;

2)	otherwise, deregister the EEC profile from the EES and delete the resource representing EEC registration information; and

3)	return the "204 No Content" message to the EEC, indicating the successful deregistration of the EEC information.

* * * End of Change * * * *