3GPP TSG-CT WG1 Meeting #130-e	C1-213296

Electronic meeting; 20-28 May 2021

Source:	Huawei, HiSilicon

Title:	Evaluation of Solutions for KI#9

Spec:	3GPP TR 24.811

Agenda item:	17.2.9

Document for:	Agreement

1. Introduction

This pCR attempts to provide a conclusionbased on the evaluations of the solutions for key issue #9

2. Reason for Change

To conclude the solutions for KI#9

3. Conclusions

4. Proposal

It is proposed to agree the following changes to 3GPP TR 24.811.

* * * First Change * * * *

## 8.9	Conclusions on Key Issue #9

It is concluded that:

-	The solution #51 is not progressed in the normative phase of FS_MINT-CT.

-	The PLMN providing disaster roaming shall not be removed from the list of forbidden PLMNs.

-	for manual network selection if only forbidden PLMNs are available and UE detects that some of those forbidden PLMNs support disaster roaming, then the UE may send an indication to the upper layers that those PLMNs support disaster roaming.

-	in manual network selection mode, reselection to an EPLMN is allowed only if the EPLMN can provide the UE with disaster roaming as determined according to the conclusions of KI#3 as specified in subclause 8.3.

* * * End of Change * * * *