# 3GPP TSG CT WG1 Meeting 130-e	TDoc C1-212894

# Electronic meeting, 20-28 May 2021

Title:	LS on user controlled services during SOR

Response to:	-

Release:	Rel-17

Work Item:	eCPSOR_CON

Source:	3GPP CT1

To:	GSMA 5GJA, GSMA NRG

Cc:	GSMA NG, 3GPP SA1

Contact person:	Ban Al-Bakri

ban.albakri@meadowcom.com

NTT DOCOMO

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	-

# 1	Overall description

In Rel-17, enhancement to SOR was introduced and the requirements were provided in TS 22.261 subclause 6.30, namely for steering of roaming in connected mode.

As described in stage-2 TS 23.122 Annex-C, the steering of roaming connected mode control information (SOR-CMCI) enables the HPLMN to control the timing of a UE in connected mode to move to idle mode for the purpose of performing the steering of roaming, i.e. selecting a higher priority PLMN/access technology.

As part of this enhancement, one requirement allows the user to control some services to not be interrupted due to SOR;

The UE shall be able to delay conforming to steering of roaming control information from the HPLMN while it is engaged in priority service (e.g. emergency call, MPS session), or a service defined by HPLMN policy or the user not to be interrupted (e.g. MMTEL voice/video call).

However, SOR is a business operator requirement rather than a user requirement.

NOTE: In TS23.122 Annex-C, the user preference is reflected as the "user controlled list of services exempted from release due to SOR".

CT1 has the following questions to GSMA:

Q1) is it acceptable to allow users to configure the selection of the services it can prevent from being interrupted due to SOR using the "user controlled list of services exempted from release due to SOR"?

Q2) If the answer to Q1 is YES, then can this happen without the HPLMN knowledge?

If the answer to Q2) is NO, then CT1 has the following questions:

a)- is it required to have a mechanism where the HPLMN shall be able to allow the user to configure such services in the UE, i.e. not to be interrupted due to SOR?

b)- does the HPLMN need to have the knowledge on how the user has configured the "user controlled list of services exempted from release due to SOR", i.e. the service that are not to be interrupted for that UE due to SOR?

Q3) Further, if the answer to Q1 is YES, CT1 would like to understand whether the "user controlled list of services exempted from release due to SOR" can always take precedence over the SOR information provided by HPLMN?

# Actions

To GSAM 5GJA, GSMA NRG

ACTION: 	CT1 asking GSAM 5GJA, GSMA NRG:

To provide guidance on the questions above.

# 3	Dates of next TSG CT WG1 meetings

TSG CT WG1 Meeting 131-e (electronic)	19 – 27 August 2021