# 3GPP TSG CT WG1 Meeting 130-e	TDoc C1-21xxxx

# Electronic meeting, 20-28 May 2021

Title:	LS reply on multiple TACs per PLMN

Response to:	LS R2-2104377/C1-212840 on multiple TACs per PLMN from RAN2

Release:	Rel-17

Work Item:	5GSAT_ARCH-CT, NR_NTN_solutions-Core

Source:	CT1

To:	RAN2, SA2

Cc:	RAN3

Contact person:	Sung Hwan WON

sung.won@nokia.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	-

# 1	Overall description

CT1 would like to thank RAN2 for their question in the LS R2-2104377/C1-212840. Here is the answer from CT1:

Option 2 is feasible and with Option 2 the following impacts to the NAS layer (non-exhaustive) are expected:

- The NAS layer should select a TAI from the multiple TAIs. However, it is not clear to CT1 how the NAS layer selects a TAI from the multiple TAIs.

- The NAS layer should provide the lower layers with the selected TAI.

- The selected TAI should be considered as the current TAI.

CT1 will consider further impacts and make clarification according to feedback from RAN2 and SA2. CT1 needs further analyses to consider how the network knows the selected TAI.

In addition, CT1 would like to ask what should be considered for TAI selection. In the LS R2-2104377/C1-212840, only the registration area is mentioned.

# 2	Actions

To RAN2

ACTION: 	CT1 kindly requests RAN2 to take the above answer into account for the future work and clarify what should be considered for TAI selection.

To SA2

ACTION: 	CT1 respectfully asks SA2 to provide, if any, feedback on the TAI selection in case of multiple TACs broadcast per PLMN.

# 3	Dates of next TSG CT WG1 meetings

TBD