3GPP TSG-CT WG1 Meeting #130-e	C1-21XXX

Electronic meeting, 20-28 May 2021

Title:	LS on loss of network connection for the UE with E-UTRA capability disabled in a network which does not support 2G/3G

Release:	Rel-17

Work Item:

Source:	CT1

To:	SA2

Contact person:	Mingxue Li

limx36@chinatelecom.cn

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

# 1	Overall description

TS 23.501 sepecifies that "In case the UE has signalled that S1 mode is disabled for a network that only supports IMS voice via EPS Fallback, the AMF will not indicate that IMS voice over PS session is supported over 3GPP access."

For a voice-centric UE, if the AMF indicated the IMS voice over PS session not supported over 3GPP access, the UE needs to disable its N1 mode as sepecified in Table 4.3.4.1 of TS 24.501.

Since both the S1 mode and the N1 mode are disabled, the UE has to move to 2G/3G. If the current network does not support 2G/3G, there is no other network available either, the UE will completely loss the network connection.

# 2	Actions

To SA2

ACTION:	CT1 would like to ask SA2 if deemed necessary to specify a mechanism in order to prevent the voice-centric UEs from completely losing network connection when the current network does not support 2G/3G.

# 3	Dates of next TSG CT WG1 meetings

TSG CT WG1 Meeting 131-e (electronic)	19 – 27 Aug 2021

TSG CT WG1 Meeting 132-e (electronic)	11 – 15 Oct 2021